## Slide 1
Proposal to introduce bodied L7 vehicles in R.E.3
First step in three-step approach for Harmonisation of
(passive) safety requirements for
of bodied L7 vehicles
Informal document GRSG-118-18
(15-17 July 2020, agenda item 14)
Notes: <number>

## Slide 2
IMMA Proposal to amend R.E.3
Insert new paragraphs 2.9.3. and 2.9.3.1 to read:
"2.9.3. Quadricycles (L7)
2.9.3.1. Bodied Quadricycles
Vehicle of category L7 with an enclosed driving and passenger compartment accessible via maximum three sides, whose maximum speed is not more than 90 km/h and whose dimensions do not exceed the following values:
  (a) Length: 3,700 mm;
  (b) Width: 1,500 mm;
  (c) Height: 2,500 mm."
Notes: 29/07/26
<number>

## Slide 3
Justification
There is a wide variation of different styles of L7 vehicles.
Some are very ‘car-like’ in that they are equipped with a body and some car features. Typically, such vehicles are relatively fuel efficient, some electric powered.
The car-like nature of heavy passenger quadricycles (L7) may lead to expectation that they provide similar standard safety performance as a small passenger car hence the attention to improve the vehicle passive safety.
Consolidated Resolution on the Construction of Vehicles (R.E.3) defines L7 as:
In India, the Q-category was created recently, and safety requirements were published.
In Korea, Safety Regulations on Micro Mobility incl. L7-category were recently implemented.
Quadricycles are not covered under S.R.1.
Notes: 29/07/26
<number>

## Slide 4
Example of car-like L7 vehicle
Notes: 29/07/26
<number>

## Slide 5
L7-category vehicles - EU
EU Regulation 168/2013
Heavy On road Quad
ATVs (L7-B1),
Side-by-Side (L7-B2)
commercial (L7e-CU)
passenger (L7e-CP) quadricycles.
L7-A hardly exist today on the market.
Notes: 29/07/26
<number>

## Slide 6
Introduction Q-category ((G.S.R. 99(E)) in 2014
Fully enclosed body structure with doors
  top edge of the doors having at least 200 mm from adjacent seat base top surface
  steering control through steering wheel
Specific requirements for and goods vehicles
  maximum weight 450 kg / 550 kg
  Maximum seating capacity
  Maximum load 550 kg for goods vehicles
Maximum power 15 kW
Maximum design speed 70 km/h
L7-category vehicles - India

## Slide 7
Rules on Motor vehicle management Act
vehicle shall be designed and manufactured not to exceed 80km/h.
Micro-mobility:
  Length ≤ 3.6
  Width ≤ 1.5 m
  Height ≤ 2.0 m
L7-category vehicles - Korea
GRSP-65-23(65th GRSP, 13-17 May 2019)

## Slide 8: IMMA Proposal to amend R.E.3 118/GRSG, July 2020
Introduce bodied L7 vehicle
  enclosed driving and passenger compartment accessible via maximum three sides
Introduce maximum design speed
  R.E.3 90 km/h
  Korea: 80 km/h
  EU: 90 km/h
  India: 70 km/h
Introduce maximum dimensions
  R.E.3 L ≤ 3.7 m W ≤ 1.5 m H ≤ 2.5 m
  Korea: L ≤ 3.6 m W ≤ 1.5 m H ≤ 2.0 m
  EU: L ≤ 3.7 m W ≤ 1.5 m H ≤ 2.5 m
  India: L ≤ 3.0 m W ≤ 1.5 m H ≤ 2.5 m

## Slide 9: Next steps
First step, introduce and harmonise dimension criteria in R.E.3, (July 2020 GRSG-session)
  Invitation for Contracting Parties comments on informal document
  aim to submit formal document for October session
Second step, based on analysis of requirements in key markets (Europe, India, Korea, …), develop proposals for three new UN Regulations addressing bodied passenger L7-category vehicles
  Uniform provisions concerning the approval of vehicles with regard to doors
  Uniform provisions concerning the approval of vehicles with regard to interior fittings
  Uniform provisions concerning the approval of vehicles with regard to seats and seat belt anchorages
Third step, proposal to amend UN Regulation No. R137 to include ad hoc requirements including an adapted test (e.g. reduced speed) for bodied L7 vehicles.

## Slide 10
  Thank you for your attention
Notes: <number>