## Slide 1
Proposal for EDR Performance Elements
Informal document GRSG-118-29
(118th GRSG, 15-17 July 2020
Agenda item 15)

## Slide 2
发展历程
发展历程
Overwriting
1. If an EDR non-volatile memory buffer void of previous-event data is not available, the previous event data that does not meet the trigger threshold of locking memory (GRSG-118-13 3.3.2） shall be overwritten by the current event data chronologically.
Justification:
According to the view of judicial expertise institutions, usually in traffic accident analysis the more recent event data is, the more valuable it will be.
Remark: Recording the recent event data is better than it doesn’t.
GRSG-118-13 3.3.4.1 Option #1 :If an EDR non-volatile memory buffer void of previous-event data is not available, the manufacturer may choose to either overwrite any previous event data that does not deploy an air bag with the current event data, or to not record the current event data.
The previous event could be reconstructed by the subsequent events when multi-event occur in a short period.

## Slide 3
发展历程
发展历程
Overwriting
2. If an EDR non-volatile memory buffer void of previous-event data is not available, as well as EDR has other triggering conditions except for 3.3.1, the manufacturers have the choice to overwrite any previous events according to the priority of the unlocked event.
Justification:
The regulation shall allow OEM to set a special overwriting mechanism, e.g. overwriting priority between unlocked events and locked events, for those events which are more important than normal events and less important than non-reversible deployment events.

## Slide 4
发展历程
发展历程
The number of events
The EDR non-volatile memory buffer shall accommodate the data related to at least three different events.
Justification:
Learning from relevant research, 94% of the accidents will be covered when EDR records 3 events , while about 88% when EDR records 2 events.(study based on NASS GES/CDS data, GIDAS study)
The number of events
Chart: China traffic accident statistics
| 1 | 2 | 3 or more
the number of event | 18 | 14 | 63
the pecentage of event | 0.18947 | 0.14737 | 0.66316
2014-2019，95 accidents

## Slide 5
发展历程
发展历程
VRU
Due to the different situations of all the countries and regions, the specifications of the triggering condition and the locking condition related to VRU shall be discussed until the technologies are sufficiently developed.
Justification:
The technologies of VRU protection system are under development. Different OEMs equip their products with very different VRU protection systems. The requirement of VRU protection systems are different.
The VRU protection systems are not mandatory in some countries and regions.

## Slide 6
发展历程
发展历程
Data elements
The following data elements shall be deleted:
  Multi-event, number of events (1. It is unnecessary, and it can be identified by time from Event X to X-1. 2. It is very difficult to confirm the event interval.)
  Normal acceleration(It is very hard to reach consensus on the accuracy and necessity of this data element in the industry. For example the flexible structure, the complex components and so on may lead to inaccuracy of this data. It may not be suitable for the use in event reconstruction.)
  Vehicle roll angle(It is very hard to reach consensus on the accuracy and necessity of this data element in the industry.)
  Frontal air bag deployment, nth stage disposal, driver, Y/N (whether the nth stage deployment was for occupant restraint or propellant disposal purposes). Frontal air bag deployment, nth stage disposal, right front passenger, Y/N (whether the nth stage deployment was for occupant restraint or propellant disposal purposes). (It can be determined by the airbag deployment time.)

## Slide 7
发展历程
发展历程
Data elements
The following data elements shall be deleted:
  Seat track position switch, foremost, status, driver. Seat track position switch, foremost, status, front passenger(It's recording interval time is -1.0s to T0. At that moment, the accident has not happened yet. It doesn't mean much to the accident analysis. It is used for airbag control strategy.)
  Occupant size classification, driver. Occupant size classification, front passenger.(It is easy to be obtained directly via site survey of accidents.)
  Occupant position classification, driver. Occupant position classification, front passenger .(It's recording interval time is -1.0s to T0. At that moment, the accident has not happened yet. It doesn't mean much to the accident analysis. It is used for airbag control strategy.)

## Slide 8
发展历程
发展历程
Test procedure
The EDR regulation shall provide some other test methods except for crash test.
Justification:
The technical requirement shall be verified via test method. The driving operation data is used for investigation. Vehicle dynamic parameters acceleration and delta-V are important for accident reconstruction analysis, medical assistance, collision safety research, etc. which requires the accuracy of EDR data. (Sometimes EDR record was differ from reality. There are some reports about EDR’s wrong record of the event data in some accidents.)
Case 1. Toyota's attorneys also noted that although both sides in the case agreed that one of the passengers in the vehicle was belted and the other was not, the data recorder said both seat belts were unbuckled at the time. "Everyone agrees that's wrong," the Toyota attorney said, according to a transcript So clearly the veracity of the recorded data is questionable.
The Present Limitations of Motor Vehicle Electronic Data Recording, Anderson, A.F., Kirk, B., Armstrong, K.: The Present Limitations of Motor Vehicle Electronic Data Recording, December 11, 2010. An Open Letter to the NAS team working on the project: Electronic Vehicle Controls and Unintended Acceleration (TRB-SASP-10-03)
http://www.dbicorporation.com/anderson2.pdf

## Slide 9
发展历程
发展历程
Test procedure
Case 2. A new Toyota Tundra pickup struck an oak tree off a rural road in Washington state in 2007, killing the 29-year-old driver in what in many ways seemed liked a common sort of tragedy. The data indicated that the truck had been going 177 mph when it hit the tree, much faster than what the pickup possibly could go, safety experts said. Yet a separate reading from the recorder put the speed at 75 mph before impact.
Crash data recorders in Toyota inquiry have history of problems. Peter Whoriskey Sep 1, 2012 at 12:01 AMSep 27, 2018 at 2:20 AM
https://www.statesman.com/article/20120901/NEWS/309003508

## Slide 10
发展历程
发展历程
Test procedure
Case 3. Actually, the driver safety belt was buckled, but the EDR record of safety belt status was SNA(Laboratory test, 2017.8).

## Slide 11
发展历程
发展历程
Test procedure
The EDR regulation shall provide some other test methods except for crash test:
Justification:
The crash test can not verify all the technical requirements of EDR.
“Engine throttle, percent full”, “Accelerator pedal, percent full”, “ABS activity ”, “Stability control ”, “Steering input”, “Engine RPM”, “Service brake” , “Safety belt status” , etc. can’t be verified in the crash test set by UN Regulation No. 94, 95, 137.
The EDR functional and performance requirements(eg. Overwriting mechanism, power failure record capability, data elements accuracy, etc.) can not be verified via crash test.
Bench test is important for verification of the EDR system's functional and performance requirement. Bench test is using a thruster to thrust the EDR controller with a controlled impact waveform. Bench test can conduct performance requirement test by using a controlled acceleration thrust and can do functional requirement test with much lower cost than impact test.

## Slide 12
Thank you for your attention!