## Slide 1: EXPLANATORY PRESENTATION TO CLEPA NECK LOAD LIMITS PROPOSAL
Submitted by the experts from CLEPA
67th session of GRSP, 20-23rd July 2020
Informal document GRSP-67-23
67th GRSP, 20-23 July 2020
Agenda item 12

## Slide 2: BACKGROUND
ECE/TRANS/WP.29/GRSP/2019/19 proposed chest vertical acceleration limits for Q0, Q1 and Q1.5 dummies
  Justification was potential for increased neck loading in rear-facing CRS with a supine seating position
  R129 requires tensile neck force and flexion moment to be measured for monitoring only
GRSP deferred discussion to allow analysis of neck loads collected during R129 type-approvals
  Data provided by VCA and CLEPA

## Slide 3: ANALYSIS METHOD
VCA and CLEPA samples combined
Data separated for each dummy by impact direction and CRS orientation
Worst-case condition identified for each dummy
Statistical analyses carried out (95th percentile; Mean+2SD)
Limits proposed based on statistical analyses and outliers
Overview

## Slide 4: ANALYSIS METHOD
SAE J211 sign convention may not have been used in all tests in VCA sample (especially flexion moment)
Timing of peak value is unknown and may have been generated in rebound (especially flexion moment)
VCA and CLEPA samples may not be representative of the wider CRS market
Any limits are pragmatic and their relationship to real-world injury risk is unknown
Caveats

## Slide 5: PROPOSAL
 | Q0
 | Q1
 | Q1.5
n = 60
n = 32
n = 44
Dummy | 95th %ile | Mean + (2*SD) | Limit proposal
Q0 | 732 | 680 | [700]
Q1 | 933 | 1032 | [950]
Q1.5 | 2264 | 2419 | [2300]
Tensile neck force
700 N
950 N
2300 N

## Slide 6: PROPOSAL
 | Q0
 | Q1
 | Q1.5
n = 73
n = 54
n = 44
Dummy | 95th %ile | Mean + (2*SD) | Limit proposal
Q0* | 9.8 | 7.9 | [10]
 | 8.6 | 8.3 | 
Q1 | 16.3 | 13.6 | [15]
Q1.5 | 28.5 | 29.5 | [30]
n =60
* Worst-case is unclear for Q0 dummy
Neck flexion moment
10 Nm
15 Nm
30 Nm

## Slide 7: MOVING FORWARD
The analysis and limits presented here are based on samples from VCA and CLEPA only
Can other Contracting Parties provide their anonymised monitoring data to support our analysis and confirm the proposed limits?
A formal working document proposal will be submitted at GRSP-68 in December 2020

## Slide 8: MANY THANKS FOR YOUR ATTENTION
Informal document GRSP-67-XX
67th GRSP, 20-23 July 2020
Agenda item 12