## Slide 1
Submitted by the expert from Republic of Korea on behalf of IWG-DPPS
Informal document GRSP-68-14
68th GRSP, 7-11 Dec. 2020, agenda item 2(b)
Status of Informal Working Group
on Deployable Pedestrian Protection Systems
(IWG-DPPS)
Chair: Jin Seop PARK, Republic of Korea(KATRI)
Secretary: Irina Dausse, OICA(Renault)

## Slide 2
2p
Overview
Objective To develop the amendment of GTR No.9 & UN R127 w.r.t. Deployable Pedestrian Protection Systems (DPPS)
Activities - TF: NOV., 2016 ~ MAR., 2018 - IWG: MAR., 2018 ~ JUN., 2021(TOR mandate)
Meetings - 6th Meeting (3rd ~ 4th MAR., 2020 / Online) - 7th Meeting (15th ~ 17th SEP., 2020 / Online) - 8th Meeting (18th NOV., 2020 / Online)
* Due to the Covid19 pandemic, the progress is slow

## Slide 3
3p
Summary of the amendment discussion
Verification
of detection
Headform Test
(physical)
Prerequisites
- System info
- HIT
- Simulation
- Physical testing
Static test in undeployed position
@LT x 0.9
Static test in undeployed position
@ 9.7 m/s
Static test in deployed position
@ 9.7 m/s
Dynamic test
@ 9.7 m/s
Must meet the regulation criteria
* HIT = Head Impact Time
LT = Lower Threshold

## Slide 4
4p
Major Issues
HIT determination - simulation : considering the modification from Euro NCAP procedure (HBM, position, etc.) - physical testing : dummy testing based on SAE J2782 - still some challenges
Verification Impactor - Reviewing Flex-PLI as a candidate impactor
Defining test area - undeployed condition : Korea, Germany, Japan, UK - deployed condition : Netherland, OICA
* HBM = Human Body Model

## Slide 5
5p
Major Issues
HIT vs WAD for dynamic test - regression : UK, Netherland, Germany, Spain - dot-to-dot : Japan, Korea
Sensing area - Discussing the definition and correlation with head test area
* WAD = Wrap Around Distance

## Slide 6
6p
Next IWG meeting
Next Meeting - 20th ~ 21st JAN., 2021 - Online meeting
More meetings (t.b.d.)
Tentative Timeline
GTR9 drafting
Informal
GRSP
Dec 2021
Formal
GRSP
May 2022
WP29
Nov 2022

## Slide 7
7p
Thank you for your attention