## Slide 1
Luis Martínez Sáez
Informal Document GRSP-68-26
68th GRSP, 7-11 December 2020
Agenda item 12

## Slide 2: CLEPA proposal based in registered values
<number>
Chin to thorax contact is included in the measured upper neck forces.
Large increment between Q1 and Q1.5 for tensile force limit, not supported by a change in neck resistance during 6 months.
Higher limits that in a biomechanics basics development.
n = 71
n = 40
n = 54
Dummy | 95th %ile | Mean + (2*SD) | Limit proposal
Q0 | 720 | 670 | [700] N
Q1 | 905 | 1018 | [950] N
Q1.5 | 2,122 | 2,443 | [2,300] N
With upper outliers removed*: |  |  | 
Q1.5 | 1,931 | 2,261 | [2,000] N

## Slide 3: The effect of chin to thorax contact
<number>
Higher Fz tensile force is registered.
Higher thorax deformation is measured.
High variability in the tests that this issue happens.
Difficulties to control when it happens.
100 ms view

## Slide 4: The effect of chin to thorax contact
<number>
Higher Fz tensile force is registered

## Slide 5: The effect of chin to thorax contact
<number>
Higher thorax deformation is measured

## Slide 6: Upper neck force balance with chin to thorax contact
<number>
Forces acting over head
Inertial forces acceleration
LC registered forces
No chin contact
Contact forces
Chin to thorax contact
Upper neck LC register higher force

## Slide 7: How compensate chin to thorax contact?
<number>
To compute only inertial forces

## Slide 8: Example of the process
<number>
Fz with chin contact 1,629.8 N.
Fz without chin contact 1,254.3 N.

## Slide 9: Next steps
<number>
To reprocess the 54 cases presented by CLEPA.
To recalculate again the Q1.5 Fz limit.
To include Fz proposed Injury Assessment in R129.
This IA process for the upper neck tensile force may be extended to other Q dummies sizes.