## Slide 1
UN-R79 Lane Keep Assist Hands-off
Proposal
Informal document GRVA-07-23
7th GRVA, 21-25 Sept. 2020 Agenda item 6 (d)

## Slide 2: Lane-keep Assist Hands-off: Background and motivation
The informal group ACSF (16th session)
  decided to develop provisions for Automated Lane Keeping Systems, ALKS based on the assumption that such systems are already Level 3-4 according to the SAE classification.
  invited industry to start directly with GRVA the discussion on what needs to be changed /added to ECE-R79 to allow for Hands-Off/ Eyes On Lane Keeping Systems under a SAE Level 1-2 assumption.
Level 2 hands-off systems lane keeping systems from various manufacturers have been successfully introduced in US, China and Japan and industry is seeking to amend UN-R79 to be able to certify these features as well in UN-R79 territories
Motivation to increase the comfort of the driver, with positive effect on safety
Allows both drivers and manufacturers a stepwise introduction to higher levels of assistance, while being affordable for a wider audience
Source: https://www.cadillac.com/world-of-cadillac/innovation/super-cruise
Industry aims to understand the principles under which such technology seems acceptable as a driver assistance system

## Slide 3: Driver assistance systems will remain important to contribute to safety
Driver assistance systems will keep a major role to contribute to safety in the next 10 years due to the wide expansion into market and further technology progress
Level 3-4 systems will have restricted ODD and driver assistance will contribute to safety outside of ODD
Drivers should be able to get the level of assistance or automation they feel comfortable with, including level 1-2

## Slide 4: Hands-off lane keeping systems introduction in the market
Hands-off lanekeeping system are provided by several manufacturers in several large markets since 2018
Introduction:
US: 2018
Canada: 2018
China: 2018
Japan: 2019

## Slide 5: Proposal and Comparison with current ACSF B1
Lane-Keep Assist Hands-Off systems are driver assistance systems which allow hands-off when drivers eyes/head direction to road is confirmed, only on highways and with vehicle equipped with additional features.
 | ACSF B1 “hands-on” Entry into force: 2017 | ACSF B1 “hands-off” Industry proposal
Category | Driver assistance systems Lane keeping assist Motion Control by system OEDR: Driver | 
ODD restriction |  | Only highway
Driver confirmation | Hands-on confirmation + Warning escalation | Eyes/head-on confirmation* + Warning escalation *Driver Monitoring system
Max lateral acceleration | 3 m/s² | 3 m/s²
Additional requirements |  | AEBS Auto slowdown in lane if no driver reaction Hands-on request & accoustic warning in case of system failure

## Slide 6: Driver Monitoring System as key safety technology enabling hands-off
Industry is aware of possible issues of driver over-reliance
A Driver Monitoring System, ensuring the driver is directing eyes/head to the road, addresses these concerns
Eyes/head-on warning after few [x] seconds continuous eyes/head off detection
Eyes/head-on warning after cumulative eyes-off threshold
System operation
eyes/head on detection
required for system continuation
driver can put hands-off the wheel
Eyes/head on
Eyes/head off
if no positive confirmation of eyes/head-on : warning escalation
if no reaction: auto slowdown in lane
In case of system failure: hands-on request + acoustic warning

## Slide 7: Comments regarding safety of hands-off lanekeeping
The objective of the proposal is to introduce an alternative means to the hands-on detection for preventing driver’s over-reliance during the assisted lane keeping operation. The fact that the driver can remove his/her hands from the steering wheel is compensated by ensuring that the driver is directing his eyes/head to the road. Both principles equivalently support the driver in his/her driving task of continuously monitoring the behavior of the system and the driving environment and to intervene appropriately when required.
Additionally, industry has been developing specific HMI concepts to avoid over-reliance, inform driver about his/her role and is open to exchange further ideas. NHTSA already investigated in detail suitable HMI for hands-off lanekeeping systems
Due to the driver monitoring system and appropriate HMI, industry does not see risk for mode confusion, as the driver is reminded about his task to watch the road (differently from level 3 systems)
Various systems have been introduced in US, Canada, China and Japan since 2018. They have received positive feedback from customers, and have built a good reputation for safety. Customers perceive it as a useful intermediate solution for future higher degrees of automation. Industry is open to discuss the proposed safety concept and welcomes any proposals and further ideas

## Slide 8: Proposal how to amend UN-ECE R79
 | UN-R79/02 ACSF B1 Entry into force: 2017 | Lane-Keep Assist-Hands Off Proposal
Type of roads | Not limited | Limited to highways, detected by system
Driver confirmation | Trough hands-on monitoring and warning escalation | Trough driver monitoring system (head/eyes to road etc) and warning escalation
Activation | By driver, when considered useful | By driver, when considered useful
Other requirements (incl. longitudinal control) | / | If no reaction from driver to warnings: Automatic slowdown in lane AEBS
Lateral limitation | MAX 3 m/s² | MAX 3 m/s²
In case all these conditions are fulfilled, ACSF B1 hands-off warnings can be suppressed.
Target is to introduce this possibility in UN-R79 ACSF B1
Manufacturers to provide detailed safety aspect description trough Annex VI

## Slide 9
Back-up

## Slide 10
10
 | ACSF B1 “hands-on” Entry into force: 2017 | ACSF B1 “hands-off” Industry proposal | UN-R 157 ALKS Entry into force: 2020
Category | Driver assistance systems Lane keeping assist Motion Control by system OEDR by Driver |  | Automated driving system Motion control & OEDR by system
ODD restriction |  | Only highway | Only highway & declared ODD
Driver confirmation | Hands-on confirmation + Warning escalation | Eyes-on confirmation* + Warning escalation * Driver monitoring system | Availability for take-over Override intention
Control requirements | Lateral |  | Lateral + Longitudinal
Additional requirements Vs. B1 |  | AEBS Auto slowdown in lane if no driver reaction Direct hands-on request & accoustic warning in case of system failure | (see R157)
Proposal and Comparison with current ACSF B1 and ALKS

## Slide 11
11
Warning sequence vs current B1

## Slide 12
12
2019 MIT study on Functional Vigilance in Real-World Human-Machine collaboration (https://hcai.mit.edu/tesla-autopilot-human-side.pdf
2016 Study by RWTH Aachen, sponsored by VDA (FAT) and BASt, on Drivers’ management of sudden take-over situations after partly automated, hands-off driving
https://www.vda.de/de/services/Publikationen/fat-schriftenreihe-289.html
2015-2018 NHTSA studies on Human Factors Evaluation & Guidance of Level 2 and Level 3 Automated Driving Concepts
  https://www.nhtsa.gov/sites/nhtsa.dot.gov/files/812182_humanfactorseval-l2l3-automdrivingconcepts.pdf
  https://www.nhtsa.gov/sites/nhtsa.dot.gov/files/documents/13494_812555_l2l3automationhfguidance.pdf
Studies related to hands-off driving