## Slide 1: How to proceed with Advanced Driver Assist Systems and continuous automation up to Level 2 within R 79
Gail, Bartels, Gasser, Wiggerich
1
J. Gail, O. Bartels,
T. Gasser, A. Wiggerich
Federal Highway Research Institute, Germany
September 2020
Submitted by the experts from Germany
Informal document: GRVA-07-42
7th GRVA, 21-25 September 2020
Agenda item 6

## Slide 2
Basics
Systems within R 79 are described as driver assist systems
On the one hand there are systems which are only deemed to work in accident-prone situations like CSF, ESF – these are similar to systems described in other Regulations like AEBS, ESC,… This kind of assist systems have a concrete benefit for traffic safety since they can act in case the driver fails to do so or within the reaction time of the driver

## Slide 3
Basics
On the other hand there are systems which continuously support or carry out the lateral control of the vehicle For these kind of system the well known SAE-Level do apply Within R 79 we find the categories A, B1 or C:
  A for low speed manoeuvres
  B1 for hands-on lane keeping
  C for hands-on lane change
  Systems within R79 do not go beyond Level 2

## Slide 4
a) How to proceed with ADAS for accident-prone situations
Treat new systems as usual
Enable systems with safety benefits
Adapt R 79 wherever necessary to allow approval
Set requirements that ensure that the expected safety gain comes true
Set requirements to avoid negative side effects
  For systems that need a lane change do not endanger other traffic

## Slide 5
b) How to proceed with systems up to Level 2, which deliver continuous lateral support
Problem: Some facts which hold for systems up to Level 2 have to be taken into account when rulemaking shall take place:
The driver is still responsible for carrying out longitudinal and lateral control at all times
The driver has to supervise all actions of the system
The driver has to act immediately in case the system is not able to master the current driving task

## Slide 6
Problems
There is always an interaction between driver and system
Therefore the design of the system has a strong influence on how the driver carries out his driving task and thus on the capabilities of the driver (on vigilance, situation awareness, reaction times…)
system
driver

## Slide 7
Problems
The capabilities of a human being decrease if workload is too high or too low
  The human being is not good at only supervising a system
  Vigilance decreases in case the system carries out the driving task for longer periods without the need for the driver to interact
Well performing Level 2 systems may encourage the driver to do other tasks than controlling the vehicle or supervising the system (overreliance) -> the driver cannot react appropriately in case the system is not able to handle a situation

## Slide 8
Problems
Highly reliable system performance makes it difficult for drivers to develop an adequate mental model with regard to their tasks and responsibilities
Especially when system limits appear rarely and drivers get no warning or additional information, it is unlikely that they will respond immediately as required
 Vehicle automation in this case is not simply relieving drivers of routine tasks by replacing him or her with continuously automating functions but introducing also new tasks and responsibilities

## Slide 9
The Level 2 system should
support self-explanatory learning of system performance and system limits
ensure correct understanding of driver´s role and responsibility by means of system design
help drivers reacting adequately in case of system limits
prevent automation complacency and foreseeable misuse
 rulemaking should take requirements and assessment of driver behaviour and cognition into account when proceeding with systems up to Level 2

## Slide 10
Approaches for possible solutions
Keep the driver in the loop by ensuring that there is the continuous need for the driver to act or ensure the system will identify driver state and apply appropriate strategies
If this is not achieved
  Do not allow such a Level 2 system or
  Require technical means to ensure that the system can compensate the risks induced by overreliance, low vigilance, longer reaction times, missing situation awareness,…

## Slide 11
Approaches for possible solutions
Keep the driver in the loop by ensuring that there is the continuous need for the driver to act
During continuous normal driving situations the Level 2 system gives the driver only appropriate/balanced support
Clearly communicate system limits at all times
In critical situations give as much support as possible by other systems like AEB, CSF, ESF

## Slide 12
Approaches for possible solutions
If this is not achieved
  Do not allow such a Level 2 system or
  Require technical means to ensure that the system can compensate the risks induced by overreliance, low vigilance, longer reaction times, missing situation awareness,…
  Technical requirements aim to reach a degree as if to address a Level 3 system (That is why we already have relatively strict requirements for B1 and C)

## Slide 13
Literature
  Shi, E., Gasser, T., Seeck, A., and Auerswald, R. (2020). “The Principles of Operation Framework: A Comprehensive Classification Concept for Automated Driving Functions”, SAE International Journal of Connected and Automated Vehicles, 3(1)
  Wiggerich, A. (2019). “Development of a modular tool for safety assessments of human-machine-interaction for assisted driving functions (SAE level 2)”, 26th International Technical Conference on the Enhanced Safety of Vehicles (ESV), Eindhoven, NL, 2019
  Wiggerich, A., Hoffmann, H., Schömig, N., Wiedemann, K., & Segler, K. (2020). „Bewertung der Sicherheit der Mensch-Maschine-Interaktion teilautomatisierter Fahrfunktionen (Level 2)“, 13. Workshop Fahrerassistenz und automatisiertes Fahren, Uni-DAS e.V., 2020