## Slide 1: UN Regulation No. 13-H Stop Lamp Illumination
Proposal for a Suppl.2 to UN-Regulation No. 13H/01
Supporting Presentation to Document
ECE/TRANS/WP.29/GRVA/2020/31
Submitted by the expert from OICA
Informal document GRVA-07-48 7th GRVA, 21-25 September 2020 Agenda item 8(c)

## Slide 2: Current regulation UN-R 13H/01 Suppl.1
For decelerations below 0.7 m/s², the stop lamps …
  shall be ON … according to 5.2.22.1
  may be ON … according to 5.2.22.2
  shall be OFF … according to 5.2.22.4
The driver of a following vehicle does not care about the kind of braking!

## Slide 3
time [min]
1.3
0.7
SL on
SL off
accelerator pedal released
according 5.2.22.1.
brake pedal activated
according 5.2.22.4.
deceleration [m/s²]
vehicle speed [m/s ]
Current Regulation UN-R 13H/01 Suppl.1
Example: Release of the accelerator pedal of an electric vehicle
Was this intended ?

## Slide 4
The stop lamp signal should reflect the intention to decelerate.
New technologies must be taken into account (increased deceleration capabilities of modern EVs)
Stop lamp illumination requirements should be independent from the type of propulsion (combustion and/or electric)
Technical constraints to be solved (e.g. accuracy of deceleration, flickering and too frequent illumination)
Rationales Of The Proposal

## Slide 5
Shall not illuminate
Shall illuminate
May illuminate
In cases where deceleration is generated by:
Air/rolling resistance
Road Slope
Natural braking effect of the engine
Selective braking (no intention to decelerate)
Avoid too frequent illumination, at low (unintended) decelerations
In cases where the intention to decelerate is obvious:
Driver presses the brake pedal
Driver releases the accelerator of an electric vehicle, generating noticeable deceleration (>1.3m/s²)
Automatically commanded braking is demanded (e.g. by AEBS, ACC…) and generating noticeable deceleration (>1.3m/s²)
The intention to decelerate is clear
In cases where:
The intention to decelerate depends on the context (e.g. Automatically commanded braking via AEBS would preferably generate stop lamps, while a slight deceleration from ACC to stabilize speed and distance to the preceding vehicle should not).
Measures to avoid stop lamps flickering (Filtering / hysteresis) makes it difficult to define a concrete threshold below which the stop lamps should be illuminated.
Avoid stop lamps flickering and ensures consistency of the signal
Rationales Of The Proposal

## Slide 6: Current Status R13H.01 vs. Proposal
Example: Braking on flat level
forbidden
5.2.22.4.
NATURAL DRVING RESISTANCE
Inconsistent !

## Slide 7: Backup

## Slide 8: Stop Lamp Illumination: Proposal For Harmonised Behaviour:
Example: Braking on flat level
X+1.3