## Slide 1: Introducing two proposals: Amendments for UN-Regulation for ALKS [157]
Informal document GRVA-07-63
7th GRVA, 21-25 September 2020
Agenda item 4 (d)
Submitted by the expert of Germany

## Slide 2: Overview: UN-Regulation for ALKS [157] today
Automated Lane Keeping System
Highways*
Maximum speed: 60 km/h
Scope: Vehicles of category M1
Optional system (not mandatory)!
ECE/TRANS/WP29/2020/81
Proposal for a new UN Regulation on uniform provisions concerning the approval of vehicles with regards to Automated Lane Keeping System
*The vehicle is on roads where pedestrians and cyclists are prohibited and which, by design, are equipped with a physical separation that divides the traffic moving in opposite directions.

## Slide 3: Two proposals adding to UN-R ALKS
Automated Lane Keeping System
Highways*
Maximum speed: 60 km/h
Scope: Vehicles of category M1
Optional system (not mandatory)!
Speed increase up to 130 km/h
Lane change functionality
*The vehicle is on roads where pedestrians and cyclists are prohibited and which, by design, are equipped with a physical separation that divides the traffic moving in opposite directions.

## Slide 4: Motivation – Why new proposals?
General:
Automated systems expected to bring advantage in traffic and road safety, therefore natural expansion for more usage (more often and longer periods of usage; not only linked to traffic jams)
Increasing political attention and pressure in Germany
Expectation: GRVA is the Working Party as technology driver for automated, autonomous and connected driving
Specific:
130 km/h was discussed by experts in IWG ACSF, but reduced due to time/deliverables according time frame/limit; current proposal is continuation of this work

## Slide 5: New proposals: main ALKS principles unchanged!
  High-level requirements regarding safety, for example:
    Free of unreasonable risks for vehicle occupants or any other roads users
    Not cause any collisions that are reasonably foreseeable and preventable
    Comply with traffic rules relating to DDT in country of operation
    Perform self-checks to detect the occurrence of failures and confirm system performance at all times
  Criteria for activation, deactivation & override
  Conditions and procedure for Transition demand, Minimum Risk maneuver & Emergency Maneuver
What‘s the same?
DDT = Dynamic Driving Task

## Slide 6: Proposal 1: Speed increase up to 130 km/h
  Maximum speed up to 130 km/h
  New: table for forward detection range (values calculated with deceleration of 5 m/s² = actual research data for braking perfor-mances of modern passenger cars; aligns to Emergency Maneuver)
  Minimum following distance (table) extended for max. speed 130 km/h (linear upscale with 2 s limit)
Key details (GRVA/2020/32)
»
What‘s the same?
What‘s new or different?
  Compliance with traffic rules in the country of operation → legal speed limit!
  Requirements relating to DDT performance, in particular: adapt vehicle speed to infrastructural and environmental conditions
  Spatial awareness to front & sides
  Detect distance to next vehicle in front & respect minimum following distance
  Collision avoidance with unobstructed crossing pedestrian up to 60 km/h
  Validation & Testing: Annex 4 and 5
»

## Slide 7: Proposal 2: Lane change functionality
High-level principles for lane change
No violation of traffic rules
Only be performed:
  if system has sufficient information about surrounding to front, side & rear,
  if traffic situation allows it and if other road users are not endangered
    LC shall not result in collision with another vehicle or road user in predicted path
    Approaching vehicle in target lane should not have to unmanageably decelerate
Intention of performing LC shall be indicated at all times in unambiguous way
  Indicated in advance
  Changing of lane one continuous movement
  Take as long as necessary, but completed as quickly as possible
Vehicle shall always end up in a single lane of travel
…
compare ALKS MRM lane change
(activity lead by UK)
Technical performance requirements
UN-R ALKS

## Slide 8: Proposal 2: Lane change functionality
Key details (GRVA/2020/33)
What‘s new?
LCM
LCP
Lane keeping
Lane change
Definitions (starting lane, target lane, lane change procedure, lane change maneuver)
Activation criteria for LCP
  Sensing capability to rear
  System self-check positive
  Target lane positively confirmed
  Completion of LCP anticipated
Conditions for lane change
Specific requirements for LCM
Indication of lane change
Lane keeping
target lane
starting lane

## Slide 9: Proposal 2: Lane change functionality
Key details (GRVA/2020/33) - continued
What‘s left to do?
  Development of appropriate physical tests (Annex)
A + B +C !
Assessment of target lane:
LCP only initiated if approaching vehicle in target lane not forced to unmanageably decelerate
Factors taken into account:
  A: Maximum deceleration,
  B: Reaction time &
  C: Safety gap
What‘s new?

## Slide 10: Advance technology ̶ increase traffic & road safety!
Both proposals fit together, but are independent from each other
Concept unchanged: ALKS (+amendments) is optional (not mandatory!)
Proposals shall not hinder on-going activities in FRAV, VMAD or others
Germany invites interested stakeholders for exchange
Lane change functionality
SEEKING EXPERT FEEDBACK & GUIDANCE BY GRVA
Speed increase up to 130 km/h
finalized
to be finalized
(for GRVA-08)
ECE/TRANS/WP29/2020/81
Proposal for a new UN Regulation on uniform provisions concerning the approval of vehicles with regards to Automated Lane Keeping System

## Slide 11: Thank you for your kind attention!