## Slide 1
UN Regulation No. 13 and
Electro Mechanical Brakes
Informal document GRVA-07-68
7th GRVA, 21-25 September 2020 Agenda item 8(c)

## Slide 2
UN Regulation 13 defines:
Transmission means the combination of components comprised between the control and the brake and linking them functionally. The transmission may be mechanical, hydraulic, pneumatic, electric or mixed.
Control Transmission - means the combination of the components of the transmission which control the operation of the brakes, including the control function and the necessary reserve(s) of energy.
Energy Transmission - means the combination of the components which supply to the brakes the necessary energy for their function, including the reserve(s) of energy necessary for the operation of the brakes.
UN R13 and Electro Mechanical Brakes (EMB) Introduction
 The transmission may be mechanical, hydraulic, pneumatic, electric or mixed.
UN R13 was updated in 1990s to account for an electronic “Control Transmission” but still assumes Pneumatic “Energy Transmission” in the service braking system.
Pneumatic Energy limitation is shown in two ways: Design Specifications – E.g. Where limits are in kPa. Design Limitations – E.g. Where it is assumed air is the medium.
Electro Mechanical Brake Technology is being developed by the industry using Electric Energy Transmission in the service braking system and the UN R13 needs to be updated accordingly.

## Slide 3
Motor vehicle with EMB brakes on all axles (not mixed with Pneumatic Or Hydraulic systems)
Motor vehicle with EMB brakes with “conventional” trailer interface according to UN R13
UN R13-H not included but considered, in particular when creating new definitions
UN R13 and Electro Mechanical Brakes (EMB) Amendment scope and motivation
Advantages and possibilities by amending Electric Energy Transmission to UN R13
Improved energy efficiency in EV´s (vs. air compressor)
Improved braking control
Elimination of noise emissions from pneumatics

## Slide 4
UN R13 and Electro Mechanical Brakes (EMB) Electrification Development
EBS in Commercial vehicles – (electronic control transmission)
Electric parking brake
Hybrid Electric vehicles
Electric Power Steering
Full Electric Vehicles
EMB in Commercial vehicles – (electronic control transmission and electric service braking)
1995
2025
Improved Vehicle Dynamics Control
Emission reduction
Energy efficiency

## Slide 5
UN R13 and Electro Mechanical Brakes (EMB) Electrification Development
Improved Vehicle Dynamics Control
  Reduced response time enhancing braking performance.
  Optimized control of safety functions like ABS, ESP, AEBS or Traction control.
Emission reduction
  Reduction of noise vs. pneumatic brake systems.
Energy efficiency
  Significant higher energy efficiency vs. pneumatic brake systems.
  Potential to reduce CO2.
Other
  Weight and space savings
  Easier packaging

## Slide 6
2. Definitions
New paragraphs defining Electric Energy Transmission ( e,g Energy Source, Electrical Storage device, Electrical Supply device)
5.1.4.6 Reference Braking forces
New paragraph 5.1.4.6.2.
Reference braking forces for electro-mechanical braking system using a roller brake tester shall be defined according to the following requirements.
5.2 Characteristics of Braking Systems.
New paragraph 5.2.1.34.
Special additional requirements for service braking systems with electric control and energy transmissions.
Annex 7, (provisions relating to energy supply and storage)
New Part D
Electro-mechanical Braking system
ECE-R13 and Electro Mechanical Brakes (EMB) Main parts to be amended

## Slide 7
7
UN R13 and Electro Mechanical Brakes (EMB) Energy Transmission principles (Pneumatic vs. Electric)
Compressor
E-APU
Pneumatic energy
storage
EBS Modulator
Actuator
Caliper
Drive and Motor
Gears
Caliper
DC/DC
Energy storage
Pneumatic
Energy
Electric
Energy
Annex 7 part A
Annex 7 new part D
Electric energy storage
Actuation
Energy supply
EBS
EMB
New 5.2.1.34.

## Slide 8
UN R13 and Electro Mechanical Brakes (EMB) Development steps comparison
Principal layouts shown

## Slide 9
System Description
Example EBS system of today in vehicle with combustion engine
Energy Source
Energy Source
Pneumatic
Storage Device
Control Transmission (example shown only front axle)
p1 and p2: Pneumatic energy monitoring and warning if storage falls below a certain level.
Energy Transmission
p1
p2
Principal layout

## Slide 10
System Description
Example EMB system in electric vehicle
Energy Transmission
Energy Source
Control Transmission (example shown only front axle)
Energy Supply Device
Electrical Storage Device
Pw: Electric energy monitoring and warning if charging demand cannot be met and if below a certain level.
ew: Electric energy monitoring and warning if storage falls below a certain level.
Pw
ew1
ew2
Principal layout

## Slide 11
Feedback in short from the delegates so far:
Further comparison between Compressed Air braking system and Electro-Mechanical braking system requested for better understanding of the differences and need for specific requirements on an EMB system.
Concerning Electrical Energy Storage devices, and in particular batteries, there is an uncertainty regarding the performance over lifetime vs. a pneumatic reservoir. A reliable and safe way of monitoring the energy level is requested.
Unclear how the PTI actually will be performed. The boundary conditions as well as a general approach exist but needs to be further verified together with industry and Technical Service representatives.
UN R13 and Electro Mechanical Brakes (EMB) Feedback from delegates and open topics