## Slide 1: Proposals from the Informal Working Group on AEBS to amend UN R. No. 152
Informal Working Group on AEBS for Light Vehicles
Informal document GRVA-07-70
7th GRVA, 21-25 September 2020, Agenda item 7
Including Car to Bicycle scenario in the regulation
Amendments of 00 and 01 series
Chair and Secretary IWG AEBS – GRVA 07
Four working documents (26, 27, 28, 35) Four informal documents (09, 10, 11, 53)

## Slide 2
Discussion point in 7th GRVA
Part I
Requirement of Car to Bicycle scenario
Implementation of requirements (Single step or 2 step)
Guidance from GRVA
Part II
Amendments of existing regulations
(00 series and 01 series)
Deactivation of AEBS, Road test surface,
False reaction scenarios, Clarifications, Corrigendum
Guidance from GRVA
Chair and Secretary IWG AEBS – GRVA 07

## Slide 3
Informal Working Group on AEBS for Light Vehicles
Chair and Secretary IWG AEBS – GRVA 05
IWG meetings 12th meeting in web (14-15 May 2020)
13th meeting in web (25-26 June 2020)
14th meeting in web (4 September 2020)
7th GRVA in September 2020:
Result of 12th and 13th → GRVA-2020-26, 27, 28, 35
Result of 14th → GRVA-07-09, 10, 11, 53
5th GRVA in February 2020:
GRVA agreed to continue the discussions about “Car to Bicycle scenario”

## Slide 4
Chair and Secretary IWG AEBS – GRVA 07
Informal Working Group on AEBS for Light Vehicles
Car to Bicycle scenario

## Slide 5
Informal Working Group on AEBS for Light Vehicles
Specifications - Car to Bicycle scenario
Chair and Secretary IWG AEBS – GRVA 07
Scenario of C2B
Inserting a new paragraph 5.2.3. and 6.7.
Crossing collision same as Car to Pedestrian scenario
What is different between C2B and C2P?
Speed (including tolerance in test) of target
C2B: 10 to 15 km/h in Para. 5.2.3.4.
C2P: Not more than 5 km/h in Para. 5.2.2.4.
Robustness system in Para. 6.10.1
C2B: 20 % and C2P: 10 %
Lower speed of ego vehicle in Para. 5.2.3.3.
Single step or 2 step
1m
0.75m
15km/h
Margin = 3.65m
Lane edge
Vehicle edge
TTC = 0.888 [s]
Vavoidance = 39.5 [km/h]
TTC

## Slide 6
At the lower speed limit: Stable detection of a bicycle is far more difficult than that of a pedestrian.
  The limiting factor of performance is the field of view of the sensing system.
  In order to make a robust decision for intervention, the objects need to be detected and classified consistently over a period of time.
At the upper speed limit: The emergency braking timing calculation used in system design is more complex than the basic assumptions used to calculate the maximum speed reduction.
  Car2Pedestrian = intervention starts, when the pedestrian is only 30cm away from the path of the vehicle.
  Car2Bicycle = intervention starts, when the bicycle is several meters away.
  Therefor the risk of false activations is increased.
Informal Working Group on AEBS for Light Vehicles
Robustness system in Para. 6.10.1 The reason for 20% - Car to Bicycle
Chair and Secretary IWG AEBS – GRVA 07

## Slide 7
Informal Working Group on AEBS for Light Vehicles
Final Specifications in GRVA-2020-27 or 28 - Car to Bicycle – Speed reduction
Maximum Impact Speed (km/h) for M1
Maximum Impact Speed (km/h) for N1
Subject vehicle speed (km/h) | Maximum mass | Mass in running order
20 | 0.00 | 0.00
25 | 0.00 | 0.00
30 | 0.00 | 0.00
35 | 0.00 | 0.00
38 | 0.00 | 0.00
40 | 10.00 | 0.00
45 | 25.00 | 25.00
50 | 30.00 | 30.00
55 | 35.00 | 35.00
60 | 40.00 | 40.00
Subject vehicle speed (km/h) | Maximum mass | Mass in running order
20 | 0.00 | 0.00
25 | 0.00 | 0.00
30 | 0.00 | 0.00
35 | 0.00 | 0.00
36 | 0.00 | 0.00
38 | 15.00 | 0.00
40 | 25.00 | 0.00
45 | 30.00 | 25.00
50 | 35.00 | 30.00
55 | 40.00 | 35.00
60 | 45.00 | 40.00
Chair and Secretary IWG AEBS – GRVA 07
IWG proposed two options for existing vehicles.
Single step: full collision avoidance from 20km/h from 5/2026
2 step: full collision avoidance from 30km/h from 5/2026
20 km/h from 9/2028

## Slide 8
Informal Working Group on AEBS for Light Vehicles
Difference between single step and 2 step: Summary
Approaches | Suppl. or Series | New Type Approvals | Existing Type Approvals
Single step approach | Car-to-bicycle (as a Suppl. 2 to the 01 series) | May 2024 | Can be mandated as from May 2026
2 step approach | Car-to-bicycle – Step 1 (as a Suppl. 2 to the 01 series) | Date of Entry Into Force and before May 2024 | Shall be accepted until September 2028
 | Car-to-bicycle – Step 2 (as a new 02 series) | May 2024 | Can be mandated as from September 2028
Chair and Secretary IWG AEBS – GRVA 07

## Slide 9
Informal Working Group on AEBS for Light Vehicles
Guidance from GRVA about Car to Bicycle scenario
Guidance from GRVA related Car to Bicycle scenario
Requirement of Car to Bicycle scenario
Implementation of requirements (Single step or 2 step)
Documents
Single step
GRVA-2020-27 (Supplement amendment of 01 series)
2 step
GRVA-2020-35 (Supplement amendment of 01 series)
GRVA-2020-28 (New 02 series)
GRVA-07-12 (OICA/CLEPA)
Chair and Secretary IWG AEBS – GRVA 07

## Slide 10
Informal Working Group on AEBS for Light Vehicles
Part II
Amendments of existing regulations
(00 series and 01 series)
Deactivation of AEBS, Road test surface,
False reaction scenarios, Clarifications, Corrigendum
Chair and Secretary IWG AEBS – GRVA 07

## Slide 11
Informal Working Group on AEBS for Light Vehicles
Working Documents
Reflecting the result of IWG in June 2020
GRVA-2020-26 (Supplement 3 amendment of 00 series)
GRVA-2020-27, 28 and 35 were reflected same amendments of GRVA-2020-26.
Informal Documents
Reflecting the result of IWG in September 2020
GRVA-2020-26 was amended by GRVA-07-09 (00 series)
GRVA-2020-27 was amended by GRVA-07-10 (01 series as single step)
GRVA-2020-28 was amended by GRVA-07-11 (02 series as 2 step)
GRVA-2020-35 was amended by GRVA-07-53 (01 series as 2 step)
Chair and Secretary IWG AEBS – GRVA 07

## Slide 12
Informal Working Group on AEBS for Light Vehicles
Amendment of existing regulations
Items
Deactivation of AEBS (Para. 5.4.2.3)
Road test surface (Para. 6.1.1.1)
False reaction scenarios (Appendix 2 in Annex 3)
Response to failures (Para. 5.1.4.1.3)
False reaction avoidance (Para. 5.1.6)
Speed reduction by demand (Para. 5.2.1.4, 5.2.2.4, 5.2.3.4)
Sensor misalignment (Para. 5.4.2)
Relationship between AEBS and other ADAS (Para. 5.4.4)
Yellow color for signaling AEBS temporary deactivation (Para. 5.5.7)
Permitting deviating test conditions (Para. 6.1.6)
Test target of Car to Car scenario (Para. 6.3.1)
Subject vehicle test speed in test procedures (Para. 6.4, 6.5, 6.6, 6.7)
Proposed by (1) Working document, (2) Working and Informal document,
(3) Informal document.
Chair and Secretary IWG AEBS – GRVA 07

## Slide 13
Informal Working Group on AEBS for Light Vehicles
Amendment of existing regulations
Chair and Secretary IWG AEBS – GRVA 07
Deactivation of AEBS (Para. 5.4.2)
Working document (26, 27, 35)
5.4.2. When the vehicle is equipped with a means to automatically deactivate the AEBS function, for instance in situations such as off-road use, being towed, being operated on a dynamometer, being operated in a washing plant, in case of a non-detectable misalignment of sensors, [or when the Electronic Stability Control is switched off,] the following conditions shall apply as appropriate:
OICA propose this issue as GRVA-2020-25.
IWG could agree the below requirement in last Sep. IWG.
New proposal in informal documents (9, 10, 11)
5.4.2.3. Where automatic deactivation of the AEBS function is a consequence of the driver manually switching off the ESC function of the vehicle, this deactivation of the AEBS shall require at least two deliberate actions by the driver.

## Slide 14
Informal Working Group on AEBS for Light Vehicles
Amendment of existing regulations
Road test surface (Para. 6.1.1.1)
Working document (26, 27, 35)
6.1.1.1. The road test surface shall have a nominal peak braking coefficient (PBC) of at least 0.9. unless otherwise specified. when measured using either:
In footnote 3: The "nominal" value is understood as being the minimum theoretical target value.”
IWG agreed the below requirement in last Sep. IWG.
New proposal in informal documents (9, 10, 53)
6.1.1.1. The road test surface shall have a nominal peak braking coefficient (PBC) of at least 0.9. unless otherwise specified. when measured using either:
In footnote 3: The "nominal" value is understood as being the minimum theoretical target value.”
Since it is the provisions regarding road to be used in other tests (R140 / R78), PBC value should be in the same sentence as the R140 / R78 in accordance with GTR3 / GTR8.
As a practical issue according to ASTM, there are several test surfaces that do not exceed a PBC value of 0.9 per year check. Taking into account this, the simple wording “nominal” is suitable according to ASTM method.

## Slide 15
False reaction scenarios (Appendix 2 in Annex 3)
Working document (26, 27, 35)
Informal Working Group on AEBS for Light Vehicles
Amendment of existing regulations
Insert a new introductory paragraph, to read:
The following scenarios shall be used to assess the system’s strategies implemented in order to minimize the generation of false reactions. For each type of scenario the vehicle manufacturer shall explain the principle strategies implemented to ensure safety.
The manufacturer shall provide evidence (e.g. simulation results, real-world test data, track test data) of the system’s behaviour in the described types of scenarios. The parameters described in subparagraph 2 of each scenario shall be used as guidance if the Technical Service deems a demonstration of the scenario necessary.
New scenario for false reaction of AEBS
Scenario 1: Left turn or Right turn at the intersection
Scenario 2: Right turn or Left turn of a forward vehicle
Scenario 3: Curved road with guard pipes and a stationary object
Scenario 4: Lane change due to road construction
These scenarios were proposed by Japan (AEBS-13-07)
Chair and Secretary IWG AEBS – GRVA 07

## Slide 16
False reaction scenarios (Appendix 2 in Annex 3)
Informal document (9, 10, 53)
Informal Working Group on AEBS for Light Vehicles
Amendment of existing regulations
1. Move definitions as a new introduction paragraph.
Overlap ratio
(The name change from the wrap ratio to the overlap ratio)
Offset ratio
2. Amendment of corrigendum
in Figure 1 (left turn) and Figure 2 (right turn).
Chair and Secretary IWG AEBS – GRVA 07

## Slide 17
Informal Working Group on AEBS for Light Vehicles
Amendment of existing regulations
Insert a new paragraph 5.1.4.1.3., to read:
“5.1.4.1.3. Upon detection of any non-electrical failure condition (e.g. sensor blindness or sensor misalignment), the warning signal as defined in paragraph 5.1.4.1. shall be illuminated.”
Paragraph 5.1.4.3., delete.
Response to failures (Para. 5.1.4.1.3)
Informal documents (9, 10, 53)
Proposal to move the current paragraph 5.1.4.3. up as a 3rd subparagraph of 5.1.4.1.
The latter states that any failure that leads the system to no longer meet the requirements, shall be indicated to the driver. The following sub-paragraphs address the individual failure response to an electrical failure (5.1.4.1.1.) to a delayed initialization (5.1.4.1.2.) and the third sub-paragraph should be non-electrical failure conditions (which is currently a separate paragraph).
Chair and Secretary IWG AEBS – GRVA 07

## Slide 18
Informal Working Group on AEBS for Light Vehicles
Amendment of existing regulations
False reaction avoidance (Para. 5.1.6)
Informal documents (9, 10, 53)
5.1.6. False reaction avoidance
The system shall be designed to minimise the generation of collision warning signals and to avoid advanced emergency braking in situations where there is no risk of an imminent collision the driver would not recognise an impending collision. This shall be demonstrated in the assessment carried out under Annex 3, and this assessment shall include in particular scenarios listed in Appendix 2 of Annex 3.
This amendment aims to clarify that warning or emergency brakings shall not be given in situations where the driver would not assess the situation to be critical. With the original wording “where the driver would not recognise an impending collision” it could be misunderstood that interventions were only justified where the criticality of a situation was obvious to the driver, which is not always the case.
Chair and Secretary IWG AEBS – GRVA 07

## Slide 19
5.2.1.4. Speed reduction by braking demand
(e) In ambient illumination conditions of at least 1000 Lux without direct blinding of the sensors (e.g. direct blinding sunlight);
(f) In absence of weather conditions affecting the dynamic performance of the vehicle (e.g. no storm, not below 0°C); and in absence of extreme driving conditions (e.g. harsh cornering).
(g) When driving straight with no curve, and not turning at an intersection.
Informal Working Group on AEBS for Light Vehicles
Amendment of existing regulations
Speed reduction by demand (Para. 5.2.1.4 and Para. 5.2.2.4)
Working document (26, 27, 35)
Paragraph 5.2.1.4.(e): refining the wording since the light affecting the sensor can be indirect; the direct sunlight is only an example
Paragraph 5.2.1.4.(f): attempts to further discriminate the relevant affecting parameters in order to avoid large exemptions. Technically, two effects are simultaneously at stake:
(a) The yaw movement of the sensor attached to the vehicle can create a “ghost” movement in the perception of a stationary (or slow moving) obstacle
(b) In the case of a turning event (e.g. at a junction or in a parking) an obstacle can remain out of the field of detection until the very end of the manoeuvre.

## Slide 20
Informal Working Group on AEBS for Light Vehicles
Amendment of existing regulations
Sensor misalignment (Para. 5.4.2)
Informal documents (9, 10, 53)
This provision is already covered by the new paragraph 5.1.4.1.3.: need to avoid confusion with the warning.
5.4.2. When the vehicle is equipped with a means to automatically deactivate the AEBS function, for instance in situations such as off-road use, being towed, being operated on a dynamometer, being operated in a washing plant, in case of a non-detectable misalignment of sensors, the following conditions shall apply as appropriate:
Chair and Secretary IWG AEBS – GRVA 07

## Slide 21
Informal Working Group on AEBS for Light Vehicles
Amendment of existing regulations
Speed reduction by demand (Para. 5.2.2.4)
Working document (26, 27, 35)
5.2.2.4. Speed reduction by braking demand
(a) With unobstructed perpendicularly crossing pedestrians with a lateral speed component of not more than 5 km/h;
Paragraph 5.2.2.4 (a): clarifies that the pedestrian’s path is assumed to be broadly perpendicular to the ego vehicle’s path for avoiding the effect of an unexpected component of movement.
Chair and Secretary IWG AEBS – GRVA 07

## Slide 22
Informal Working Group on AEBS for Light Vehicles
Amendment of existing regulations
Insert a new paragraph 5.4.4., to read
5.4.4. While automated driving functions are in longitudinal control of the vehicle (e.g. ALKS is active) the AEBS function may be suspended or its control strategies (i.e. braking demand, warning timing) adapted without indication to the driver, as long as it remains ensured that the vehicle provides at least the same collision avoidance capabilities as the AEBS function during manual operation.
This proposal to clarify the understanding of the AEBS functioning when assistance systems are in operation: “when a longitudinal control system is active, the vehicle deceleration may be smooth enough not to reach the requested 5 m/s² (paragraph 5.2.2.2.) hence making the AEBS superfluous. Of course, AEBS remains in veil and intervenes in case of sudden unexpected event”.
Relationship between AEBS and other ADAS (Para. 5.4.4)
Working document (26, 27, 35)
Chair and Secretary IWG AEBS – GRVA 07

## Slide 23
Informal Working Group on AEBS for Light Vehicles
Amendment of existing regulations
Yellow color for signaling AEBS temporary deactivation (Para. 5.5.7)
Informal documents (9, 10, 53)
5.5.7. When the driver is provided with an optical warning signal to indicate that the AEBS is temporarily not available, for example due to inclement weather conditions, the signal shall be constant and yellow in colour. The failure warning signal specified in paragraph 5.5.4. above may be used for this purpose.
Proposal to avoid a confusion by the driver of the conditions of paragraph 5.4.3. (AEBS deactivation) and of paragraph 5.5.7. (function not available).
Chair and Secretary IWG AEBS – GRVA 07

## Slide 24
Informal Working Group on AEBS for Light Vehicles
Amendment of existing regulations
Insert a new paragraph 6.1.6., to read
6.1.6. At the request of the manufacturer and with the agreement of the Technical Service tests may be conducted under deviating test conditions (suboptimal conditions, e.g. on a not dry surface; below the specified minimum ambient temperature), whilst the performance requirements are still to be met.
This amendment aims to carry over the amendment to UN-R79 ACSF B1 already adopted by GRVA-04 to the AEBS Regulation as well.
In order to ensure type approval testing also during the winter months it should be possible to test vehicles also on wet surfaces or at lower temperatures. Since both influences tend to result in lower adhesion, this results in a more challenging situation to the system than the standard test conditions defined by the Regulation, and additional demonstration of system behavior within the specified range is not necessary because it would already be covered by the performed tests.
Permitting deviating test conditions (Para. 6.1.6)
Informal documents (9, 10, 53)
Chair and Secretary IWG AEBS – GRVA 07

## Slide 25
Informal Working Group on AEBS for Light Vehicles
Amendment of existing regulations
Test target of car to car scenario (Para. 6.3.1)
Working document (26, 27, 35)
6.3.1. The target used for the vehicle detection tests shall be a regular high-volume series production passenger car of Category M1 AA saloon. or alternatively a "soft target" representative of such a vehicle in terms of its identification characteristics applicable to the sensor system of the AEBS under test according to ISO 19206-1:2018 ISO 19206-3:2020. The reference point for the location of the vehicle shall be the most rearward point on the centreline of the vehicle.
Chair and Secretary IWG AEBS – GRVA 07

## Slide 26
Informal Working Group on AEBS for Light Vehicles
Amendment of existing regulations
Maximum mass | Mass in running order | Tolerance
20 | 20 | +2/-0
40 | 42 | +0/-2
60 | 60 | +0/-2
All values in km/h with a tolerance of +0/-2 km/h
Subject vehicle test speed in test procedures (Para. 6.4, 6.5, 6.6, 6.7)
Working document (26, 27, 28, 35)
Informal documents (9, 10, 11, 53)
At low test speeds, the current tolerance would force testing at e.g. 18 km/h, i.e. at speeds beyond the operating design domain of the system or of the frame of testing conditions. The tolerance must hence be shifted into the domain of operation and/or the defined test conditions.
Chair and Secretary IWG AEBS – GRVA 07

## Slide 27
Informal Working Group on AEBS for Light Vehicles
Activities of this IWG
TOR (GRRF-84-03)
The informal group shall address the following issues:
  Define AEBS requirements adapted to moving and stationary obstacles. Priority will be given to rear end collision with M/N vehicles.
  Define AEBS requirements adapted to pedestrians.
  Define AEBS requirements adapted to cyclists
  Shall provide a technical review for the extension of technical requirements to include motorcyclists and large animals.
Chair and Secretary IWG AEBS – GRVA 07

## Slide 28
Informal Working Group on AEBS for Light Vehicles
Thank you
for your attention
Chair and Secretary IWG AEBS – GRVA 07

## Slide 29
4th GRVA (September 2019)
GRVA agreed two proposal in 4th session.
01 supplement amendment of existing regulation (GRVA-04-51 → WP29-2020-09)
01 series amendment for C2P and deletion of N1 full cab (GRVA-04-52 → WP29-2020-10)
Result of 180th WP29 in March 2020
WP29-2020-09 and WP29-2020-10 were adopted at WP29 in March.
01 supplement amendment of the original series (Revision of requirements etc.)
01 series amendment (Remove N1 full cab vehicle etc.)
5th GRVA (February 2020)
GRVA agreed the proposal for “Robustness of system” in 5th session.
GRVA adopted the proposal of the original and 01 series amendment in 5th session.
(GRVA-2020-17 amended by GRVA-05-60 → WP29-2020-98)
181th WP29 in June 2020
WP29-2020-98 (original series) was adopted at WP29 in June.
02 supplement amendment of the original series (Robustness system)
01 supplement amendment of 01 series (Robustness system) (Confirmation: 182th WP29 in November 2020)
Chair and Secretary IWG AEBS – GRVA 07
Appendix

## Slide 30
Informal Working Group on AEBS for Light Vehicles
Implementation of requirements – Single step or 2 step
Single step (Details in GRVA-2020-27)
Below requirements apply as Supplement 02 of the 01 series.
Lower speed range of subject vehicle is from 20 km/h
Maximum Impact Speed (km/h) for M1
Maximum Impact Speed (km/h) for N1
Subject vehicle speed (km/h) | Maximum mass | Mass in running order
20 | 0.00 | 0.00
25 | 0.00 | 0.00
30 | 0.00 | 0.00
35 | 0.00 | 0.00
38 | 0.00 | 0.00
40 | 10.00 | 0.00
45 | 25.00 | 25.00
50 | 30.00 | 30.00
55 | 35.00 | 35.00
60 | 40.00 | 40.00
Subject vehicle speed (km/h) | Maximum mass | Mass in running order
20 | 0.00 | 0.00
25 | 0.00 | 0.00
30 | 0.00 | 0.00
35 | 0.00 | 0.00
36 | 0.00 | 0.00
38 | 15.00 | 0.00
40 | 25.00 | 0.00
45 | 30.00 | 25.00
50 | 35.00 | 30.00
55 | 40.00 | 35.00
60 | 45.00 | 40.00
Chair and Secretary IWG AEBS – GRVA 07
Appendix

## Slide 31
Informal Working Group on AEBS for Light Vehicles
Implementation of requirements – Single step or 2 step
2 step
Combination of Supplement amendment and Series amendment.
Below table show the transitional provision for the series amendment.
 | New Type Approvals | Existing Type Approvals
Car-to-bicycle – Step 1 (as a Suppl. 2 to the 01 series) | Date of Entry Into Force | Shall be accepted until September 2028
Car-to-bicycle – Step 2 (as a new 02 series) | May 2024 | Can be mandated as from September 2028
Chair and Secretary IWG AEBS – GRVA 07
Appendix

## Slide 32
Informal Working Group on AEBS for Light Vehicles
Implementation of requirements – Single step or 2 step
2 step (Details in GRVA-2020-35)-Step1
Below requirements apply as Supplement 02 of the 01 series.
Lower speed of subject vehicle is from 30 km/h
Subject vehicle speed (km/h) | Maximum mass | Mass in running order
30 | 0.00 | 0.00
35 | 0.00 | 0.00
38 | 0.00 | 0.00
40 | 10.00 | 0.00 10.00
45 | 25.00 | 25.00
50 | 30.00 | 30.00
55 | 35.00 | 35.00
60 | 40.00 | 40.00
Subject vehicle speed (km/h) | Maximum mass | Mass in running order
30 | 0.00 | 0.00
35 | 0.00 | 0.00
38 | 15.00 | 0.00
40 | 25.00 | 10.00
45 | 30.00 | 25.00
50 | 35.00 | 30.00
55 | 40.00 | 35.00
60 | 45.00 | 40.00
Maximum Impact Speed (km/h) for M1
Maximum Impact Speed (km/h) for N1
Chair and Secretary IWG AEBS – GRVA 07
IWG agreed the collision avoidance at 40 km/h.
GRVA-07-11 Para. 5.2.3.4.
Appendix

## Slide 33
Informal Working Group on AEBS for Light Vehicles
Implementation of requirements – Single step or 2 step
2 step (Details in GRVA-2020-28)-Step2
Below requirements apply as the new 02 series.
Lower speed of subject vehicle is from 20 km/h
Maximum Impact Speed (km/h) for M1
Maximum Impact Speed (km/h) for N1
Subject vehicle speed (km/h) | Maximum mass | Mass in running order
20 | 0.00 | 0.00
25 | 0.00 | 0.00
30 | 0.00 | 0.00
35 | 0.00 | 0.00
38 | 0.00 | 0.00
40 | 10.00 | 0.00
45 | 25.00 | 25.00
50 | 30.00 | 30.00
55 | 35.00 | 35.00
60 | 40.00 | 40.00
Subject vehicle speed (km/h) | Maximum mass | Mass in running order
20 | 0.00 | 0.00
25 | 0.00 | 0.00
30 | 0.00 | 0.00
35 | 0.00 | 0.00
36 | 0.00 | 0.00
38 | 15.00 | 0.00
40 | 25.00 | 0.00
45 | 30.00 | 25.00
50 | 35.00 | 30.00
55 | 40.00 | 35.00
60 | 45.00 | 40.00
Chair and Secretary IWG AEBS – GRVA 07
Appendix