## Slide 1: IWG Safer Transport of Children in Buses and Coaches
Fifth meeting
28/01/2021
OICA
Informal document GRSG-121-03
(121th GRSG, 12-16 April 2021 Agenda item 2(a))

## Slide 2: CRS installation in buses & coaches
Influence on interior arrangements of buses & coaches:
  Seat dimensions and spacing
  Access to the vehicle seats
  Relevant vehicle classes
  2-pts belt / 3-pts belt restraint availability
  In-vehicle child seats (eg: Sit Safe)
  Support leg assessment volume
France, Germany, Spain and UK accident data

## Slide 3: Influence on interior arrangements of buses 1) Seat dimensions and spacing
Using UN R 129-CRS would lead to larger seat spacing and a significant loss of seats in the vehicles
Seat spacing
UN-R107 Annex 3 §7.7.8.4
 | H
Classes I, A and B | 650 mm
Classes II and III | 680 mm
Rear-facing ISO/R2 CLASS D
Front-facing ISO/F3 CLASS A
1300 mm
915 mm

## Slide 4: Influence on interior arrangements of buses 1) Seat dimensions and spacing
Permitted intrusions acc. to UN R 107 are in conflict with the dimensions of UN R 129-CRS!
Permitted intrusion above a seating position
UN-R107 Annex 3 §7.7.8.6.3.2
I (mm)
400 to 500 (for Classes A, B, I and II min 350 mm at wheel arches and engine compartment(s))
5
6
5
6
Top view
Front view
5
6
Handrail
Cantrail

## Slide 5: Influence on interior arrangements of buses 2) Access to the vehicle seats
Class B mannequin
Class | B (mm) | C (mm) | D (mm) | E (mm) | F (mm)
I | 550 | 450 | 500 | 1900 | 900
A and II | 550 | 350 | 500 | 1900 | 900
B | 450 | 300 | 300 | 1500 | 900
III | 450 | 300 | 500 | 1900 | 900
Gangway mannequin (Class B)
UN-R107 Annex 3 §7.7.8.6.3.2
1500 mm
900 mm
300 mm
Ø450 mm
Ø300 mm
ISO/F3 CLASS A
UN R 107 Gangway dimensions do not permit to move the CRS to the individual passenger seats!

## Slide 6: Influence on interior arrangements of buses 3) Relevant vehicle classes
Seat belt fitting in Class II – vehicles follows national regulations of CPs – harmonisation needed?
 |  |  | UN-R16 Minmum requirements for safety belts |  | 
Number of passengers | Accomodation of passengers | Class | GVM ≤ 5t (M2) |  | GVM > 5t (M3)
 |  |  | GVM ≤ 3.5t | GVM > 3.5t | 
9 - 22 | Standing +seated | A | No * | No * | No *
 | All seated | B | 3-pt belt ** | 2-pt belt ** | 2-pt belt **
> 22 | Standing & seated (urban) | I | No * | No * | No *
 | Mostly seated (interurban) | II | No *** | No *** | No ***
 | All seated (coach) | III | 3-pt belt | 2-pt belt ** | 2-pt belt **
* When fitted, safety-belts must be in compliance with this regulation
** 8.1.7 – 3-pt belt must be installed unless:
1) Reference zone empty or
2) UN-R80 seat or
3) Parts fulfilling UN-R80 energy absorption test.
*** Contracting Parties applying this Regulation may demand the installation of safety belts on M2 and M3 vehicles belonging to Class II.

## Slide 7: Influence on interior arrangements of buses 4) 2-pts belt / 3-pts belt availability
Most vehicles on the market are fitted with 2P-belts with energy absorbing zones!
 |  |  | UN-R16 Minmum requirements for safety belts |  | 
Number of passengers | Accomodation of passengers | Class | GVM ≤ 5t (M2) |  | GVM > 5t (M3)
 |  |  | GVM ≤ 3.5t | GVM > 3.5t | 
9 - 22 | Standing +seated | A | No * | No * | No *
 | All seated | B | 3-pt belt ** | 2-pt belt ** | 2-pt belt **
> 22 | Standing & seated (urban) | I | No * | No * | No *
 | Mostly seated (interurban) | II | No *** | No *** | No ***
 | All seated (coach) | III | 3-pt belt | 2-pt belt ** | 2-pt belt **
* When fitted, safety-belts must be in compliance with this regulation
** 8.1.7 – 3-pt belt must be installed unless:
1) Reference zone empty or
2) UN-R80 seat or
3) Parts fulfilling UN-R80 energy absorption test.
*** Contracting Parties applying this Regulation may demand the installation of safety belts on M2 and M3 vehicles belonging to Class II.

## Slide 8: Influence on interior arrangements of buses 5) In-vehicle child seats
CRS-bus approval shall follow prescriptions on UN R 80 – basis, shall be technology neutral and not focused on existing R 129-CRS
Eg: SiTSafe as a solution for option in Nordic bus procurement requirements
« At least 2 child seats for 3 years of age (UN-R44) »

## Slide 9: Influence on interior arrangements of buses 6) Support leg volume assessment
585
695
200 mm
525
Side view
585
695
200
525
200 mm
Support leg might lead to further increase of seat spacing and further loss of seats in the vehicle!
Front-facing ISO/F3 CLASS A

## Slide 10: France, Germany, Spain and UK accident data
Most of injured children are above 9 years old
Most of them were not restrained.

## Slide 11: SUMMARY
We identified some issues with significant influence on vehicle and its interior and seating layout :
  CRS according to UN-R129 seem not to be compatible with Bus interior arrangements according to UN-R 107
France, Germany, Spain and UK accident data :
    Main victim population: 9 years and older
    Cause: unrestrained
We propose to seek guidance from GRSG
  How to deal with vehicle requirements (UN-R107)
  Number of designated CRS places in the vehicle needed?
  ToR of the IWG to be amended accordingly