## Slide 1: IWG AEBS-HDV Status and Outlook
Toshiya Hirose (JP) & Patrick Seiniger (BASt, DE)
Chairs of the IWG on AEBS for HDV
Submitted by the IWG on AEBS-HDV
Informal document GRVA-11-27
11th GRVA, 27 Sept. – 1 Oct. 2021 Provisional agenda item 7

## Slide 2: Introduction
Informal Working Group on AEBS-HDV was initiated by GRVA in September 2021
ToR requests an updated regulation per GRVA in February 2022
ToR asks for a dedicated report to GRVA in September 2021 with special emphasis on whether this timing can be met

## Slide 3: Current Status of IWG (accomplished, running)
IWG had 6 meetings (last meeting: September 21/22)
Main task: develop a draft regulatory proposal to revise UN Regulation No. 131
  a) Assess the accident situation for heavy duty vehicles
  b) Investigate the feasibility of a generic marker triggering AEBS
  c) Define state of the art performance requirements
  d) Review the values for the target speed reduction for M2 and N2
  e) Review AEBS on V2Car, V2Ped, V2Bicycle, others
  f) Incorporate as relevant new concepts from UN Regulation No. 152
Current activity and status: Writing draft regulation, basically finished (open issues left, see following slides) up to and including section 5 (specs)

## Slide 4: Outlook
Next meeting: October 26-28 (in total 9 hrs)
Core activities of AEBS-HDV-07
  Clarify open issues after feedback from GRVA-11
  Finish remaining sections 6 (testing), 12 (transitional provisions) and Annex 3, Appendix 2 (false reaction scenarios)
  Prepare working document for GRVA in February
Buffer:
  Meetings in Nov, Dec, Jan to prepare an informal document amending the working document
Timing goal will be achieved

## Slide 5: Agreement on Performance
Vehicle category |  |  | AEB Vehicle-Vehicle | AEB Vehicle-Pedestrian | AEB Vehicle-Bicycle
M2 N2 < 8t | derived from M1N1 | Hydraulic braking | 50 km/h (R152 as alternative) | 26 km/h (R152 as alternative) | - (no systems)
 | derived from / based on “heavies” | Hydraulic braking (inclu-ding M3) | 35 km/h | 20 km/h | - (no systems)
 |  | Pneumatic braking | 70 km/h 40 km/h (urban) | 20 km/h | - (no systems)
N2 > 8t M3 (except hydraulic braking) N3 |  |  | 70 km/h 40 km/h (urban)* | 20 km/h | - (no systems)
No differentiation Moving/Stationary
This is relative speed v0,Ego-v0,Target, up to which avoidance would be required. Mitigation speeds also required, comparable to R152
Ambition for higher values and AEB Vehicle-Bicycle will be expressed in a preamble.

## Slide 6: Open issues
Deactivation of AEBS
An agreement on the deactivation procedure is not yet reached
Specifically:
  Deactivation possible only below 10 km/h  from R152
  Request for guidance from GRVA-11
Definition of performance requirements
As in R152, performance requirements are given together with boundary requirements
Different interpretations of the text (copied from R152) possible
See next two slides for an introduction
After clarifying, the text in R152 might need to be aligned as well.

## Slide 7: Performance Req‘s (comparable to R152)
5.2.1.4. Speed reduction by braking demand
  In absence of driver’s input which would lead to interruption according to paragraph 5.3.2., the AEBS shall be able to achieve a relative impact speed that is less or equal to the maximum relative impact speed as shown in the following table:
  (a) For collisions with unobstructed and constantly travelling or stationary targets;
  (b) On flat, horizontal and dry roads affording good adhesion;
  (c) No trailer is coupled to the motor vehicle and the mass of the motor vehicle is between maximum mass and mass in running order conditions;
  (d) …
  It is recognised that the performances required in this table may not be fully achieved in other conditions than those listed above. However, the system shall not deactivate or unreasonably switch the control strategy in these other conditions. This shall be demonstrated in accordance with Annex 3 of this Regulation.
  [… Performance requirements table …]
Condition list in which the requirements have to be fulfilled
How to treat situations when conditions above are not met
Performance requirements in conditions above

## Slide 8: Problem Description
Clear:
  Not all conditions (a) – (…) are fulfilled
  Performance targets not required, but changing strategy not allowed
Unclear
  All conditions (a) – (…) are fulfilled
  An additional parameter (e.g. lane markings, lamp posts, fog, anything else) is introduced
How to deal with parameters not explicitly listed in the requirements, but obviously influencing the performance?
Request for Guidance from GRVA: What is GRVA’s interpretation?

## Slide 9: Summary
Performance requirements agreed within the group
Timing target will very likely be met; progress is good and buffer for unforeseeable difficulties is considered
Request for guidance from GRVA:
1. Deactivation of AEBS possible at speeds > 10 km/h or not?
2. Interpretation of condition list w.r.t. performance requirements and conditions