## Slide 1
Update from the Special Interest Group on UN Regulation 157
Informal document GRVA-11-32
11th GRVA, 27 Sept. – 1 Oct. 2021
Agenda item 4(d)
Submitted by the SIG R157

## Slide 2: Meetings of the group
Eight meetings held so far
Three more meetings scheduled in 2021 (Oct, Nov, Dec)
  Meeting documents can be found here
Goal: Finalize speed increase + lane change for GRVA-12 (Feb 2022)
… 7th SIG
Speed increase
GRVA/2021/31
Lane change
GRVA/2021/30
8th SIG
Speed increase
GRVA-11-33
HDV (DSSAD review)
GRVA-11-08

## Slide 3: Items addressed by SIG on UN R157
Higher Speeds
Lane Change
Clarifications
HDV (scope extension for M and N vehicle categories)

## Slide 4: Higher Speeds GRVA/2021/31 + GRVA-11-33
Group conclusions & proposed amendments:
  Following distances above 60 km/h should be in line with local traffic rules
  Provisions to ensure smooth and anticipatory driving that avoids inducing string instability
  Requirement for strategies to mitigate collisions with wrong way drivers and pedestrians (below 60km/h original requirement remain)
  Forward detection ranges along with control strategies to adapt speed if braking performance and/or detection range is impaired
  New performance model introduced for reference

## Slide 5: Higher Speeds UNR157-08-03
Open points of discussion:
  Requirement for lane change capability for systems operating above 60km/h
  Test and Audit requirements

## Slide 6: Lane change GRVA/2021/30
Open points of discussion:
  Type of lane change needed
  Parameters and requirements associated with each lane change type
  Field of view requirements
  Test and audit requirements

## Slide 7: Cross-cutting
Areas which are still to be considered:
  Changes to the HMI and driver monitoring
  DSSAD event data
  Improvements to information document and introducing interpretation document

## Slide 8: Clarifications
Points still under discussion:
  Active assistance systems after ALKS deactivation
  “Detectable collisions”

## Slide 9: HDV (scope extension) GRVA-11-08
Decision GRVA-10: “GRVA requested the secretariat to submit ECE/TRANS/WP.29/GRVA/2021/2 as amended by GRVA-10-36 to WP.29 and AC.1 for consideration and vote at their November 2021 sessions, subject to final review by GRVA at its September 2021 session.”
Cooperation between IWG EDR/DSSAD & SIG on UN-R 157 to review DSSAD part (para. 8.4.3.)
Outcome of exchange is to amend WP.29/2021/143 with GRVA-11-08
»
»

## Slide 10
Thank you for your attention.