## Slide 1
This presentation supports the draft proposal for the
new 01 series of amendments to
UN Regulation No. 149
(GRE/2021/14)
GRE IWG „Simplification of Lighting and Light-Signalling Regulations“
Reg. 149 Stage II, Step 1 – Summary
GRE
IWG
SLR
Informal document GRE-85-04
85th GRE, 26-29 October 2021
Agenda item 4 (c)

## Slide 2: Summary of the proposed changes.

## Slide 3: Improved and unified photometry for all RID functions
Introduction of revised and unified beam pattern for driving beams, passing beams, AFS, front fog lamps and cornering lamps as well as their symbols.
Introduction of new passing beam classes C (based on and aligned with AFS country light of class C) and V (for slow moving vehicles, based on and aligned with AFS town light of class V) as a replacement of the existing classes A, B and D.
Introduction of improved and simplified photometric tables for passing beams of classes C, V, E and W.
Removal of classes D and ES driving beams.
Introduction of auxiliary driving beams (class RA).
Improved and unified photometric tables for classes BS, CS and DS.
Improved photometric tables for classes A and B driving beams.
Revised photometric tables for CoP based on the new photometric tables in paragraph 5.
R149-Stage II-Step 1_Main changes

## Slide 4
Introduce the “matched pair”
Introduction of matched pairs for driving beams and passing beams with exceptions for several important measuring points
Introduction of new symbols for devices being part of a matched pair
R149-Stage II-Step 1_Main changes

## Slide 5: Technological neutrality
All provisions regarding testing with respect to light sources are moved to the new Annex 10 „Testing procedures with respect to light sources”.
Cornering lamps now are defined as road illumination devices. Test voltage is changed from 13.5V to 13.2V in order to be consistent throughout the regulation.
Introduction of a performance based alternative provision with regard to the minimum light source luminous flux for passing beams of classes C, V, AS, BS, CS and DS.
Inclusion of all light source technologies (including future ones) and combinations of them.
Alignment and improvement of the testing conditions according to the different light source technologies.
R149-Stage II-Step 1_Main changes

## Slide 6: Harmonisation and restructuring
Introduction of revised Annex 5 regarding visual aiming provisions for all road illumination devices including cornering lamps and harmonisation of the re-aim tolerances
Introduction of revised Annex 6 regarding the instrumental aiming provisions for passing beam headlamps and front fog lamps as well as the provisions on the cut-off quality
Improved wording of the text regarding module marking
New structure regarding homologation marking (aligned with R148.01 and R150.01)
Re-structuring the CoP provisions for road illumination devices by collecting them in paragraph 6
Introduction of scientific notation in order to assure that not more than 3 significant digits are shown for the required luminous intensity and luminous flux values
R149-Stage II-Step 1_Main changes

## Slide 7: Chronological overview of the proposed changes

## Slide 8
Base document | Paragraph | Content of the proposed change
SLR-28-13 | div. | proposal for improved and simplified photometry for all RID functions
SLR-28-08/Rev.1 | annexes 5 and 6 | revised annexes regarding aiming and cut-off provisions
SLR-29-02/Rev.1 | Annex 5 , Par. 4. | unified provisions for allowed re-aim of the beam patterns
SLR-29-08 | par. 3.5 and 6, annexes 2 and 3 | draft proposal for CoP provisions
SLR-31-05/Rev.1 | par. 3.5 and 6; annexes 5 and 6 | CoP provisions – restructering; aiming and cut-off provisions
SLR-32-07/Rev.2 | div. | introduction of technologically neutral requirements related to light sources, introduction of activation time for each function
R149-Stage II-Step Chronological overview

## Slide 9
Base document | Paragraph | Content of the proposed change
SLR-32-13/Rev.1 | par. 5.5 and 5.6 | photometric requirements for front fog lamps and cornering lamps
SLR-32-14 | par. 5.2 and 5.3 | proposal for passing beams
SLR-32-15 | par. 5.4 | symmetrical passing beams
SLR-32-16 | par. 5.1 | new and harmonized driving beam requirements; introduction of auxiliary driving beam
SLR-34-09 | par. 3.3.2.6.3. | module marking
SLR-35-04/Rev.1 | par. 4.5.3.2.3. and 4.5.3.2.4. | light source and beam pattern flux
SLR-35-12 | table 1 | beams and their symbols
SLR-37-08 | par. 6 | changed CoP tables based on par. 5
R149-Stage II-Step Chronological overview

## Slide 10
Base document | Paragraph | Content of the proposed change
SLR-39-11/Rev.1 | par. 4.18. Photometric tables | provisions on matched pairs (system approach for photometric measurements)
SLR-43-06/Rev.1 | all photometric tables; annexes 1 and 7 | introduction of scientific notation
SLR-46-01/Rev.1, based on SLR-45-03 (R148) | par. 4.5. and 4.6.; annex 10 | restructuring of provisions with regard to light sources
SLR-49-06 | par. 3.3. | restructuring of provisions with regard to homologation markings – alignment with R148.01 and R150.01 proposals
R149-Stage II-Step Chronological overview