## Slide 1
1
DETA-41-06e Rev.1
Based on SLR-48-15
Proposal for extension of DETA to improve the use of the
UNIQUE IDENTIFIER for UN Regulations
As introduced and accepted by WP.29 IWG on DETA
UI
270650
Informal document GRSG-122-03
(122nd GRSG, 12-15 October 2021
Agenda item 19c)

## Slide 2
Approval marking
R1 S1 2aY F1 AR
E1
148R00
3169
3170
UNIQUE IDENTIFIER / DETA Database
Legal Basis / Motivation
Device markings (depending on Regulation text)
Approval marking
Other marking
….
Marking example for lighting & light-signalling Regulations
P21W
P21/5W
PY21W
MD E4 3349
Light sources / modules used in the device
Trademark / Logo of manufacturer
Rated voltage
12V
Legal Basis: 1958 Agreement Revision 3 Schedule 5:
“… the approval markings required by UN Regulations may be replaced by a Unique Identifier (UI) preceded
by the symbol , unless specified otherwise in the UN Regulations.”
UI

## Slide 3
UI
270650
With UI currently required information becomes invisible, unless you are one of the existing user groups in DETA
R1 S1 2aY F1 AR
E1
148R00
3170
MAY BE REPLACED BY
The (traditional) Approval Marking specifies (Example R148):
The number of the type approval
The contracting party (country) who is responsible for the type approval
The Regulation Number the device was type approved to
The status of the Regulation at the time of type approval
The different functions that are included in the device
Any possible restrictions in mounting height
Any possible restrictions in mounting position
Any possible restriction to the number of devices necessary (D or Y)
IMPORTANT:
ALL these markings must be visible after the installation of the device on the vehicle
3170
E1
148R
(series) 00
R1 S1 2aY F1 AR
(2a)Y
The (new) Unique Identifier Marking specifies:
The unique number for accessing the DETA
IMPORTANT:
ALL these markings must be visible after the installation of the device on the vehicle
270650
UNIQUE IDENTIFIER / DETA Database
Motivation / Text of the Regulation (R148, R149, R150)

## Slide 4
Redefine the approval marking
R1 S1 2aY F1 AR
E1
148R00
UNIQUE IDENTIFIER / DETA Database
Motivation / Possible solutions
3169
3170
E1
3169
3170
Result: All the necessary information is available
as it is not replaced by the UI
Amend DETA
R1 S1 2aY F1 AR
E1
148R00
3169
3170
Result: All the necessary information is available
but part of DETA
UI
270650
OR
UI
270650
OR
+
+
New usergroup
Solution A
Solution B
Electronic database (DETA)
Information
Information
Information

## Slide 5
E6
R14900
F3 K PL
00 XEWR 11111 22222 33333 44444
00 XCV 55555 66666 77777
00 XCWT 88888 99999
00 XCVR 121210 112211
00 XCWR 14441 14442
00 XCWR 552200 552201
Approval marking
UI
1234567
(On any fixed part visible after installation i.e. lens)
(On any fixed part visible after installation i.e. lens)
Unique Identifier
Electronic database (DETA)
Information
Information
Information
Database
+
Marking
60+ mm
35+ mm
20 mm
9 mm
The presence of the marking in front of the optics could have an influence on the quality of the optical system
5
UNIQUE IDENTIFIER / DETA Database
Motivation / Reason for the chosen solution
1122
Example: Device used as a beam contributor for different AFS systems

## Slide 6
Part A: Document management
Create a new „Summary“ document in DETA (PDF)
showing for example, depending on GRs decisions for each Regulation:
Proposal - Make the relevant information available to those dependent on the content
Part B: Usergroup management
Create a new usergroup in DETA
UNIQUE IDENTIFIER / DETA Database
Details of the amendment to DETA
  Usergroup level: Public (e.g. law enforcement, repair shops, etc.)
  Usergroup rights: Read only the „Summary“ document
  Description
  Traditional markings / Explaining text
  If they exist, limitations to the installation and/or use
  The public has only access to the „Summary“ document stored in DETA via a separate web application.

## Slide 7
Summary
UI
270650
HEADLINE
UNIQUE IDENTIFIER as on the device
TRADITIONAL MARKING The alternative marking as in the Regulation / Explaining text for the device.
R1 S1 2aY F1 AR
E1
148R00
3169
3170
The above information, except for the alternative marking, is available somewhere in the existing documents in DETA. According to the currently proposed usergroups matrix, this information could be found by authorised experts only, but not by anyone else. The existing documents also contain a lot of information that is not for public view in any case!
EXPLAINING / ADDITIONAL TEXT
Explaining text to the symbols / markings /device if necessary.
The intention is to provide equivalent information to the existing marking
UNIQUE IDENTIFIER / DETA Database
Details of the amendment to DETA – Part A
Information text
Part A – „Summary“ document managment
Depending on GR‘s decision

## Slide 8
All decisions to be made by each GR separately for each Regulation
NO (“…unless specified otherwise in the UN Regulations…” e.g. R44, R129)
YES
NO
YES (“… may be replaced by a UI…” e.g. R148, R149, R150)
UI marking allowed by the Regulation?
Summary document necessary?
UNIQUE IDENTIFIER / DETA Database
Details of the amendment to DETA – Part A
Summary
Information
Information
Information
Summary
Information
Information
Information
Content?
YES
UI
270650
R1 S1 2aY F1 AR
E1
148R
3170
OR
R1 S1 2aY F1 AR
E1
148R
3170

## Slide 9
UNIQUE IDENTIFIER / DETA Database
Details of the amendment to DETA – Part B
Part B – Usergroup managment

## Slide 10
BACKUP

## Slide 11
UI
270650
R1 S1 2aY F1 AR
E1
148R00
0170
E1
3.3.2.1.1. „Approval mark“
0170
3.3.2.1.2. „four to six digit sequential number“
3.3.2.1.4. „Regulation Number + „R“ + Series“
148R00
R1 S1 2a F1 AR
3.3.2.1.3. „Symbols“
3.3.2.1.5. „Additional symbols“
Y
3.3.2. „Approval Marking“
3.3.3. „Unique Identifier“
E1*148R00/00*0170*00
„Approval number“ acc. to schedule 4 of the 1958 agreement
3.3.4. „Other marking“
12V
3.3.4.x. Trademark, Modulemarking, Voltage,(Substitute) light source category ….
ALTERNATIVES
P21W
UNIQUE IDENTIFIER / DETA Database
Explanation to „approval mark“ / „approval marking“ / „approval number“ ……
The explanation below is based on the text of Regulation No. 148, draft series 01