## Slide 1
OICA discussion
UN-R16 proposal by Japan ECE/TRANS/WP.29/GRSP/2021/19
Informal document GRSP-70-25
70th GRSP, 06 – 10 December 2021
Agenda item 6

## Slide 2
Summary of technical analysis
Findings by Japan show for booster seats secured by both seat belt and ISOFIX:
  The seatbelt slipped upward toward the dummy's neck by a larger amount
  The dummy’s knee position was located further forward
  The angle between the dummy's upper body and thigh was larger  submarining effect
  Neck upper tension, chest acceleration, abdominal pressure are higher
Main reason for higher loads is slack in the belt system due to double fixture by belt and ISOFIX
Increased movement between cushion part of the booster seat and child/dummy in case of booster seats fixed by ISOFIX and booster seat not following the dummy when moving forward
During IG Child Safety, 31st meeting, no safety benefit for booster seat with belt and ISOFIX was recognized, just slight higher dummy loadings

## Slide 3: Summary of OICA position
Summary
Installing booster seats with belt and ISOFIX could cause slack in the belt system which leads to increased dummy loadings
A change in UN R16 cannot guarantee that similar situation will not occur when booster seats with ISOFIX attachments are used as universal ECRS without checking them in the vehicle environment
There is no general safety benefit for booster seats with ISOFIX attachments
The problem (dummy loading, dummy movement…) is not occurring when the booster seat is installed using the vehicle safety belt
OICA proposal
Booster seats with ISOFIX attachments should be homologated (UN R129) as “specific to vehicle” and not “universal” or “i-Size”
There are no other indications to change UN R16
Alternatively: add some requirement in UN R129, to ensure ISOFIX connectors in the booster seat shall not take any load during a dynamic test on the UN R129 test bench with smallest dummy