## Slide 1
Progress report from the Special Interest Group on UN Regulation 157
Informal document GRVA-12-36
12th GRVA, 24–28 January 2022
Agenda item 4(d)
Submitted by the SIG R157

## Slide 2: Meetings of the group
Twelve meetings held
  All meeting documents of the group can be found here
Goal: Principle agreement now in 12th GRVA,
final endorsement in 13th GRVA (May 2022)
→ official adoption in 187th WP.29 (June 2022)
… 12th SIG
GRVA-12
Speed increase
GRVA/2022/4
Lane change
GRVA/2022/3
Lane change
new inf doc
Testing
new inf doc

## Slide 3: Items addressed by SIG on UN R157
Higher Speeds
Lane Change
Clarifications

## Slide 4: Recap: Higher Speeds GRVA/2022/4
Group conclusions & proposed amendments:
  Following distances above 60 km/h should be in line with local traffic rules
  Provisions to ensure smooth and anticipatory driving that avoids inducing string instability
  Requirement for strategies to mitigate collisions with wrong way drivers and pedestrians (below 60km/h original requirement remain)
  Forward detection ranges along with control strategies to adapt speed if braking performance and/or detection range is impaired
  New performance model introduced for reference

## Slide 5: Recap: Lane change GRVA/2022/3
Open points of discussion in GRVA-11:
  Type of lane change needed
  Parameters and requirements associated with each
  lane change type
  Field of view requirements
  Test and audit requirements

## Slide 6: Lane change GRVA/2022/3 + new informal document
Now covered in new informal documents:
  Type of lane change needed
  Parameters and requirements associated with each
  lane change type
  Field of view requirements
    new requirements added to cover detection range for lane change
  Test and audit requirements
    two annexes for testing: Annex 5 - track, Annex 6 – public road

## Slide 7: Clarifications new informal document
Further group accomplishments:
  New wording for detectable collisions
Further considerations within group:
  EDR requirements in UNR157 (EC&DE proposal)
separate inf. doc.

## Slide 8: Summary
Remaining open points of discussion:
  Requirement for lane change capability (in particular for MRM case) for systems operating above 60km/h
  Final adjustments of provisions for intentional lane crossing and evasive lane crossing
  Final review of testing annex (after all requirements and open points above are settled)
  If still needed (OICA/CLEPA proposal):
  Active assistance systems after ALKS deactivation

## Slide 9
Thank you for your attention.