## Slide 1: Development of 08 series of amendments to UN Regulation No. 83
GRPE 86, 30 May -2 June 2022
Submitted by the expert of The European Commission Informal document GRPE-86-07
86th GRPE, 30 May -2 June 2022
agenda item 3.(a)

## Slide 2: UNR 83 08 series - Background
UNR No. 154 introduced new test requirements which superseded some requirements previously in UNR No. 83 (07 series of amendments), including:
Type 1 WLTP test from GTR 15 replacing the UNR83 Type I NEDC test
Type 4 evaporative emissions test from GTR 19 replacing the UNR83 Type IV test
Type 5 durability test with updated requirements developed for UNR154 replacing the UNR83 Type V durability test
Updated OBD requirements developed for UNR154
Updated Conformity of Production procedures developed for UNR154

## Slide 3: UNR 83 08 series - Background
Some UNR83 tests which have not been updated, need to remain in UNR83 (08 series):
  Type II
  Type III
  Type VI
UNR83 08 needs to also include additional elements for equivalency purposes with EU type approvals:
In-Service Conformity requirements – to cover UNR154 and UNR RDE, as being updated by the EU ‘Euro 6e’ proposal
In-Use Performance Requirements (IUPR) for OBD

## Slide 4: UNR83 08 vs UNR154 and UNR RDE
UNR 154
Level 1a (Europe) – including Type 1, 4 and 5 tests, OBD
UNR 83 08 series
Shall demonstrate compliance with
Level 1A of UNR 154 and UNR RDE
Type I test
Type III test *
Type V test
Type VI test *
OBD, OBD IUPR
Level 2 most stringent – including Type 1, Type 4 and Type 5 tests, OBD
Level 1b (Japan) – including Type 1, 4 and 5 tests, OBD
+
Type II test *
Type IV test
* Update to align with ‘WLTP world’ where appropriate (e.g. allow use of UNR154 road load coefficients and test mass)
UNR RDE
RDE test
ISC – for UNR154 & UNR RDE

## Slide 5: Next Steps
Finalisation of draft text with inclusion of Euro 6e elements
Vote of Euro 6e in EU expected on 5 July 2022
Draft text submitted as informal document to GRPE after the vote
  Kindly request the approval of GRPE for the late submission
Comments to be received as early as possible and at the latest by 19 September 2022
Submission of working document for GRPE 87 by 18 October 2022

## Slide 6: Thank you
Notes: Update/add/delete parts of the copy right notice where appropriate.
More information: https://myintracomm.ec.europa.eu/corp/intellectual-property/Documents/2019_Reuse-guidelines%28CC-BY%29.pdf