## Slide 1
Transmitted by the Chair and Secretary of VIAQ
Geneva, 30 May – 2 June, 2022
Chair: Andrey KOZLOV, Russian Federation
Co-Chair: Inji PARK, The Republic of Korea
Secretary: Andreas WEHRMEIER, BMW
Status Report of the
VIAQ (Vehicle Interior Air Quality)
Informal Working Group
Informal document GRPE-86-35
86th GRPE, 30 May – 2 June 2022
Agenda item 12

## Slide 2
ToR for the Third Stage
Terms of reference and rules of procedure for the IWG on Vehicle Interior Air Quality
Informal document GRPE-81-09
Background. The group considered the inclusion in the scope of interior air pollutants from outside sources as a possible extension of the mandate at third stage. As an extension of the existing Mutual Resolution on VIAQ, this will take into account not only interior air emissions generated from interior materials and exhaust gases from the vehicle entering into the cabin but also outside air pollution sources. The list of outside air pollutions could include CO, NO, NO2, SO2, O3 volatile organic compounds (VOC), aldehydes, aromatic and aliphatic hydrocarbons, particulate number (PN) and mass (PM) and microbiological substances, e.g. allergens, fungi, bacteria and viruses. As an extension of the existing Mutual Resolution on VIAQ, this will take into account not only interior air quality but also the air cleaning efficiency of the vehicle air handling & treatment system.
Objective. This proposal expands on the issues of the vehicle interior air quality, addressing outside air pollutants entering into the vehicle cabin and the interior air cleaning efficiency, to develop a test procedure in a recommendation by including Part 4 in the Mutual Resolution No. 3.
Scope and work items. Outside air pollutants entering into the vehicle cabin and their cleaning efficiencies
(a) Collect the information and research data on relevant air pollutants and similar issues, and understand the current regulatory requirements with respect to vehicle interior air quality in different markets.
(b) Review, assess and develop new test procedures suitable for the measurement methods of air pollutants entering into the vehicle cabin and their cleaning efficiencies (including test modes, sample collection methods and analysis methods, etc.)
(c) Discuss the potential of air pollutants in the vehicle interior air with toxicologists.
(d) Develop a draft for test procedures in a recommendation.
Notes: 2

## Slide 3
VIAQ IWG Meetings since the last GRPE session
24th VIAQ IWG Meeting
  • Webex, 24th May 2022
  Half a day
Notes: 3

## Slide 4
Timeline
2020 | 2021 | 2022 | 2023 | 2024 | 2025
81
GRPE
82
83
Data collection
Analysis of existing test procedures
Tests by VIAQ IWG members
Developing of harmonized test procedure
84
86
87
88
89
90
91
92
VIAQ
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
WP.29
197
PM Draft +Gas Draft Final Draft
Stage 3. Phase 1
Stage 3. Phase 2
85
Notes: 4

## Slide 5
Information presented last meeting
Company | Presenter Name | Document Title | Document No.
Freudenberg Filtration Technologies | Ulrich Stahl | Influence of the Cabin Air Filter Age on the Pressure Loss and the Indoor Air Quality | VIAQ-24-04
UTAC/ESTACA | Nadir Hafs | The bubble: a dedicated platform for car cabin air pollution measurements | VIAQ-24-05
ACEA/CLEPA | Markus Michael, Andreas Wehrmeier | Statement of ACEA and CLEPA on CEN WS 103 draft document | VIAQ-24-06
NAMI | Andrey Kozlov | The group feedback analysis regarding to test methodology, conditions, equipment | VIAQ-24-07

## Slide 6
Discussion of working items
The purpose of this discussion was to formulate tasks for farther group activities and to develop harmonized PM measurement test method
Vehicle Category
Criteria for excluding a vehicle from tests
Test Vehicle age/millage
Meteorological Conditions
Test Conditions
Sampling Points/Sampling Lines
Background air pollution level
Cabin air filter age
PM and gas components to be Measured
Measurement Methods
Test equipment requirements
Gas Analysers Calibration
Test Modes
HVAC Modes
Test Procedure
Test Protocol
The items
Notes: 6

## Slide 7
Feedback from:
CLEPA
(EU Association of Supplier)
Korea Automobile Testing & Research Institute
CEN/WS 103*
OICA Members
UTAC/ESTACA
(Paris saclay)
CabinAir
Sweden AB
CabinAir
CLEPA
CEN
Korea
OICA
UTAC
The full text feedback tables are in the document VIAQ-23-09
*CEN/WS 103 items from the document “Real drive test method for collecting vehicle interior air quality data” // Doc. CEN/WS 103 N. 34, 2022
Notes: 7

## Slide 8
Working items
1. Vehicle Category (agreed)
Category 1-1
Notes: 8

## Slide 9
Working items
2. Criteria for excluding a vehicle from tests (agreed)
Exclusion shall be based on a positive answer to any of the criteria below:
Does the vehicle not have a full service history?
Is there a Malfunction Indication Light showing on the vehicle instrument panel?
Has the vehicle had unauthorised vehicle repairs?
Has any part of the vehicle’s heating and ventilation system replaced with non-original parts?
Through visual inspection of the vehicle, are there any damaged ventilation system relevant components?
Are there any obstructions to the vehicle air intake path?
Is the vehicle not in overall safe operating condition?
Is there any damage to the body of the vehicle, including but not limited to doors, windows and the rear?
Notes: 9

## Slide 10
Working items
3. Test Vehicle age/mileage (agreed)
Test vehicle age: more than one month
Test vehicle mileage: 3 000…15 000 km
Notes: 10

## Slide 11
Working items
4. Meteorological Conditions (agreed)
Weather condition: no rain, fog, snow or standing water on the carriageway
Relative Humidity: 40…80%
Atmospheric pressure: 85…110 kPa
Temperature: +5…+25oC
Notes: 11

## Slide 12
Working items
5. Test Conditions
The test must be primarily conducted on city roads and urban locations
Road condition: Paved streets
Windows, doors, sunroof or convertible soft top must be closed at all times. Heated or cooled seats should not be used.
The vehicle shall have been driven at least 50 km in the seven days prior to the start of the test, to ensure that the vehicle has been in regularly use prior to the test and not left unused for a long period.
When cleaning the vehicle prior to testing, only a damp cloth should be used. Fragrances and air fresheners should be avoided.
There should the driver and one passenger present in the vehicle for the duration of the test. All outer clothing of the driver should be made of polyester to minimize particle generation from the driver. Clothing should cover both arms and legs.
The occupants should avoid applying any fragrances or make-up prior to or during the test. Further, occupants should not have smoked for at least 24 hours before a test.
Notes: 12

## Slide 13
Working items
5. Test Conditions
Task: Test conditions for urban and urban motorway driving must be clearly defined
On the base of EU requirements for urban part of RDE*:
Vehicle speeds lower than or equal to 60 km/h
The average speed (including stops) of the urban driving part of the trip should be between 15 and 40 km/h
The start and the end point of a trip shall not differ in their elevation above sea level by more than 100 m
Altitude lower or equal to 700 meters above sea level
The minimum distance of operation shall be 16 km
The group decided to add to urban part of the test also urban motorway part
*Requirements regarding: Commission Regulation (EU) 2017/1151
Notes: 13

## Slide 14
Working items
6. Sampling Points/Sampling Lines
The interior sampling point should be a head-height between the front headrests
The external sampling point should be (alternatively)
2.1. As close as reasonably possible to the ventilation air intake. Sampling should be isokinetic
2.2. A forward-facing, horizontally oriented sampling probe securely mounted to minimize vehicle aerodynamic influences, at least 5 cm from the vehicle surface
3. The sampling lines to the analyzer that is designed to minimize particle losses from 10 nm to 2.5 mm. The sampling lines should be constructed of materials to minimize electrostatic particle losses (for example, conductive materials) and sized to minimize inertial and/or diffusional particle losses
Task: External sampling position must be further defined. Sampling lines maximal length and minimal diameter must be defined
Notes: 14

## Slide 15
Working items
7. Background air pollution level
PM2.5 concentration: > 15 µg/m3 (regarding 24-hour mean values of WHO Air quality guideline)
Task: The group need to set background levels to all measured components (regarding item 9)
Notes: 15

## Slide 16
Working items
8. Cabin air filter age
HVAC filter age:
New, OEM-approved
OEM-approved filter used for 3000 km
If a vehicle is not installed with a filter by the OEM, the vehicle to be tested with no filter present.
After filter was replaced with a new one the car should then be driven on the road for a minimum of 100 km before starting the test.
Task: Make a round robin test to see influence on filter age and define milage diapason
Notes: 16

## Slide 17
Working items
9. PM and gas components to be Measured
PM2.5
NO
NO2
CO2
Tasks:
1. Substantiate inclusion of PN to list of measured components taking into account modern tendences to ambient and interior air quality requirements
2. Investigate the influence of fluctuation of external concentration of CO2 in ambient air to interior concentration of CO2 (do we need to measure external CO2 simultaneously with internal)
Optionally:
PN
small fraction PM (0.1-1 µm)
PM10
CO
tVOC
PAH
NH3
O3
Notes: 17

## Slide 18
Working items
10. Measurement Methods (agreed)
PM concentration Optical particle counter
NO and NO2 concentration Non-dispersive ultra-violet
chemiluminescent detector
CO2 concentration Non-dispersive infra-red
Notes: 18

## Slide 19
Working items
11. Test equipment requirements
Task: Further check realistic values for measured concentration diapason and time resolution
PM2.5 concentration 0 to 0.5 mg/m3
NO concentration 0 to 0.5 ppm
NO2 concentration 0 to 0.5 ppm
CO2 concentration 0 to 5,000 ppm
Time resolution: <2 s
Notes: 19

## Slide 20
Working items
12. Gas Analysers Calibration (agreed)
Calibration and linearization of the equipment shall be performed according to manufacturer recommendations prior to the commencement of measurements.
After the equipment is installed in the vehicle, a dynamic calibration shall be performed. The dynamic calibration ensures that the paired instruments are measuring the same concentrations. The dynamic calibration should be run each time: before the test series; if there is a new or changes to an existing test equipment installation on a vehicle; and after the first test to ensure in correct measurement. For the purposes of this calibration test, a stainless steel Y-piece should be used to split the air from the exterior sample probe equally between the interior and exterior measurement instruments. At the end of the calibration, the Y-piece should be removed and the installation returned to the test configuration.
The dynamic calibration test should be run for at least 30 minutes and expose the vehicle to concentrations in the range defined in item 7. The Pearson correlation coefficient between the data points from each matched pair of measurement devices shall be calculated. For a valid calibration, the r2 on all devices should be at least 0.98.
The drift of the zero response of the particle number instruments, defined as the mean response to HEPA filtered air at the inlet of the sampling line during a time interval of at least 30 seconds, shall be tested prior to each test and shall be less than 3 mg/m3.
The drift of the zero response of the carbon dioxide instruments, defined as the mean response to ambient air at the inlet of the sampling line during a time interval of at least 30 seconds, shall be tested prior to each test and shall be 413 ppm ±20 ppm.
Annual calibration following supplier recommendation.
Notes: 20

## Slide 21
Working items
13. Test Modes
Real driving conditions (urban + urban motorway)
Laboratory test (see VIAQ-22-11, VIAQ-23-05, VIAQ-23-10, VIAQ-23-11, VIAQ-24-05)
Task: Investigate the necessity and validity of laboratory test inclusion to test procedure
Notes: 21

## Slide 22
Working items
14. HVAC Modes
HVAC system settings:
For Automatic mode: temperature 22˚C, if possible adjust manually: fan speed 50%/medium
For manual mode: fan speed 50%/medium, temperature 50%/medium, fresh air mode
Air conditioning switched OFF
Ventilation flaps fully open and directed straight ahead
If a vehicle has manufacturer-installed air quality sensors, these should be left in the predominant mode
Task: Investigate the influence of fan speed to measurements results and necessity to set not fan handle position, but air flow value trough HVAC (e.g. 200 m3/h)
Notes: 22

## Slide 23
Working items
15. Test Procedure
Task: To write draft test procedure and discuss in the next meetings
Notes: 23

## Slide 24
Working items
16. Test Protocol
The protocol contains
Vehicle information (type, variant, version, manufacturer, mileage, engine type, fuel type, filter type and date of installation…)
Test condition information (testing date, test locations, test time, test equipment…)
Reporting of test results (inside and outside concentrations measurement results, ventilation mode, ambient conditions, mean vehicle speed, test distance, altitude, filtering efficiency…)
Task: This item must further be updated, when test procedure will be finalized
Notes: 24

## Slide 25
List of tasks
Working Item | Tasks
5. Test Conditions | Test conditions for urban and urban motorway driving must be clearly defined
6. Sampling Points/Sampling Lines | External sampling position must be further defined. Sampling lines maximal length and minimal diameter must be defined
7. Background air pollution level | The group need to set background levels to all measured components (regarding item 9)
8. Cabin air filter age | Make a round robin test to see influence on filter age and define milage diapason
9. PM and gas components to be Measured | 1. Substantiate inclusion of PN to list of measured components taking into account modern tendences to ambient and interior air quality requirements 2. Investigate the influence of fluctuation of external concentration of CO2 in ambient air to interior concentration of CO2 (do we need to measure external CO2 simultaneously with internal)
11. Test equipment requirements | Further check realistic values for measured concentration diapason and time resolution
13. Test Modes | Investigate the necessity and validity of laboratory test inclusion to test procedure
14. HVAC Modes | Investigate the influence of fan speed to measurements results and necessity to set not fan handle position, but air flow value trough HVAC (e.g. 200 m3/h)
15. Test Procedure | To write draft test procedure and discuss in the next meetings
16. Test Protocol | This item must further be updated, when test procedure will be finalized
Notes: 25

## Slide 26
Next VIAQ IWG Meetings
25th VIAQ IWG Meeting (TBD)
  Paris, France, October, 2022
  Two days
26th VIAQ IWG Meeting (TBD)
  • Geneva, Switzerland, January, 2023
  • Half a day
Notes: 26