## Slide 1
Electromechanical Brakes and UNECE R13/R13-H
Workshop in Brussels – March 29th/30th
Presentation GRVA-EMB-02/Rev.1

## Slide 2
1. Overview of new technical concepts for Electro-Mechanical Brakes
Day 1, 10:00 – 12:00

## Slide 3
Electric transmission:
  Current regulation for the service braking only addresses electric control transmission
  The purpose of the EMB amendment is to address also electric energy transmission in the regulation
In a first step for UNECE-R13, the scope is limited to EMB on the motor vehicle; the trailer remains as today
Electro-Mechanical Brakes (EMB) Purpose and Scope

## Slide 4
Motor vehicle with EMB brakes on all axles (not mixed with Pneumatic Or Hydraulic systems)
Motor vehicle with EMB brakes with “conventional” trailer interface according to current UN R13
Trailers with EMB excluded from scope
UN R13-H not included but considered, in particular when creating new definitions
UN R13 and Electro-Mechanical Brakes (EMB) Amendment scope and motivation
Advantages and possibilities by amending Electric Energy Transmission to UN R13
Improved energy efficiency in EV´s (vs. air compressor)
Improved braking control
Elimination of noise emissions from pneumatics
Agenda item 1.(a)

## Slide 5
BEV
ICE
DC/DC
MECHANICAL
Received Energy
Supply
Type of powertrain
COMPRESSOR
ALTERNATOR
PUMP
HIGH VOLTAGE POWER
compressed air
pressurized fluid
vacuum
low voltage power
…
low voltage power
TB
ICE
Generator
Hybrid
24V
+ Governor valve
+ Air dryer
Supplied
energy
source
Conditioning
No source
Energy supply
Energy supply
1.(a)

## Slide 6
6
UN R13 and Electro-Mechanical Brakes (EMB) Energy Transmission principles (Pneumatic vs. Electric)
E-APU
Pneumatic energy
storage
EBS Modulator
Actuator
Caliper
Drive and Motor
Gears
Caliper
DC/DC
Energy reserve
Pneumatic Energy
Electric Energy
Annex 7 part A
Annex 7 new part D
Electric energy storage
Actuation
Energy supply
EBS
EMB
New 5.2.1.35.
5.2.1.27
1.(a)

## Slide 7: Motivation amending UN R13-H on Full Power Braking Systems
Full Power Braking Systems are under development as an alternative to conventional hydraulic braking systems.
Currently potential approvals to UN-R 13H/01 Suppl.4 for such Full Power Braking Systems are unclear due to missing defnitions and requirments.
1.(b)

## Slide 8: Classification Brake by Wire (BBW) versus Electro Mechanical Brake (EMB)
a mix of energy
is converted to actuating forces by purely mechanical means
electro-hydraulic braking system
(EHB)
electric-mechanic/ electro-hydraulic braking system
(EMB-EHB)
electrical power only
is converted to actuating forces by purely mechanical means
electric-mechanic braking system
(EMB)
Control and Energy Transmission
 Brake By Wire (BBW)
Energy Transmission
 EMB
Agenda item 1.(b)

## Slide 9
2. Traditional brakes and new concepts
Day 1, 13:00 – 18:00

## Slide 10: Main challenges
Keep same safety level as with current technologies
Account for new technology, while avoiding design restrictions
Keep the requirements performance-/function oriented
Avoid unwanted side-effects on existing regulation
Keep R13 and R13-H definitions and principles aligned
Example technical challenge:
  Effect of ageing and temperature on the performance of energy storage devices
Example regulatory challenge:
  Ensure energy warnings are displayed to the driver acc. to performance level

## Slide 11
Traditional brakes and new concepts
(2a) “Full” EMB for Heavy Duty Motor Vehicles
Day 1, 13:00 – 16:00

## Slide 12
System Board-net (Energy and Control transmissions)
Energy Source, Supply ,Storage and friction brake actuation
Existing typical layout (EBS)
Intermediate layout between EBS and EMB
Targeted EMB principal layouts

## Slide 13
ICE
Compressor
Brake Controller
R13 - Existing typical layout - EBS
Brake Valve
2
1
2
KL 30.1
Circuit 1
Circuit 2
Supply
Tank
Energy
Reserve 2
Energy
Reserve 1
Brake Valve
1
Battery
24V
Alternator
Energy Reserve
Transmission
Control
to be defined
Energy Supply * (including energy source, if any)
Energy Transmission I
Electric
I Pneumatic
Control Transmission I
I Pneumatic
Electric
3
2.5.1. "Control transmission" means the combination of the components of the transmission which control the operation of the brakes, including the control function and the necessary reserve(s) of energy.
Energy transmission = pneumatic
Control transmission = electric + pneumatic (backup)
Mechanical drive
“energy source of the electric control transmission” (5.2.1.27.5)
Agenda item 2.(a)

## Slide 14
Traction Battery (HV)
Electric Compressor
Brake Controller
R13 - Existing typical layout - EBS
Brake Valve
2
1
2
KL 30.1
Circuit 1
Circuit 2
Supply
Tank
Energy
Reserve 2
Energy
Reserve 1
Brake Valve
1
Battery
24V
DC/DC
Energy Reserve
Transmission
Control
to be defined
Energy Supply * (including energy source, if any)
Energy Transmission I
Electric
I Pneumatic
Control Transmission I
I Pneumatic
Electric
3
Energy transmission = pneumatic
Control transmission = electric + pneumatic (backup)
2.5.1. "Control transmission" means the combination of the components of the transmission which control the operation of the brakes, including the control function and the necessary reserve(s) of energy.
2.(a)

## Slide 15
Traction Battery (HV)
Electric Compressor
R13 - Intermediate step between EBS and EMB
Brake Controller 1
Brake Valve
2
1
2
Circuit 1
Circuit 2
Supply
Tank
Energy
Reserve 2
Energy
Reserve 1
Brake Valve
1
Battery 1
DC/DC
Energy Reserve
Transmission
Control
to be defined
Energy Supply * (including energy source, if any)
Energy Transmission I
Electric
I Pneumatic
Control Transmission I
I Pneumatic
Electric
Brake Controller 2
Battery 2
Energy transmission = pneumatic
Control transmission = electric
2.(a)

## Slide 16
Traction Battery (HV)
DC /DC
Brake Controller
1
R13 EMB Targeted layouts – layout 1a
(Electro-Mechanical-Brake)
Brake Controller
2
1
2
KL 30.1
Circuit 1
Circuit 2
Battery
24 V
Energy
Reserve 2
Energy
Reserve 1
Energy Reserve
Transmission
Control Transmission
Control
to be defined
Energy Supply * (including energy source, if any)
Energy Transmission I
Electric
I Hydraulic
Specific battery to braking
Energy transmission = electric
Control transmission = electric
2.(a)

## Slide 17
Traction Battery (HV)
DC /DC
Brake Controller
1
R13 EMB Targeted layouts – layout 1b
(Electro-Mechanical-Brake)
Brake Controller
2
1
2
KL 30.1
Circuit 1
Circuit 2
Battery 24V
Battery 24V
Energy Reserve
Transmission
Control Transmission
Control
to be defined
Energy Supply * (including energy source, if any)
Energy Transmission I
Electric
I Hydraulic
battery for braking
And other consumers
Energy Reserve 1
Energy transmission = electric
Control transmission = electric
Energy Reserve 2
2.(a)

## Slide 18
III. Performance requirements for single failure

## Slide 19: 5.2.1.2.7.2. If the service braking force and transmission depend exclusively on the use, controlled by the driver, of an energy reserve, there shall be at least two completely independent energy reserves, each provided with its own transmission likewise independent; each of them may act on the brakes of only two or more wheels so selected as to be capable of ensuring by themselves the prescribed degree of secondary braking without endangering the stability of the vehicle during braking; in addition, each of the aforesaid energy reserves shall be equipped with a warning device as defined in paragraph 5.2.1.13. below. In each service braking circuit in at least one of the air reservoirs a device for draining and exhausting is required in an adequate and easily accessible position;
UN R13 Today
Agenda item 2.(a)

## Slide 20
Traction Battery (HV)
Electric Compressor
Brake Controller
R13 - Existing typical layout - EBS
Brake Valve
2
1
2
KL 30.1
Circuit 1
Circuit 2
Supply
Tank
Energy
Reserve 2
Energy
Reserve 1
Brake Valve
1
Battery
24V
DC/DC
Energy Reserve
Transmission
Control
to be defined
Energy Supply * (including energy source, if any)
Energy Transmission I
Electric
I Pneumatic
Control Transmission I
I Pneumatic
Electric
3
Energy transmission = pneumatic
Control transmission = electric + pneumatic (backup)
2.5.1. "Control transmission" means the combination of the components of the transmission which control the operation of the brakes, including the control function and the necessary reserve(s) of energy.
Secondary performance
2.(a)

## Slide 21
Traction Battery (HV)
DC /DC
Brake Controller
1
R13 EMB Targeted layouts – layout 1a
(Electro-Mechanical-Brake)
Brake Controller
2
1
2
KL 30.1
Circuit 1
Circuit 2
Battery
24 V
Energy
Reserve 2
Energy
Reserve 1
Energy Reserve
Transmission
Control Transmission
Control
to be defined
Energy Supply * (including energy source, if any)
Energy Transmission I
Electric
I Hydraulic
Specific battery to braking
Energy transmission = electric
Control transmission = electric
Secondary performance
2.(a)

## Slide 22: 5.2.1.5. Where use is made of energy other than the muscular energy of the driver, there need not be more than one source of such energy (hydraulic pump, air compressor, etc.), but the means by which the device constituting that source is driven shall be as safe as practicable.
UN R13 Today
2.(a)

## Slide 23
Traction Battery (HV)
Electric Compressor
Brake Controller
R13 - Existing typical layout - EBS
Brake Valve
2
1
2
KL 30.1
Circuit 1
Circuit 2
Supply
Tank
Energy
Reserve 2
Energy
Reserve 1
Brake Valve
1
Battery
24V
DC/DC
Energy Reserve
Transmission
Control
to be defined
Energy Supply * (including energy source, if any)
Energy Transmission I
Electric
I Pneumatic
Control Transmission I
I Pneumatic
Electric
3
Energy transmission = pneumatic
Control transmission = electric + pneumatic (backup)
2.5.1. "Control transmission" means the combination of the components of the transmission which control the operation of the brakes, including the control function and the necessary reserve(s) of energy.
At least 8 applications before Secondary performance
2.(a)

## Slide 24
Traction Battery (HV)
DC /DC
Brake Controller
1
R13 EMB Targeted layouts – layout 1a
(Electro-Mechanical-Brake)
Brake Controller
2
1
2
KL 30.1
Circuit 1
Circuit 2
Battery
24 V
Energy
Reserve 2
Energy
Reserve 1
Energy Reserve
Transmission
Control Transmission
Control
to be defined
Energy Supply * (including energy source, if any)
Energy Transmission I
Electric
I Hydraulic
Specific battery to braking
Energy transmission = electric
Control transmission = electric
At least 8 applications before Secondary performance
2.(a)

## Slide 25: Proposed definitions
“Energy supply” means all parts, including an energy source, if any, that are necessary to supply energy for the operation of the braking system. The supplied energy can be used to be stored in the energy storage devices and/or can be used directly to feed the control transmission and/or the energy transmission.
"Energy source" means a device which receives energy and converts it into the required form (i.e. medium). An energy storage device is not considered as a source.
“Energy reserve” means the stored energy needed for the operation of the braking system.
e.g. compressor, pump, alternator…
But not the traction battery nor a DC/DC converter
e.g. DC/DC converter
2.(a)

## Slide 26
Traditional brakes and new concepts
(b) Provistion of Energy for braking systems on passenger cars (ICE and BEV)
(c) Hybrid brake system on passenger cars (e.g. hydraulic front-, electro mechanic rear axle)
Day 1, 16:30 – 18:00
Passenger Car layouts
electro-mechanical-brake
electro-hydraulic-brake
electro-mechanical-brake / electro-hydraulic-brake

## Slide 27
R13H todays layout – Full Power Braking Systems with mechanical fallback
UN R13-H, para. 5.2.2.9.
with
mechanical fall back
Circuit 1
Circuit 2
Traction Battery (HV)
LV
Battery
KL 30
Other
consumers
Steering System
Energy Reserve
Transmission
Control Transmission
Control
Not exclusively used by braking system, but total vehicle functions, e.g. Steering
Energy Supply (including energy source, if any)
Energy Transmission I
Electric
I Hydraulic
DC/DC
Brake Control Unit
hydraulic
hydraulic
hydraulic
hydraulic
Agenda item 2(b)

## Slide 28
Traction Battery (HV)
DC /DC
LV-Battery
Brake Controller
1
R13H Targeted layouts – layout 1a # (electro-mechanical-brake)
Brake Controller
2
1
2
KL 30.1
KL 30.2
Circuit 1
Circuit 2
Energy Reserve
Transmission
Control Transmission
Control
Not exclusively used by braking system, but total vehicle functions, e.g. Steering
Energy Supply (including energy source, if any)
Energy Transmission I
Electric
I Hydraulic
Other
consumers
Steering System
KL 30.1 = (+) circuit1
KL 30.2 = (+) circuit2
There can be [n] circuits (*)
(*) 5.2.8. The action of the service braking system shall be distributed between the wheels of one and the same axle symmetrically in relation to the longitudinal median plane of the vehicle.
DC/DC
2(b)

## Slide 29
hydraulic
hydraulic
R13H Targeted layouts – layout 2a # (electro-hydraulic-brake)
Brake Controller1
Brake Controller 2
hydraulic
hydraulic
Modulator 1
Modulator 2
Traction Battery (HV)
LV-Battery
1
2
KL 30.1
KL 30.2
Other
consumers
Steering System
KL 30.1 = (+) circuit1
KL 30.2 = (+) circuit2
There can be [n] circuits (*)
(*) 5.2.8. The action of the service braking system shall be distributed between the wheels of one and the same axle symmetrically in relation to the longitudinal median plane of the vehicle.
Energy Reserve
Transmission
Control Transmission
Control
Not exclusively used by braking system, but total vehicle functions, e.g. Steering
Energy Supply (including energy source, if any)
Energy Transmission I
Electric
I Hydraulic
DC /DC
DC /DC
2(b)

## Slide 30
DC /DC
DC /DC
hydraulic
R13H Targeted layouts – layout 3a#
(electro-mechanical-brake / electro-hydraulic-brake)
Brake Controller1
Brake Controller 2
hydraulic
1
2
Modulator 1
KL 30.1
KL 30.2
LV-Battery
Other
consumers
Steering System
KL 30.1 = (+) cicuit1
KL 30.2 = (+) circuit2
There can be [n] circuits (*)
(*) 5.2.8. The action of the service braking system shall be distributed between the wheels of one and the same axle symmetrically in relation to the longitudinal median plane of the vehicle.
Energy Reserve
Transmission
Control Transmission
Control
Not exclusively used by braking system, but total vehicle functions, e.g. Steering
Energy Supply (including energy source, if any)
Energy Transmission I
Electric
I Hydraulic
Traction Battery (HV)
2(c)

## Slide 31
3. Past activities
Day 2, 9:00 – 12:00
Brief review, Structure list and format of exiting documents

## Slide 32
4. UN R13 and UN R13-H
Day 2, 9:00 – 12:00
Scope of amendment and affected sections and paragraphs, see embedded document below (UN R13).

## Slide 33
New definitions:
“Certified Usable Performance (CUP)” means the maximum usable performance of an electrical energy storage device available for an electro-mechanical braking system determined at the time of type approval.
“Minimum Required Usable Performance (MRUP)” means the minimum usable performance of an electrical energy storage device available for an electro-mechanical braking system to fulfil the relevant requirements of this Regulation.
“Actual Electric Usable Performance (AEUP)” is the level of energy stored in an electrical energy storage device, as well as its available power, at a given time. It is defined as a percentage of the CUP value.
New proposal
The “usable performance” means the portion of the performance of an electrical energy storage device that is actually available to the supplied system (e.g. the system may not use the maximum theoretical performance).
Electrical Energy Storage device
Addressing the effect of ageing - example
 Still pending discussion and proposal will be updated during Q2 2023

## Slide 34
Content of the planned amendments to UN R13-H
Introduce and amend definitions for energy supply, energy source, and energy reserve. To ensure a harmonization with UN R13.
Link the demonstration of the independency among the energy reserves (electrical) to annex 8.
Additions and clarifications to requirements of electric control transmission regarding Full Power Braking Systems (i.e., para. 5.2.20).
Clarify and align the required capacity of electrical energy reserves to hydraulic energy reserves (e.g., para. 5.2.4.2., 5.2.14., annex 4).
Amend trigger conditions in case of loosing one brake circuit (reference: para. 5.2.3@ hydraulic systems: warning at a differential pressure of more than 15.5 bar)
Agenda item 4.

## Slide 35
UN R13 and UNR13-H
Day 2, 13:00 – 15:00
Approach and harmonization e.g. Energy Transmission
Ambitions: Keep R13 and R13-H definitions and principles aligned (ref. Day 1 principal layouts)

## Slide 36: Proposed definitions
“Energy supply” means all parts, including an energy source, if any, that are necessary to supply energy for the operation of the braking system. The supplied energy can be used to be stored in the energy storage devices and/or can be used directly to feed the control transmission and/or the energy transmission.
"Energy source" means a device which receives energy and converts it into the required form (i.e. medium). An energy storage device is not considered as a source.
“Energy reserve” means the stored energy needed for the operation of the braking system.
e.g. compressor, pump, alternator…
But not the traction battery nor a DC/DC converter
e.g. DC/DC converter

## Slide 37
Wrap up and next steps
Day 2, 15:30 – 16:00
Format and structure of future work - Discussion