## Slide 1: Draft UN Regulation on DCAS – Outline
Submitted by the TF on ADAS leadership
Informal document GRVA-17-12
17th GRVA, 25-29 September 2023
Provisional agenda item 6(a)

## Slide 2: I. General

## Slide 3: Background
GRVA adopted at its 9th session in February 2021 the terms of reference for the Task Force on Advanced Driver Assistance Systems (ADAS).
The Task Force (TF) focuses on Advanced Driver Assistance Systems (ADAS), and shall address the simplification of UN Regulation No. 79 and if needed, develop a new ADAS UN Regulation with a focus on ADAS systems up to of level 2 (as defined in ECE/TRANS/WP.29/1140).
The TF on ADAS agreed to start developing a new UN Regulation.

## Slide 4: What to be covered in a new UN Regulation? (ADAS-03-07, updated)
To address ADAS in general with a focus on systems combining longitudinal and lateral support on a sustained basis:
  To provide a safety net (minimum requirements) for any ADAS especially the ones can’t be approved today.
  To consider combinations of lateral and longitudinal assisted driving systems.
To introduce a comprehensive approach to Driver Control Assistance Systems (DCAS) performance/assessment:
  Performance requirements applicable to any combination of lateral and longitudinal motion control assistance (UN R R79 focused on steering system). Strong emphasis on driver engagement in vehicle operation and HMI.
  More comprehensive compliance assessment methods compared to those in UN R 79 (where specific tests are developed for each use case).
  Aligned with discussions in FRAV/VMAD on generic requirements/ assessment for ADS.
Without prejudice to possible more detailed requirements on some ADAS in other regulations such as the ones currently covered in UN R 79

## Slide 5
Continuous assistance – primarily designed to reduce the workload while driving, these systems are still beneficial for road safety (ADAS-06-10)
Key contributors to road traffic accidents:
  Speeding
  Too little distance
  driver disengagement from the driving task
  Human limitations
  Wrong judgement
The use of continuous assistance could encourage the driver to:
  Keep an appropriate distance to other road users
  Drive at the permitted speed
  React to potential hazard preventatively
  Judge situations correctly
And thereby contribute to overall road safety, provided appropriate measures are taken to ensure drivers properly monitor the system and the environment.

## Slide 6: New industry-requested ADAS use cases: a few examples (ADAS-08-04)
Main requests by the industry:
Allow operation in a larger set of operational environments
Allow more dynamic control
Allow system-initiated manoeuvring
Allow so called “hands-off” systems

## Slide 7: Safety issues (ADAS-15-04)
“L2 systems cannot become L3 systems by just further extending the ODD and performance” – Schuster (BMW), 2022 SafetyWeek
“The driver needs to be able aware of the allocation of driving task all times!” – Raisch (BMW), 2022 SafetyWeek
System should be robust “enough” that it does not bring the vehicle to safety critical situation
“Added functionality can exacerbate driver misunderstanding about system limitations” - IIHS
“Risky situations can develop if the vehicle starts to move or performs a complex maneuver before the driver is ready” - IIHS
“Unexpected system behavior takes time for a driver to react to”

## Slide 8: Identifying risks with level 2 systems
Vehicle longitudinal motion control
Vehicle lateral motion control
+
Level 2:
Level 3:
Still Level 2:
+
OEDR (partial)
ODD (specific)
DDT fallback-ready user
A driver is permanently engaged in vehicle control
There are two main risks with a level 2 system:
The system is so poor that the operator (driver) is constantly intervening to prevent catastrophic outcomes, and/or
The system is so good that the operator (driver) ceases to provide proper supervision (up to and including driver unresponsiveness).
In the first case, the system requires so much driver intervention that it impairs driver operation of the vehicle.
In the second case, the system is so reliable that the driver may not be available to intervene when needed.
The regulatory objectives should ensure that:
The system provides stable control under the use conditions for which it is designed;
The system has safeguards to guarantee that the driver is always ready to intervene;
The system enables smooth transactions with the driver with safeguards to manage problematic transactions.

## Slide 9: Agreed DCAS Key Principles
1. “Driver” refers to a human being driving a vehicle.
1.1. A DCAS does not replace the driver (ADS); a DCAS assists the driver (ADAS).
1.2. A DCAS does not change the driver’s responsibilities for control of the vehicle.
2. A DCAS is a driver-operated vehicle system.
2.1. A DCAS must prevent reasonably foreseeable risks of driver misuse or abuse.
2.2. A DCAS must have means to evaluate continuous driver involvement in and supervision of the vehicle operation.
2.3. A DCAS do not aim to permit driver activities other than driving in addition to those permitted for manual driving.
2.4. A DCAS must provide sufficient information to enable the driver to supervise its motion-control assistance.
3. A DCAS assists the driver via sustained lateral and longitudinal motion-control support.
3.1. The DCAS support must not adversely impact road safety.
3.2. The DCAS support must not adversely impact driver control over the vehicle behavior.
4. The availability of a DCAS to the driver is constrained by defined system boundaries.
4.1. The manufacturer must describe the system boundaries.

## Slide 10: II. DCAS UN R & UN R 79 Scope Separation

## Slide 11: DCAS Definition
“Driver Control Assistance System (DCAS)” means the hardware and software collectively capable of assisting a driver in controlling the longitudinal and lateral motion of the vehicle on a sustained basis.

## Slide 12
System Configuration | UN R 79 | Draft DCAS UN R
ACSF-B1 + manual longitudinal control | YES | NO (only Level 2)
ACSF-B1 + manual longitudinal control + Hands off | NO | NO (anything beyond R 79 needs to be L2)
ACSF-B1 + ACC | YES | YES (but Level 2 requirements)
ACSF-B1* + ACC * Lateral accelerations > 3m/s2 | NO | YES (but Level 2 requirements)
ACSF-B1 + ACC + Hands-off | NO | YES (but Level 2 requirements)
Fore this case, an equivalent level of safety needs to be ensured!
Applicability of UN R 79 / draft DCAS UN R for various system configurations

## Slide 13
The obvious:
L1 lane keeping and lane change systems continue to be approved to UN R 79 ACSF B1 and ACSF C, and can be used together with an ACC
Features of the draft DCAS UN R - section 6 have to be approved to DCAS UN R (because they are in conflict with UN R 79)
What about the rest of the systems:
Requirements between UN R 79 and the draft DCAS UN R applicable to lane keeping and driver initiated lane change will not be identical, because the draft DCAS UN R is deliberately drafted to cover more operating domains and apply to different types of systems.
But the draft DCAS UN R should ensure an equal level of safety compared to the provisions established in UN R 79, although potentially achieved through other means.
To achieve such an equal level, the provisions of the draft DCAS UN R shall be matched with those of UN R 79. Even, the relevant provisions of UN R 79 could be used for the draft DCAS UN R as well. The drafting is ongoing to achieve this.
General principles on the scope and separation of the draft DCAS UN R and UN R 79 (1/3)

## Slide 14
Consequences:
An ACSF that can only be operated as L2 hands-on and without any advanced features has to be approved to UN R 79 (this ensures consistency for existing systems and the driver’s experience with them);
Sustained lane keeping and driver-initiated lane change that are activated together with advanced DCAS features can be either approved to UN R DCAS, or UN R 79 if they meet the UN R 79 ACSF requirements, by the manufacturer’s declaration, to ensure a consistent safety argumentation for all parts of the system.
If the system can be configured that sustained lane keeping and driver initiated lane change can operate without any of the specific features implemented in the vehicle, this mode of operation is still covered by UN R DCAS and shall fulfill the provisions of UN R DCAS.
General principles on the scope and separation of the draft DCAS UN R and UN R 79 (2/3)

## Slide 15
The concept of scope separation
The essential concept remains to eliminate both ‘double-testing’ and incompatibilities in technical provisions, at the same time keeping UN R 79 unchanged for those parties which might only apply UN R 79. This would also help to simplify the scope of the draft DCAS UN R:
Functions approved to UN R R79 shouldn’t have to also be approved to (or meet the technical requirements of) DCAS UN R;
Functions approved to DCAS UN R shouldn’t also have to be approved to (or meet the technical requirements of) UN R 79;
Contracting Parties which do not apply DCAS UN R should still be able to require compliance with UN R 79 in-full.
Realization
The proposal for amendments to UN R 79 is presented in GRVA-17-07.
General principles on the scope and separation of the draft DCAS UN R and UN R 79 (3/3)

## Slide 16: III. DCAS UN R Construction

## Slide 17: Content of the draft DCAS UN Regulation (1/2)
Introduction | ← | Detailed explanation of the nature of DCAS and regulatory consequences
1. Scope |  | 
2. Definitions |  | 
3. Application for approval | ← | Common content with other UN Regulations
4. Approval | ← | Common content with other UN Regulations
5. Specifications |  | 
6. Requirements for Specific DCAS Features |  | 
7. Monitoring of DCAS operation | ← | Provisions for in-service monitoring and reporting (post-type approval compliance assessment pillar)
8. System Validation | ← | General provisions regarding compliance assessment with reference to annexes dedicated to system validation
9. System Information Data | ← | Provisions requesting specific data to be submitted by manufacturers in the approval process
10. Requirements for Software Identification and Cyber Security | ← | Provisions stipulating manufacturers’ actions in case of software update

## Slide 18: Content of the draft DCAS UN Regulation (2/2)
11. Modification of vehicle type and extension of approval | ← | Common content with other UN Regulations
12. Conformity of Production | ← | Common content with other UN Regulations
13. Penalties for non-conformity of production | ← | Common content with other UN Regulations
14. Production definitively discontinued | ← | Common content with other UN Regulations
15. Names and addresses of the Approval Bodies | ← | Common content with other UN Regulations
Annex 1 – Communication | ← | Common content with other UN Regulations
Annex 2 - Arrangements of approval marks | ← | Common content with other UN Regulations
Annex 3 (plus appendixes) – Audit | ← | Provisions regarding compliance assessment by means of auditing manufacturers’ documentation
Annex 4 - Physical Test Specifications for DCAS Validation | ← | Provisions regarding compliance assessment by means of track and public road testing
Annex 5 - Principles for Credibility Assessment for using Virtual Toolchain in DCAS Validation | ← | Provisions to be applied in case of using simulation in compliance assessment process

## Slide 19: Language of requirements (ADAS-23-04)
The availability of DCAS, and their capability to assist, are constrained by the defined system operational boundaries. This impact of system boundaries on the system’s ability to fulfil certain requirements, and the nature of how certain requirements can be assessed, is reflected by the language of requirements:
Some requirements are expected to always be met, including in all relevant tests. These provisions are phrased as “the system shall…”.
Some requirements are such that whilst the system is generally expected to fulfil them, either this might not be appropriate or achievable under the specific circumstances, or external disturbances may still lead to a varying output. These provisions are phrased as “the system shall aim to…”.
Some requirements are difficult to verify by assessing system performance directly and are more readily verified by assessing the design of the system, for example by analyzing its control strategies. These provisions are phrased as “the system shall be designed to…”.

## Slide 20
Feature 1 – Basis lateral & longitudinal control
DCAS
5. Specifications
6. Requirements for DCAS specific features
Feature 2 - (e.g., system-initiated lane change)
Feature 3 - (e.g., advanced driver-Initiated lane change)
Etc.
5.1. General requirements
5.2. Interaction with other assistance systems
Operation modes:
Active
Stand-by
Off
5.3. Functional requirements
DCAS to be assessed as a L2 system comprising of a number of features
5.4. System safety response to detected failures
5.5. HMI
5.6. Driver information materials
“(DCAS) Feature” means a specific DCAS capability providing assistance to the driver in defined traffic scenarios, circumstances and system boundaries.
6.2. System-initiated maneuvers
6.2.2. Lane Changes
6.2.3. Other System-Initiated Manoeuvres
6.1.2. Other advanced driver-initiated manoeuvres
6.1.1. Advanced driver-initiated lane change
6.1. Advanced driver initiated maneuvers
6.2.1. General requirements

## Slide 21: An approach to DCAS Validation (ADAS-17-03)
Due to DCAS operation in multiple domains, to ensure safe operation in all domains, for DCAS validation, “multi-pillar” techniques have been implemented, as they have been elaborated by the IWG on VMAD as the New Assessment Test Method (NATM):
  The multiple assessment techniques compensate uncertainties related to operational cases that are not assessed directly and thus cover DCAS multiple operational cases that should be assessed;
  Extensive assessment through multiple pillars allows a deep assessment of the manufacturer’s design (e.g., functional safety, controllability, driver engagement strategies) and allows for system flexibility to dynamically handle environments.
  This in turn avoids requiring the definition of specific limit values. Appropriate behavior and control is verified in test scenarios;
  In addition, the manufacturer will be required to monitor and report on system performance following entry into service;
  The enhanced assessment techniques are not new; they are already known and implemented in other areas: this would ensure easier implementation of those in the DCAS UN Regulation; We implement synergy of these techniques.

## Slide 22
1958 Agreement Compliance Assessment Chart
 | Approval |  |  |  |  |  |  | Post- Approval | 
Traditional compliance assessment | Analysis of the manufacturer’s documentation | Product identification | Physical tests/checks (may be substituted by simulation) |  |  | COP assessment |  | COP Inspection | 
NATM – multi-pillar assessment | Audit of the manufacturer’s documentation | Product identification | Scenario-based: |  |  | COP assessment |  | COP Inspection | In-service monitoring & reporting
 |  |  | Virtual tests | Track tests | Road tests |  |  |  | 
The width of the cells is not time-scaled.
The NATM elements are more comprehensive compare to those of traditional compliance assessment.
Partly performed by the manufacturer, and the results are submitted for the purpose of audit

## Slide 23: Proposed Multi-Pillar Techniques for DCAS Validation
DCAS compliance assessment
Type Approval
Post Type Approval
Audit of the manufacturer’s documentation
Physical tests
COP assessment
COP inspection
In-service monitoring and reporting
Track tests
Road tests
Simulation (optional, at the discretion of the manufacturer
Annex 3
Annex 4
Sect. 7
Sect. 8
Sect. 12
Sect. 12
Annex 5

## Slide 24: IV. Specifications (Requirements)

## Slide 25
Section 5 – 5.1. General Requirements
Driver must remain engaged (Re.: 5.5.4.2.)
Manufacturer shall implement strategies to ensure mode awareness and avoid driver overreliance (Re.: 5.5.4.)
Manufacturer shall take effective measures to guard against reasonably foreseeable misuse by the driver
Driver must be able to override or deactivate at any time (Re.: 5.5.3.4.)
Must be equipped with emergency safety systems (UN Regulation Nos. 131, 152, 179 and 130)
Section 5 – 5.2. DCAS interaction with other vehicle assistance systems
DCAS operation shall not suppress or deactivate other emergency assistance systems
Transitions between DCAS and other assistance or automation systems, prioritization, suppression and deactivation to ensure nominal and safe operation shall be described to the TAA.

## Slide 26
Section 5 – 5.3. Functional Requirements Outline
Detailed manufacturer description of detection capabilities and system boundaries of system and features, as well as other equipped systems
Assess and respond to surroundings as required to implement intended functionality
Adapt behaviour to surrounding traffic conditions by avoiding disruption of the flow of traffic
Use longitudinal and lateral motion to maintain appropriate distances from other road users
Other relevant vehicle systems may be activated (e.g. wipers, heating, indicators)
Control strategy shall aim to reduce risk of collision and ensure controllability (per 5.3.6)

## Slide 27
5.3.1. System detection capabilities to be described by the manufacturer
5.3.2. The system shall be able to assess and respond to its surroundings according to its functionality, within the system boundaries
5.3.3. The system may activate relevant vehicle systems when necessary (e.g., direction indicators)
5.3.4. The manufacturer’s control strategy shall [aim to] reduce the risk of collision and the system shall aim to ensure controllability by the driver
5.3.5. Response to system boundaries
5.3.6. Controllability
Section 5 – 5.3. Functional Requirements

## Slide 28
Section 5 – 5.3.5. Response to system boundaries
Detected boundaries when switched on
Detailed description of system boundary conditions for each system and feature (considering Annex 3 Appendix 3)
Describe behaviour and impact on system performance when beyond boundaries
Declare means of identification of system boundaries
Notify driver when system boundary is exceeded and terminate assistance in predictable and controlled way. Strategy described.
Warning when approaching of a system boundary

## Slide 29
Section 5 – 5.3.6. Controllability
System shall aim to ensure that control actions by the system including, but not limited to those resulting from failures and/or reaching system boundaries remain controllable. This must take into account the driver’s potential reaction time.
System shall implement strategies relevant to the system’s intended operational design, within defined system boundaries to be assessed by the TAA, e.g.:
  Limiting system steering output
  Adjusting position in the lane of travel
  Road type and attribute determination
  Other road user behaviour determination
  Driver monitoring used

## Slide 30
5.3.7. System dynamic control
5.3.8. Longitudinal control
5.3.7.1. Lane keeping
5.3.7.2. Lane change
5.3.7.2.1. General
5.3.7.2.2. Driver-initiated lane-change assistance
5.3.7.3. Driver unavailability response
5.3.8.1. Deceleration and acceleration
5.3.8.2. Speed limit compliance assistance
5.3.8.3. Safe headway assistance
Section 5 – 5.3. Functional Requirements (cont-d)

## Slide 31
Section 5 – 5.3.7.1. Lane keeping
Shall keep a stable position in its lane of travel within its boundary conditions. Lateral acceleration values to be specified by the manufacturer.
Only permitted higher lateral acceleration than 3.0 m/s² provided
  the system provides visual information to the driver on the upcoming driving situation/manoeuvre which may induce higher values
  System adapts vehicle speed to upcoming changes in road curvature
  System ensures driver is engaged confirming visual attention
Leaving the lane to form an access corridor for emergency and enforcement vehicles allowed
  If system only leaves its current lane of travel when this is required and allowed according to national traffic rules
  System to ensure sufficient lateral and longitudinal distance to road boundaries, vehicles and other road users
  Return completely to original lane of travel once situation requiring intervention transpired

## Slide 32
Section 5 – 5.3.7.2. Lane change
Sufficient notice to be provided to the driver. Compliance with requirements in 6.1.1 and 6.2.2 mandated.
Lane change requirements largely aligned with recent approaches in R79
Section 5 – 5.3.7.3. Driver unavailability response
When driver is determined to be unavailable following an engagement warning cascade, slow down and aim to remain in the lane of travel. Avoid deceleration demand of greater than 4.0 m/s² until coming to a stop. Hazard lights activated
Manufacturer to implement strategies to draw external attention to the emergency situation (e.g. emergency call, horn use)
Higher deceleration values are permitted for very short durations, e.g. as haptic warning
If equipped with a lane change system, aim to perform lane changes towards a slower or emergency lane if capable of doing so, accounting for surrounding traffic and road infrastructure.
Alternatively, compliance with RMF or additional response strategies can be evidenced.

## Slide 33: Driver unavailability response chart
Driver Unavailable
System capable of LC
Controlled stop in lane
LC to slower or emergency lane (if possible)
Draw attention (eCall, horn, emergency lights, etc.)
No
Yes
Alternative (e.g. RMF) or more complex strategies permissible to account for varied use cases
MINIMUM CAPABILITY

## Slide 34
Section 5 – 5.3.8.1. Deceleration and acceleration
System acceleration or deceleration shall remain controllable for surrounding traffic, unless increased levels of deceleration are required to ensure safety of the vehicle and/or surrounding road users. To be declared.
Section 5 – 5.3.8.2. Speed limit compliance assistance
Aim to detect the applicable speed limit in current lane of travel
Continuously display system-determined speed limit
Aim to follow the system-determined speed limit or driver-speed limit, whichever is lower
Control not to exceed the speed limit, provide a means to override
Any assisted deceleration should be controllable
When the driver overrides and exceeds a system-determined speed limit, provide optical warning
When override ends, system resumes control based on last system-determined speed limit or driver-set speed.
Alternatively, evidence compliance with national regulations for speed limit control systems. To be declared.

## Slide 35
Section 5 – 5.3.8.3. Safe headway assistance
System aims to make driver comply regulatorily defined headway according to national traffic rules
For M1 & N1, requirement fulfilled if either:
  A visual warning is provided upon first activation during a run cycle that the headway configuration is set to <[2]s
  Visual warning is provided when system detects that the headway to the road user ahead is too short/shorter than necessary for safe operation

## Slide 36
Section 5 – 5.4. System safety response to detected failures
Detection of electrical and non-electrical failure conditions affecting safe operation
If a failure affects safe operation of a system/feature, control assistance of given system/feature to be terminated in safe manner according to safety concept
Manufacturer to take measures to ensure failures must remain controllable for the driver
System to switch “off” if failure affects the entire system upon termination of assistance, coupled with optical and audible failure warning signal. Gradually reduce control assistance if capable of doing so and inform the driver.
If failure affects specific features, system operation is permitted to continue if remaining features are unaffected
Notice to driver when a system or feature affected by a failure is attempted to be switched “on” or “activated” by driver.

## Slide 37
5.5.1. System modes of operation
5.5.2. General requirements
5.5.3. Activation, deactivation, driver override)
5.5.4. Driver information, driver engagement and warnings to the driver
5.5.4.1. System messages and signals
5.5.4.2. Driver state monitoring and warning strategies
5.5.4.2.1. Driver disengagement monitoring
5.5.4.2.2. General requirements for driver disengagement warnings
5.5.4.2.3. Types of warnings
5.5.4.2.4. Disengagement detection and re-engagement support
5.5.4.2.5. Assessment of motoric disengagement
5.5.4.2.6. Warning escalation sequence in the event of motoric disengagement
5.5.4.2.7. Assessment of visual disengagement
5.5.4.2.8. Warning cascade in the event of visual disengagement
5.5.4.2.9. Repeated or prolonged driver disengagement
Section 5 – 5.5. HMI

## Slide 38
Section 5 – 5.5.1. Modes of operation

## Slide 39
“Off” to “On” only upon a deliberate action by the driver
“Active” only if:
  Driver’s in the seat and safety belt is fastened
  System is able to monitor driver’s engagement with the driving task
  No failure affecting the safe operation of the system has been detected
  System has not detected to be outside of system boundaries
  Other safety systems are operational
Section 5 – 5.5.3.2. System activation
System can be switched off at any time. When switched off, system to go “off”
If preconditions for activation are no longer met, the system or features shall no longer generate control output by transitioning to “stand-by” or “off”
Automatic deactivation upon a standstill following an emergency intervention.
Section 5 – 5.5.3.3. System deactivation

## Slide 40
Section 5 – 5.5.3.4. Driver override
May remain “active” when a driver overrides provided priority is given to the driver’s input
Input to the brakin control higher than system-generated deceleraton or by maintaining the vehicle in standstill, to override longitudinal control function
Accelerator input shall temporarily revert longitudinal control assistance to “stand-by” until end of override
Steering input shall override the steering action. Effort necessary shall not exceed 50 N. May allow minor lateral corrections.

## Slide 41
Inform the driver on system status, request of the driver to perform a specific action, system boundaries, detected failures, intended driver-confirmed or system-initiated manoeuvres (or sequence)
Signals to be clear, timely and noticeable. Not lead to confusion.
Use combination of visual, audio and/or haptic feedback
Messages and signals should be prioritized if offered in parallel. Safety-relevant messages and signals to be prioritized. Explained by manufacturer
Messages and signals to encourage driver understanding of intended system control outputs
System messages to be unambiguously distinguishable from messages by other assistance or automation systems equipped on the vehicle
Aim to visually communicate deactivation reason
Inform driver on availability of features, and inability to activate a given feature.
[May take into account potential impairments of users]
Section 5 – 5.5.4.1. System messages and signals

## Slide 42
System to visually inform the driver about upcoming manoeuvres [at least 3 seconds] ahead of their initiation. System to
  Inform the driver ahead of time about the sequence of manoeuvres that are upcoming
  Inform the driver of system intent at a given point in time (e.g. notice that system is changing speeds to perform a lane change)
Any notice to clear and easy to understand
Messages and signals aim to avoid driver complacency and misuse
Section 5 – 5.5.4.1.11. System messages and signals for system-initiated manoeuvres

## Slide 43
System to be equipped with the means to detect driver disengagement depending on the assistance provided, driving and environmental conditions
Monitor physical [and/or] visual disengagement using appropriate criteria
If driver detected to be disengaged, warning to be provided
Warning shall guide driver about the required actions to resume appropriate engagement
If the driver continues to be disengaged, he warning shall be escalated. Remains on as long as driver is disengaged or until system deactivation
Continued disengagement triggers unavailability response
Repeated or prolonged driver disengagement may lead to inability to reactivate the system for the start/run cycle
Section 5 – 5.5.4.2. Driver state monitoring and warning strategies (1/2)

## Slide 44
The system shall monitor driver attentiveness according to all of the following criteria:
The driver’s gaze and/or head movement is confirmed as primarily directed towards the currently driving task relevant area (e.g., road ahead, relevant mirrors or relevant direction of travel).
The driver’s distraction or drowsiness..
The driver is providing motoric input to the vehicle controls (e.g. steering control input, pedal application, control switch operation, etc ) appropriate for the current driving situation.
The driver shall be considered to be attentive if any of the above criteria are met. The manufacturer may declare additional criteria. All criteria used to assess the driver’s general attentiveness shall be evidenced and demonstrated by the manufacturer to the satisfaction of the Type Approval Authority.
Section 5 – 5.5.4.2. Driver state monitoring and warning strategies (2/2)

## Slide 45
Section 5 – 5.6. Driver information materials
Manufacturer must provide clear and easily accessible information (e.g. documentation, video, website materials) instructing the driver on DCAS operation
Materials should explain responsibility, limitations and how warnings should be interpreted
Documentation and educational materials not to describe system in a manner that would mislead customer about the capabilities/limits
Information to be legible for a non-technical audience
Example information points:
    Safety benefit of DCAS
    How DCAS exerts dynamic control assisting the driver
    System Boundaries
    Driver Engagement Detection
    HMI elements
    Etc.

## Slide 46
6.2. System-initiated maneuvers
6.2.2. Lane Changes
6.2.3. Other System-Initiated Manoeuvres
6.1.2. Other advanced driver-initiated manoeuvres
6.1.1. Advanced driver-initiated lane change
6.1. Advanced driver initiated maneuvers
6.2.1. General requirements
Section 6 – Requirements for DCAS specific features

## Slide 47
If system designed to assist lane changes on roads where there is no physical separation, system shall implement strategies to ensure that lane change procedure is only performed where there is no oncoming traffic in the target lane
Only permitted to perform lane changes on roads with pedestrians and cyclists if the system is able to reduce the risk of a collision with any vulnerable road user
Time between initiation of the lane change procedure and start of the lane change is only permitted to be extended beyond [7s] where this is not in violation of national traffic rules, and there is engagement of the driver with the ongoing lane change by looking at the relevant areas of road ahead, to the side, or looking to the vehicle’s mirrors.
Section 6 – 6.1.1. Advanced Driver-initiated lane change

## Slide 48
Relevant to manoeuvres where the vehicle selects a lane, enters into or takes a roundabout exit, leads vehicle to leave its lane of travel when this is no a lane change, leads the vehicle to take a turn, leads the vehicle to depart or arrive at a parked position, other
System and signals for system-initiated manoeuvres applies. System to ensure driver has sufficient time to confirm.
Request to be indicated through a visual and audible signal
Cannot proceed if request is not confirmed. If so, continue on lane of travel or request resumption of control
Aim to respond to vehicles, road users, infrastructure and a blocked path ahead within or to be in planned trajectory
Aim to respond to traffic lights, stop signs, right-of-way infrastructure and restricted lanes.
Aim to safely and cautiously navigate hillcrests where relevant for the manoeuvre
Aim to respond appropriately to road users and infrastructure where VRUs cross the lane of travel
Detailed activation requirements
Section 6 – 6.1.2. Other driver-initiated manoeuvres

## Slide 49
Text adjusted from ALKS
Consideration of adjusted parameters for the assessment of the target lane for a regular lane change, in consideration of different lane characteristics in e.g. urban environments. To be declared by the manufacturer
Section 6 – 6.2.2. System-initiated lane changes
Similarity to driver-initiated manoeuvres
More extensive, stringent national traffic rule compliance obligations
More extensive detect and response requirements
Any manoeuvre to be indicated to other traffic
System cannot be initiated if manoeuvre would cause other road users to unreasonable decelerate/evade
Section 6 – 6.2.3. Other system-initiated manoeuvres

## Slide 50
New obligation, in addition to CEL Audit, for manufacturer to declare in detail the system and features permitting detailed assessment/verification.
Aimed to outline system characteristics
Specific features on the system according to section 6
Conditions for activation & system boundaries
DCAS interaction with other vehicle systems
Means for activation, deactivation and override
Criteria monitored and means to determine sufficient driver engagement
Section 9 – System information data

## Slide 51
Section 10 – Requirements for software identification and cyber security
RXSWIN may be implemented, if so must comply with UN Regulation No. 156 (based on R.E.3)
System compliance with UN Regulation No. 155 to be evidenced

## Slide 52: V. DCAS Validation

## Slide 53: Assessment Pillar: Audit (Annex 3)
x
Audit
Description of DCAS functions and control strategies
DCAS layout and schematics
Safety Concept
Manufacturer’s Safety Management System
Results of physical tests performed by the manufacturer
Compliance with specific provisions of DCAS UN Regulation
Generation of scenarios for assessment
Assurance of DCAS controllability
Functional safety & Risk Assessment
SOTIF
Virtual testing (voluntary)
Results of simulation
Virtual model credibility assessment

## Slide 54: Appendices to Annex 3
Appendix 1 - Model assessment form for electronic systems, and/or complex electronic systems
Appendix 2 - System design to be assessed during the audit (list of items stipulated in the main text of the Regulation, required to be submitted by the manufacturer for the purpose of audit)
Appendix 3 - Exemplary Classification of the System Detection Capabilities and Relevant System Boundaries
Appendix 4 – Manufacturer’s declaration of system capability

## Slide 55: Appendix 4 – Manufacturer’s declaration of system capability
Aimed to outline system/feature performance to support testing.
System’s capability to respond to other road users
System’s capability to follow the course of the lane
Road events which the system may recognize relevant to the given declared system boundaries and system design
System’s ability to ensure safe operation when assisting lane changes (applicable to both driver- and system-initiated lane changes)
System’s ability to safely perform other driver-initiated or system-initiated manoeuvres in non-highway environments without driver intervention
System’s ability to operate in accordance with traffic rules related to a certain driver-initiated manoeuvre
System’s ability to operate in accordance with traffic rules related to a certain system-initiated manoeuvre

## Slide 56: Assessment Pillar: Physical testing (Annex 4)
PUBLIC ROAD TESTING
Final verification
Normal operation in real world
Representativeness
TRACK TESTING
Basic capabilities
Critical/emergency situations
Repeatability

## Slide 57: Principles of testing (ADAS-21-05)
Test all relevant requirements either through track or public road tests
Include relevant traffic, ODD related and failure scenarios
Include a variety of ODD related targets
Scenarios with possible danger -> track
Nominal behaviour -> public roads
Create a framework for the definition of pass-fail criteria

## Slide 58: Track test framework
Audit – Validation of safety and declaration of parameters – Appendix 4
Operating domains
Defined test to check the declared parameters
Extended tests to check if the system does not change strategy
Defined test to check the declared parameters
Extended tests to check if the system does not change strategy
Highway
Non-Highway
Pass-fail
Base tests
Extended tests
Response to road users
Follow the lane / path
Road events
Specific manoeuvres
Traffic rules
Different road users, speed, angle, lane marking, etc.
Refers to Appendix 4 to Annex 3 (declaration)
“Base Test” means a test scenario where the manufacturer shall declare a threshold for the missing boundary conditions (e.g. vehicle under test speed) up to which the system is able to safely control the vehicle.
“Extended Testing” means a set of test scenarios with a combination of test design variations to verify that the system does not unreasonably change the control strategy compared to the declared value and strategy in the base test, within the declared system boundaries.

## Slide 59: Requirements and system aspects to be tested
Requirements or system aspect to be assessed | Physical test scenario or audit | Reference in main text
Driver Information, Driver Engagement and Warnings to the Driver | Annex 3 , 4.1.1. | Paras. 5.1.1. and 5.5.4.
System Assurance of Driver Engagement | Annex 3 , 4.1.1. | Paras. 5.1.2. and 5.5.4.2
Reasonably foreseeable misuse | Annex 3, 4.1.1. | Para. 5.1.3.
System override | Annex 3, 4.1.1. | Paras. 5.1.4. and 5.5.3.4.
Equivalent performance of other safety systems (UN Regulations No. 131, No. 152, No. 79 and No. 130) | 4.2.5.2.1.1., 4.2.5.2.2.1., 4.2.5.2.3.1., 4.2.5.2.4.1., 4.2.5.2.8.1., 4.2.5.2.9.1., 4.2.5.2.10.1., 4.2.5.2.11.1. | Para. 5.1.5.
Functional requirements |  | Para. 5.3.
Detection Ranges for lane change | 4.2.5.2.5.1, 4.2.5.2.6.1. | Para. 5.3.2.
Vehicle behaviour in traffic (Avoid disruption of traffic flow, maintain appropriate distance from other road users, reduce risk of harm, deceleration/acceleration, traffic rules, headway distance) | 4.3.1., 4.3.2. | Paras. 5.3.4., 5.3.5., 5.3.8., 5.3.13.1, 5.3.13.2., 5.3.13.3.
Activating relevant vehicle systems | Annex 3 , 4.1.1. | Para. 5.3.6.
Detecting and Reaching DCAS boundaries | Annex 3 , 4.1.1. | Para. 5.3.10.
Controllability | Annex 3 , 4.1.1. | Para. 5.3.11.
Lane keeping | 4.2.4., 4.2.5.1.1. | Para. 5.3.12.1.
Driver-initiated lane-change assistance | 4.2.5.1.2. | Para. 5.3.12.2.
Driver unavailability response |  | Para. 5.3.12.4.
Failure response |  | Para. 5.4.
DCAS operation, driver interaction and driver information |  | Para. 5.5.
Lane Keeping (increased lateral dynamics) |  | Para. 6.1.1
Driver-initiated lane change |  | Para. 6.2.1.
Other driver-initiated manoeuvres | 4.3.3. | Para. 6.2.2.
System initiated manoeuvres | 4.3.3. | Para. 6.3.
System-initiated Lane Change | 4.2.4., 4.2.5.1.1. | Para. 6.3.2
Other system-initiated Lane Changes |  | Para. 6.3.3

## Slide 60: Assessment Pillar: In-Service Monitoring (Section 7)
x
Monitoring
Periodic Reporting to the Approval Authority
List of occurrences for in-service reporting
Manufacturer must maintain processes to monitor safety-critical occurrences resulting from DCAS operation
Manufacturer must notify Authority without undue delay of any severe accidents where DCAS was active, or active [x] seconds before accident, resulting in:
  Deployment of airbags and/or restraints
  Activation of emergency systems
Any safety-critical occurence within system boundaries which may impact the broader safe use of DCAS, must be investigated and notified to the Authority (incl. applicable remediations)
Approval Authority shall have authority to request investigation results from the manufacturer [within 6 months of the occurence or accident] subject to national rules
Occurrence | Periodic Reporting once a Year
1.a. Safety-critical occurrences known to the manufacturer | X
1.b. Aggregated distance driven with Paragraph 6 features switched on or active | X
2.a. Detection of prolonged driver disengagement, resulting in a warning escalation sequence | X
2.b. Activation of an emergency system, such as a Risk Mitigation Function, due to the continuous driver disengagement | X
3.a Detected system-level failures resulting in the unavailability of DCAS | X
3.b Detected DCAS-deactivations without prior warning to the driver | X
3.c Detected driver response to system deactivation | X

## Slide 61
Simulation may be optionally used by manufacturers to extend evidence of compliance
If simulation is used, the principles for credibility assessment for using virtual toolchain in DCAS validation shall be implemented.
Assessment Pillar: Simulation (Annex 5)

## Slide 62: Acknowledgements
The draft DCAS UN R is a result of the work of the team of experts from the Contracting Parties, industry and NGO’s. Many experts had contributed to the drafting.
Special thanks to the ADAS TF secretary – Mr. Marc Van Impe (AVERE) who carried out all paper-work of the ADAS TF.

## Slide 63: Thank you for your attention!