## Slide 1: Report from the Informal Working Group on Acceleration Control for Pedal Error (ACPE)
Informal Working Group on ACPE
Informal document GRVA-17-40
17th GRVA, 25-29 September 2023 Agenda item 6(c)
Chair and Secretary IWG ACPE – GRVA 17
Discussion items on 3rd informal meeting

## Slide 2
Informal Working Group on ACPE
Chair and Secretary IWG ACPE – GRVA 17
IWG meeting 1st meeting in web (24, 27 March 2023):
Confirmation of TOR
Accident data , existing technologies and state of the art
Discussion items
Definition of ACPE, Vehicle categories, Collision obstacle
Report: ACPE-01-10-r1
IWG meeting 2nd meeting in web (15, 16, 17 May 2023):
Confirmation of accident data
Discussion items (ACPE-02-09r2)
Definition of ACPE, Vehicle categories, Collision obstacle, Requirements,
Distance from obstacle, Velocity (e.g. below 10km/h),
AEBS interaction, Control strategies (e.g. activation, deactivation),
Trigger (e.g. after collision, after Risk Mitigation Function),
Confirmation of consistency with Vienna convention and Geneva convention
Report: ACPE-02-12

## Slide 3
3
Informal Working Group on ACPE
Chair and Secretary IWG ACPE – GRVA 17
IWG meeting 3rd meeting in BASt (19, 20, 21 September 2023):
Pedal application
Discussion for draft proposal of ACPE based on the skeleton document (ACPE-03-14)
Scope
Definitions
Specifications
Test procedure
Report: ACPE-03-15
Status: Revision by chair and secretary is ongoing.

## Slide 4
4
4
Informal Working Group on ACPE
Chair and Secretary IWG ACPE – GRVA 17
Skeleton document:
Germany proposed to prevent unintended acceleration by pedal misapplication up to 30 km/h with their accident data.
Japan proposed low speed (below 5km/h or 10km/h) based on their experience of J-NCAP.
Chair and secretary proposed a 2-step approach,
low-speed system
“high-speed” system (up to 30km/h)

## Slide 5
5
5
Informal Working Group on ACPE
Chair and Secretary IWG ACPE – GRVA 17
Pedal application
ACPE-03-04 (UK):
UK introduced their accident data (TfL), and proposed an accelerator application force as a measurement of pedal misapplication.
ACPE-03-07 and 08 (Korea):
Korea introduced their accident data (EDR). Korea supported the accelerator pedal speed as a measurement of pedal misapplication.
ACPE-03-06 (OICA/CLEPA)
OICA/CLEPA proposed M1 only (exclude the N1), and proposed to consider the requirement for the pedestrian for the 2nd step.

## Slide 6
Informal Working Group on ACPE
Chair and Secretary IWG ACPE – GRVA 17
Discussion for draft proposal of ACPE based on the skeleton document (ACPE-03-14)
Scope
1.1 This UN Regulation applies to the type approval of vehicles of Categories M1 [and N1] with regard to their Acceleration Control for Pedal Error (APCE). [Automatic transmission only]
1.2 At the request of a manufacturer, vehicles other than those mentioned in paragraph 1.1. above may be approved under this Regulation.
Definitions
“Acceleration Control for Pedal Error (ACPE)” means a system to detect misapplication of the accelerator control by the driver and control unintended acceleration.

## Slide 7
7
Informal Working Group on ACPE
Chair and Secretary IWG ACPE – GRVA 17
Specifications
5.1.1. ACPE shall be able to limit unintended acceleration of a vehicle when a pedal misapplication by driver has been detected at least when an obstacle exists in front of the vehicle when intending to go forward or when an obstacle exists behind the vehicle when intending to go backward.
5.1.2. ACPE shall control acceleration at least when the vehicle is stationary or moving off. (“Moving off” means starting from stationary and moving forward or rearward after releasing the brakes.)
5.1.3. The system shall prevent or mitigate a collision to a maximum collision speed of [5/10] km/h on a stationary obstacle of “Type A” located in a range from [1m to 1,5m / to 2m] in front or rear of the stationary ACPE vehicle.

## Slide 8
8
8
Informal Working Group on ACPE
Chair and Secretary IWG ACPE – GRVA 17
Specifications
Warnings
Interruption of Acceleration Control by driver
Avoidance of Secondary collision
Manual deactivation
Warning indication
Provisions for the Periodic Technical Inspection
Test Procedure
In the 3rd informal meeting:
Specifications included the above items in the skeleton document (ACPE-03-14). At the 3rd informal meeting, each paragraph (specifications and test procedure) was discussed, and it will be discussed again at the next meeting. For details, please refer to the report (ACPE-03-15 including the history of discussion).

## Slide 9
Chair and Secretary IWG ACPE – GRVA 17
Informal Working Group on ACPE – Next Step -
IWG meetings 4th meeting in Tokyo (Japan)
21, 22, 24 November 2023
Schedule of meetings:
Date | Meeting | Detail
17-18 January 2024 | 5th Informal meeting Web (3 hours: 8-11CET) | Discussion about requirements and test procedures
22-26 January 2024 | 18th GRVA | Report of IWG activities Submit draft regulation as informal document
27-29 February 2024 | 6th Informal meeting In-Person (Europe) | Discussion about requirements and test procedures
Early or Middle of May 2024 | 7th Informal meeting Web or In-person | Discussion about requirements and test procedures
21-24 May 2024 | 19th GRVA | Report of IWG activities Submit draft regulation as formal document
ACPE-04-03 (Furthermore information)
Please contact ACPE IWG secretariat (including Mr. Tsuburai (tsuburai@jasic.org)) by the 13th October if you plan to attend the meeting.

## Slide 10
Informal Working Group on ACPE
Thank you
for your attention
Chair and Secretary IWG ACPE – GRVA 17