## Slide 1: Type Approval of H2 Engines Extension of the ECE Regulation 49/07 to include dual-fuel hydrogen engines
M. Hygrell, F. Rost, M. Schumacher / OICA GRPE Meeting 09th - 12th January 2024
Informal document GRPE-90-18
90th GRPE, 10-12 January2024
Agenda item 4.(a)

## Slide 2
Starting from an ACEA proposal, OICA undertook an initiative at UNECE GRPE to include H2 ICE into UN Reg 49/07; GRPE adopted during the January 2023 session an amendment to include single hydrogen fuel engines in the scopes of above UN Reg.
In the next future, OICA has the plan for introducing H2 also for dual-fuel engines, as second step (the related internal discussion among members is still ongoing).
Motivation for AMENDMENT

## Slide 3
Today the dual-fuel technology already exist within ECE R49 (and EuVI) for diesel fuel combined with some carbon containing gases (e.g. CNG/LNG)
The dual-fuel engines are classified in ECE R49 after their gas substitution rates in Type 1A/B, 2A/B and 3B
Today the Type 1A is also included in the European CO2 regulation and possible to declare in the VECTO tool
It is today foreseen only to validate with a ‘Type 1’* engine. Further validation with Type 2/3 depending on request and availability of engines and vehicles possible.
Integration of diluted measurement** possible if measurement systems engines and vehicles are available for validation
The proposal is to extend the ‘lean’ update for pure hydrogen ICE (WP-29 agreed 06/2023) to Dual-Fuel ‘type1A’ hydrogen engines but adding provisions for corrected dry based emission measurements for ‘type1A’ through measurement of the water content.
SCOPE of Amendment
*max 10% energy in a WHTC from the diesel pilot fuel
**including H2O measurement by NDIR or FTIR

## Slide 4
Next steps
Adaptation of dual-fuel exhaust emission formulas as described in Annex 15, ECE R49/07 (proposal still to be defined with contribution of OICA/EC/JRC experts)
Technology verification (with support from JRC, TBC) similar to the work done for single fuel hydrogen engines. A similar set of tests have now been performed on a Dual-Fuel Hydrogen type1A prototype.
Functional verification of existing test methods regarding determination of exhaust emission
Functional verification of existing vehicle emission test methods (PEMS) seems not required, as fuel and exhaust composition is between already tested pure H2 and pure diesel.
A test package with the EuVI laboratory cycles has recently been performed including recorded EuVI ISC cycles. Evaluation of the data is ongoing.
Time frame: see next slide
Next Steps

## Slide 5
Proposed timeline for inclusion of Dual-Fuel Hydrogen engines type 1A (diesel pilot fuel) in ECE Reg49/07
Status presentation GRPE Jan-2024
Informal document GRPE May-2024
Working document GRPE October-2024
Proposed time line

## Slide 6
Thank you for your attention
Are there any questions