## Slide 1: Report of the TF on ADAS for the 18th GRVA session
Submitted by the TF on ADAS
Informal document GRVA-18-16
18th GRVA, 22-26 January 2024
Provisional agenda item 6(a)

## Slide 2
Status after the 18th GRVA session
Hybrid meeting (Brussels, 23-27 October 2023)
Four online meetings (5 October 2023, 29 November 2023, 8 December 2023, 15 January 2024)
Two online meetings of the Small Drafting Group
The draft DCAS UN Regulation is in the agenda of the 18th GRVA session
  Working document ECE/TRANS/WP.29/GRVA/2024/2 agreed by the ADAS TF at the Brussels session (Eight pairs of square brackets remained)
  Informal document GRVA-18-07 amending ECE/TRANS/WP.29/GRVA/2024/2 agreed by ADAS TF at the November and December sessions, resolving all issues with square brackets plus textual improvements. Available since mid-December
  Informal document GRVA-18-07-Rev.1 amending GRVA-18-07 incorporating textual and requirement consistency improvements agreed by ADAS TF at the January session
Corresponding draft amendments to UN Regulation No. 79 to segregate its scope and the scope of the DCAS UN Regulation in the agenda of the 18th GRVA session
  Working document ECE/TRANS/WP.29/GRVA/2024/12 submitted by D, EC, F, NL and UK
  Informal document GRVA-18-14 amending ECE/TRANS/WP.29/GRVA/2024/12 agreed by the ADAS TF at its January session
  Additional reference informal document GRVA-18-15 providing an overview of the changes to ECE/TRANS/WP.29/GRVA/2024/12
Link to the ADAS TF documents: https://wiki.unece.org/display/trans/ADAS

## Slide 3: DCAS UN Regulation Drafting Process
Stage 1
Stage 2
Stage 3
Stage 1
overview and restructuring
identify issues (redundancies, contradiction with principles, interpretation…) to be solved on the Stage 2
Stage 2
detailed review
agree on content of the requirements
Stage 3
fine tuning
finalize wording and definitions
14 GRVA
Sep. ‘22
Draft 1
16 GRVA
May ‘23
18 GRVA
Jan. ‘24
Draft 3
(final)
We are here
14 ADAS TF
30 Aug. ‘22
Draft 1 = ADAS-14-02
20 ADAS TF
15 May ‘23
Draft 2 = ADAS-20-02
Interim
ECE/TRANS/WP.29/GRVA/2024/2 + GRVA-18-07

## Slide 4: Next steps
Further development of the DCAS UN Regulation - Phase 2, to address:
  System-initiated manoeuvres (lane changes and other)
  Driver disengagement monitoring by means of assessment of visual disengagement only (realization of the “Hands-off” technology)
Background:
  FKA hands-off study
  Provisions for automated lane changes established in UN-R157 that could serve as blueprint for system initiated lane changes
  Existing multi-pillar assessment in DCAS
  Experience with the indicated features in non-UNECE markets
Workplan after the 18th GRVA session:
  Several online meetings of the ADAS TF upon availability of proposals
  Long in-person (hybrid) meeting [in Brussels] in April/May 2024
  Target to submit the working document to the 20th GRVA session in September 2024

## Slide 5: Introduction of the draft UN Regulation on DCAS
Working document ECE/TRANS/WP.29/GRVA/2024/2
Informal document GRVA-18-07
Informal document GRVA-18-07-Rev.1

## Slide 6: Specific changes introduced by GRVA-18-07 (1/2)
Agreed definitions (2.)
Series of manoeuvres can be considered as one manoeuvre (2.10.)
Specified mandatory systems on a DCAS-equipped vehicle: AEBS plus either Lane Departure Prevention System (CSF) of LDWS per UN R 131, 152, 79 (CSF) and 130 as appropriate per vehicle category (5.1.5.)
Conditions for the initiation of a manoeuvre (5.3.7.2.1.1.)
Optimizing provisions for the Speed Limit Compliance Assistance (5.3.7.4.)
“Stand-by” mode of operation is divided to “Inactive” (DCAS outside system boundaries) and “Passive” (DCAS within system boundaries) modes of operation for the purpose of ISMR (2.18, 5.5.1.)

## Slide 7: Specific changes introduced by GRVA-18-07 (2/2)
If the system is no longer permitted to provide assistance, the manufacturer shall implement strategies to ensure controllability of these phases of operation (5.5.3.4.1.5.)
The manufacturer shall implement strategies to address the detection and response to multiple subsequent short aversions of eye gaze or head posture by the driver (5.5.4.2.5.3.)
Optimized timing of driver alerts in case of his/her disengagement (5.5.4.2.6.2.3. deleted)
Conditions for navigating around an obstruction in the lane of travel (6.3.9.1., 6.3.9.3.)
Editorial amendments to improve English language

## Slide 8: Specific changes introduced by GRVA-18-07-Rev.1
Textual & requirements consistency improvements to:
  5.3.2.3.
  5.3.7.2.1.1.
  5.4.2.1.
  5.5.2.2.
  5.5.3.1.
  5.5.3.3.3.
  5.5.3.4.1.5.
  5.5.4.1.1
  5.5.4.2.3.1.2.
  5.5.4.2.5.2.

## Slide 9
DCAS
5. General Specifications (Applicable to all DCAS)
6. Additional specifications for DCAS features
Feature 1 – Lane Positioning & longitudinal control
Feature 2 - (e.g., driver-confirmed lane change)
Feature 3 - (e.g., driver-Initiated lane change)
Etc.
5.1. General requirements
5.2. DCAS interaction with other assistance systems
Operation modes:
Active
Stand-by
Off
5.3. Functional requirements
General overview of the draft DCAS UN Regulation (changes introduced in GRVA-18-07)
5.4. System safety response to detected failures
5.5. HMI
5.6. Driver information materials
6.2. Specific requirements for lane changes
6.1. Specific requirements for positioning in the lane of travel
6.3. Specific requirements for other manoeuvres
DCAS is a system comprising of a number of features

## Slide 10
5.3.1. System detection capabilities to be described by the manufacturer
5.3.2. The system shall be able to assess and respond to its surroundings according to its functionality, within the system boundaries
5.3.3. The system may activate relevant vehicle systems when necessary (e.g., direction indicators)
5.3.4. The manufacturer’s control strategy shall be designed to reduce the risk of collision whilst remaining controllable accounting for the reaction time of the driver
5.3.5. Response to system boundaries
5.3.6. Controllability
Section 5 – 5.3. Functional Requirements

## Slide 11
5.3.7. System dynamic control
5.3.8. Longitudinal control
5.3.7.1. Positioning of the vehicle in the lane of travel
5.3.7.2. Manoeuvre
5.3.7.2.1. General requirements
5.3.7.2.2. General requirements for driver-initiated manoeuvres
5.3.7.2.3. General requirements for driver-confirmed manoeuvres 5.3.7.2.4. General requirements for system-initiated manoeuvres (Reserved)
5.3.7.3. Driver Unavailability Response
5.3.7.4. Speed Limit Compliance Assistance
5.3.7.5. Safe Headway Assistance
5.3.8.1. Deceleration and acceleration
5.3.8.2. Speed limit compliance assistance
5.3.8.3. Safe headway assistance
Section 5 – 5.3. Functional Requirements (cont-d)
5.3.7. System Dynamic Control

## Slide 12
5.5.1. System modes of operation
5.5.2. General requirements
5.5.3. Activation, deactivation, driver override)
5.5.4. Driver information, driver disengagement and warnings to the driver
5.5.4.1. Driver information
5.5.4.2. Driver state monitoring and warning strategies
5.5.4.2.1. Driver disengagement monitoring
5.5.4.2.2. General requirements for driver disengagement warnings
5.5.4.2.3. Types of warnings
5.5.4.2.4. Assessment of motoric disengagement
5.5.4.2.5. Assessment of visual disengagement
5.5.4.2.6. Warning escalation sequence
5.5.4.2.7. Additional Strategies for Disengagement Detection and Re-Engagement Support
5.5.4.2.8. Repeated or prolonged driver disengagement
Section 5 – 5.5. HMI

## Slide 13
Section 5 – 5.5.1. Modes of operation

## Slide 14
6.2.1.-6.2.8. Miscellaneous requirements
6.3.1. List of manoeuvres
6.3.2.-6.3.8. Miscellaneous requirements
6.1.3. Leaving the lane to form an access corridor for emergency and enforcement vehicles
6.1.4. Lane positioning on roads without lane marking
6.1.1. Increased lateral dynamics
6.2.9. Additional requirements
Section 6 – Additional specifications for DCAS features
6.2. Specific requirements for lane changes
6.1. Specific requirements for positioning in the lane of travel
6.3. Specific requirements for other manoeuvres
6.1.2. Merging roads and slip roads on highways
6.2.9.1. Driver-confirmed lane changes
6.2.9.2. System-initiated lane changes (Reserved)
6.2.9.3. Lane changes on roads with no physical separation from moving opposite traffic
6.2.9.4. Lane changes on roads where pedestrians and/or bicycles are allowed
6.2.9.5. Lane changes in situations where the manoeuvre cannot be started within 7 seconds from the initiation of the lane-change procedure
6.3.9. Additional requirements for navigating around an obstruction in the lane of travel

## Slide 15: Two Points for GRVA Guidance
‘Powertrain’ vs ‘Engine’
  The draft DCAS UN Regulation consistently references ‘powertrain’ cycles (e.g., 5.5.3.1.), whereas other regulations refer to ‘engine’ cycles. Which term should be used for the sake of consistency in UN regulations?
Capability to perform RMF lane changes (5.3.7.3.2.)
  The draft DCAS UN Regulation stipulates that DCAS shall be equipped with RMF in compliance with the provisions of UN Regulation No. 79 (5.3.7.3.1.). According to UN Regulation No. 79, the capability of RMF to perform lane changes is at the discretion of the manufacturer
  In addition, the draft DCAS UN Regulation mandates RMF to perform lane changes (5.3.7.3.2.) if DCAS is capable of:
    Option 1: either driver-confirmed and system-initiated lane changes
    Option 2: only system-initiated lane changes
  Explanation:
    To perform lane changes automatically (the case of RMF), DCAS should have sufficient detection capabilities, which are available with the feature of system-initiated lane changes
    Manufacturers question whether the driver-confirmed lane changes feature would incorporate sufficient capabilities to safe;y perform automated lane changes in emergency situations. Thus, Option 1 creates extra burden to achieve compliance with 5.3.7.3.2.

## Slide 16: Thank you for your attention!

## Slide 17: Back-up

## Slide 18: Content of the draft DCAS UN Regulation (1/2)
Introduction | ← | Detailed explanation of the nature of DCAS and regulatory consequences
1. Scope |  | 
2. Definitions |  | 
3. Application for approval | ← | Common content with other UN Regulations
4. Approval | ← | Common content with other UN Regulations
5. General Specifications |  | 
6. Additional Specifications for DCAS Features |  | 
7. Monitoring of DCAS operation | ← | Provisions for in-service monitoring and reporting (post-type approval compliance assessment pillar)
8. System Validation | ← | General provisions regarding compliance assessment with reference to annexes dedicated to system validation
9. System Information Data | ← | Provisions requesting specific data to be submitted by manufacturers in the approval process
10. Requirements for Software Identification | ← | Provisions stipulating manufacturers’ actions in case of software update

## Slide 19: Content of the draft DCAS UN Regulation (2/2)
11. Modification of vehicle type and extension of approval | ← | Common content with other UN Regulations
12. Conformity of Production | ← | Common content with other UN Regulations
13. Penalties for non-conformity of production | ← | Common content with other UN Regulations
14. Production definitively discontinued | ← | Common content with other UN Regulations
15. Names and addresses of the Approval Bodies | ← | Common content with other UN Regulations
Annex 1 – Communication | ← | Common content with other UN Regulations
Annex 2 - Arrangements of approval marks | ← | Common content with other UN Regulations
Annex 3 (plus appendixes) – Special requirements to be applied to the audit | ← | Provisions regarding compliance assessment by means of auditing manufacturers’ documentation
Annex 4 - Physical Test Specifications for DCAS Validation | ← | Provisions regarding compliance assessment by means of track and public road testing
Annex 5 - Principles for Credibility Assessment for using Virtual Toolchain in DCAS Validation | ← | Provisions to be applied in case of using simulation in compliance assessment process

## Slide 20: Background
GRVA adopted at its 9th session in February 2021 the terms of reference for the Task Force on Advanced Driver Assistance Systems (ADAS).
The Task Force (TF) focuses on Advanced Driver Assistance Systems (ADAS), and shall address the simplification of UN Regulation No. 79 and if needed, develop a new ADAS UN Regulation with a focus on ADAS systems up to of level 2 (as defined in ECE/TRANS/WP.29/1140).
The TF on ADAS agreed to start developing a new UN Regulation

## Slide 21: Two Parallel Workstreams of the TF
Development of the provisions for the new ADAS use cases
Analysis of ADAS use cases and associated requirements
Development of the definitions, classification and scope of regulatory activities
Development of the high-level regulatory items for ADAS
New UN Regulation on longitudinal + lateral control on a sustained basis
Working on the pending proposals for UN R 79
Finding open issues hindering to adopt the proposals
Proposals on how to resolve open issues
Drafting the amended proposals to UN R 79

## Slide 22: Agreed DCAS Key Principles
1. “Driver” refers to a human being driving a vehicle.
1.1. A DCAS does not replace the driver (ADS); a DCAS assists the driver (ADAS).
1.2. A DCAS does not change the driver’s responsibilities for control of the vehicle.
2. A DCAS is a driver-operated vehicle system.
2.1. A DCAS must prevent reasonably foreseeable risks of driver misuse or abuse.
2.2. A DCAS must have means to evaluate continuous driver involvement in and supervision of the vehicle operation.
2.3. A DCAS do not aim to permit driver activities other than driving in addition to those permitted for manual driving.
2.4. A DCAS must provide sufficient information to enable the driver to supervise its motion-control assistance.
3. A DCAS assists the driver via sustained lateral and longitudinal motion-control support.
3.1. The DCAS support must not adversely impact road safety.
3.2. The DCAS support must not adversely impact driver control over the vehicle behavior.
4. The availability of a DCAS to the driver is constrained by defined system boundaries.
4.1. The manufacturer must describe the system boundaries.

## Slide 23: The Small Drafting Group (SDG)
The Small Drafting Group (SDG) was set up at the 11th ADAS TF session
  The SDG participants: RUS, D, EC-JRC, NL, UK, AVERE, OICA, CLEPA, AAPC, ETSC
The SDG:
  Continues the development of the Master Document
  Addressed separating DCAS between UN R 79 and DCAS UN Regulation
  Targeted to submit the working document for the 17th GRVA session in September 2023