## Slide 1
Electrical Braking Special Interest Group
Electrical Braking Special Interest Group
(Electrical Transmission Braking Systems)
Informal document GRVA-19-48
19th GRVA session, 25 June 2024 (For review during the Troy Meeting 20-24 May 2024)
Agenda item 8(b)
Proposals to amend Regulation 13 and Regulation 13H

## Slide 2
Electrical Braking Special Interest Group
Documents for Consideration
Regulation 13 | Regulation 13H
GRVA/2024/25 - Proposal GRVA-19-23: Amendments to the above | GRVA/2024/26 - Proposal GRVA-19-24: Amendments to the above
GRVA-19-25 Workshop Presentation: Introduction of ETBS | 

## Slide 3
Electrical Braking Special Interest Group
EBSIG´s Meetings | EBSIG´s - Virtual Meetings
EBSIG-01: 12-13 July 23, Brussels(CLEPA) | EBSIG Virtual 01 : 16 February 24 (EMS)
EBSIG-02: 24-26 August 23, Paris (OICA) | EBSIG Virtual 02 : 23 February 24 (Auxiliary Equipment)
EBSIG-03: 10-12 October 23, Brussels (CLEPA) | EBSIG Virtual 03 : 01 March 24 (Annex7, indicator)
EBSIG-04: 7-9 November 23, Paris (OICA) | EBSIG Virtual 04 : 08 March 24 (Outstanding issues)
EBSIG-05: 12-14 December 23, Paris (OICA) | EBSIG Virtual 05 : 15 March 24 (EMS)
EBSIG-06: 9-11 January 24, Berlin (VDA) | EBSIG Virtual 06 : 21 March 24 (Remaining items)
EBSIG-07: 6-8 February 24, Berlin (VDA) | 
Meetings EBSIG
All documents from the EBSIG can be found on the UN Wiki:
Electro-Mechanical Braking (EMB) - Transport - Vehicle Regulations - UNECE Wiki
The meetings followed the Terms of Reference agreed at GRVA 16.

## Slide 4
Electrical Braking Special Interest Group
Regulation 13 | Regulation 13H
Special additional requirements for electrical transmission braking systems. | 
Regulation: New Section 5.2.1.35. | Regulation: New Section 5.2.24.
Provisions relating to energy sources and energy storage devices (energy accumulators) | 
Annex 7: New Part D | Annex 4: New Part B
Special requirements to be applied to the safety aspects of complex electronic vehicle control systems | 
Annex 18 Revised Requirements | Annex 8 Revised Requirements
Principal Changes

## Slide 5
Electrical Braking Special Interest Group
General Changes
The introduction of new definitions to aid understanding and interpretations of the requirements.
Adjustment of the existing general requirements to ensure that they remain applicable to this
new technology, e.g.:
Two independent braking circuits with their own energy reserve.
Sufficient capacity of the energy reserves to ensure braking capability.
At least two circuits capable of providing secondary brake performance.
Appropriate brake performance from the specific brake controls.
Appropriate warning signals when braking performance cannot be ensured.
Brake reference values (brake demand values) for PTI.

## Slide 6
Electrical Braking Special Interest Group
Special additional requirements for electrical transmission braking systems.
The existing provisions for electrically controlled braking systems were reviewed, adapted and supplemented.
Provision of technical freedom for system architecture:
  Systems with/without an energy source.
  Systems with/without an energy supply.
  Systems using a traction battery as a supply and/or storage.
Special attention given to the security of the electrical storage devices.
Recognition of the shared use of an electrical storage device for systems/equipment other than braking
  Protection of the braking system.
Automatic braking in the event of a low energy value (low state).
New Terminology
  Electrical Storage Device ≡ Energy Reservoir Performance ≡ Capacity
  State ≡ Pressure

## Slide 7
Electrical Braking Special Interest Group
Estimator of battery states & parameters
Model of the battery
Adaption of parameters
Examples of Predictors
State of the electrical storage device
Load profiles (number of brake applications)
Signals to be measured and given as an input for the “model of the battery” ( voltage ,current, temperature)
State variables and model parameters as an input for the Predictors
Determine effect of ageing
Warnings and Indicators are continuously triggered
Indicator 5.2.1.13.2. (UN R13)
5.2.14.4. (UN R13-H)
Warning light
5.2.1.35.6 (UN R13) 5.2.24.6 (UN R13-H)
-
+
V
T
A
Voltage
Current
Temperature
Energy Management System.
Influences like low temperature, high temperature, the exchange of electrical storage device, ageing; long-time parking to be considered and covered.
Example: Lead acid battery state detection| basic principle

## Slide 8
Electrical Braking Special Interest Group
Requirements for the Energy Management System.
The energy management system must continuously assess the electrical storage devices and activate the required warning signals.
If the assessment is not complete at the beginning of a start/run cycle, a warning signal must be activated and remain active until the safe status of the system has been confirmed.
The manufacture must provide the Technical Service with a detailed overview of the energy management system, explaining its:
  architecture, and functionality.
  information about the energy management system strategy.
  a list of all the input variables.
  a sensitivity analysis showing how each of the variables affects the capability of the energy management system.
By suitable testing, and in conjunction with the requirements of Annex 18 (Annex 8 in R13H) the Technical Service must:
  verify that the energy management system accurately identifies the condition at which the warning signals are required.
  verify the accuracy of the energy management system is ensured under all operating conditions.

## Slide 9
Electrical Braking Special Interest Group
Requirements for the Electrical supply and the Electrical Storage Devices.
New requirements in Annex 7 (R.13) and Annex 4 (R.13H)
Part D.
Section 1.
Tests to ensure that the electrical storage device has sufficient performance (capacity) to provide braking after the low energy warning is given.
Test condition - when the state of the electrical storage device is equivalent to the end of useful life condition of the device.
Section 2.
Where the electrical storage devices rely on an on-vehicle supply, tests to ensure that the supply can maintain the state of the device under high usage conditions.

## Slide 10
Electrical Braking Special Interest Group
Special requirements to be applied to the safety aspects of electronic control systems
For R.13 these changes are contained in document GRVA/2023/10.
GRVA/2024/25 includes adjustments to the implementation dates.
For R.13H they are integrated into the ETBS proposal GRVA-2024-26.
The changes are based upon the latest provisions for Regulation 79.
They:
  Extend the system assessment to all electric control systems not just those that are identified as “complex”.
  They clarify the amount of system detail required from the manufacturer.
  They clarify the tasks that the Technical Service is required to undertake.
The changes have the added intention of providing greater alignment across the appropriate regulations with the
objective of avoiding regulation specific documentation.

## Slide 11
Electrical Braking Special Interest Group
Amendments to GRVA/2024/25 (Regulation 13): GRVA-19-23
The 11 amendments can be split into 3 groups:
1 – Editorial/Clarification (7)
Paragraphs: 2.44., 2.5.3., 5.2.1.13.1., 5.2.1.13.1.2., 5.2.1.35., 5.2.1.35.17.2.,
and Annex 13, Appendix 2, Para. 1.1.3.
2 – Performance Related (3)
Paragraphs: 5.2.1.35.1., 5.2.1.35.11., and 5.2.1.35.13.
3 – PTI (1)
Paragraph 5.1.4.6.2.1.

## Slide 12
Electrical Braking Special Interest Group
Performance –
5.2.1.35.1. Ensures that secondary braking performance is available before the parking brake can be released.
5.2.1.35.11. Ensures that a red warning signal is activated if at any time there are not at least two independent
      circuits each able to provide secondary braking performance.
5.2.1.35.13. Ensures that, in the event of a failure in a braking circuit, secondary braking performance can still be
      achieved. As is the case today, this may be by use of the service brake control or by a separate control.
PTI –
5.2.1.35.13. The existing requirements for brake reference values were adapted to ensure that an ETBS braking system could provide a brake input value that was equivalent to measuring the pressure in an actuator of a compressed-air braking system.
The amendment goes further than the current requirements for compressed-air braking systems. It requires that the manufacturer displays the brake input values (brake demand values) so that they can be read from the driving position.
GRVA/2024/25 - Significant Amendments (4)

## Slide 13
Electrical Braking Special Interest Group
Amendments to GRVA/2024/26 (Regulation 13H): GRVA-19-24
The 8 amendments can be split into 3 groups:
1 – Editorial/Clarification (6)
Paragraphs: 2.26., 2.34., 5.2.14.1., 5.2.14.1.2., Renumbering paragraphs (5.2.24.16., 5.2.1.24.17., and 5.2.1.24.17.1.)
and Annex 6, Appendix 2, Para. 1.1.3.
2 – Performance Related (1)
Paragraphs: 5.2.4.4.1.
3 – PTI (1)
Paragraph 5.1.4.4.1.1.

## Slide 14
Electrical Braking Special Interest Group
Performance –
5.2.4.4.1. This paragraph mirrors paragraph 5.2.1.5.4.1. for Regulation 13. However, passenger cars must ensure secondary braking using the service brake control and therefore the option provided for a separate control is not valid in Regulation 13H.
PTI –
5.1.4.4.1.1. As for Regulation 13.
The existing requirements for brake reference values were adapted to ensure that an ETBS braking system could provide a brake input value that was equivalent to measuring the pressure in an actuator of a compressed-air braking system.
The amendment goes further than the current requirements for compressed-air braking systems. It requires that the manufacturer displays the brake input values (brake demand values) so that they can be read from the driving position.
GRVA/2024/26 - Significant Amendments (2)

## Slide 15
Electrical Braking Special Interest Group
THANK YOU