## Slide 1
Hybrid GRPE workshop on the global harmonization of Heavy Duty fuel economy, energy consumption and range determination Session 1 : Latest iterations of HDV Fuel Economy standards - Global overview of Heavy Duty Fuel Economy standards - Yoshihide Takenaka OICA HD-FE TF

## Slide 2: Background
OICA has requested the GRPE to promote harmonization of fuel efficiency regulations for heavy vehicles and has organized two workshops at the GRPE. Due to the interruption of activities caused by the Covid and other events, the GRPE has yet to initiate the development of harmonized fuel efficiency regulations for heavy vehicles. At last year's GRPE meeting, there was a request to resume this activity, and a workshop with government officials is scheduled to be held at GRPE in May to discuss the promotion of standards harmonization. Therefore, it is necessary to organize the current situation and compile requests as stakeholders for the workshop to be held in May.
Expert Meeting on 26th March
OICA organized the expert meeting to share the information and discuss about how to proceed the harmonization for HD fuel efficiency. Based on the discussion at this expert meeting, Workshop for HD fuel efficiency is prepared.

## Slide 3: Expert Meeting on 26th March
Background
As announced during January GRPE session, OICA organized on 26 March the first meeting of the so called «Ad Hoc Experts Group» to discuss the FE harmonization topic.
Several delegations attended the meeting, among others the EU Commission, DG Clima, Japanese Government, GRPE Chair and Secretariat, etc.
OICA made a presentation related to some key aspects:
  Purpose, background
  Status of fuel economy regulations
  Recent update
    in Japan
    in Europe
    in US
    in China
    Schedule of different areas

## Slide 4: Expert Meeting on 26th March
Discussion at the Ad Hoc Experts Group of 23 March
DG Clima (EU Commission) expects from OICA concrete proposals on the possibility of harmonization could be and where it will be difficult to harmonize; they asked to Industry to have already some ideas of harmonization during the workshop to avoid starting from the beginning.
Target should be to select the parts of the legislations that could be harmonized, as there are a lot of differences all over the world, and it is needed to define what is the goal that we can realistically achieve.
GRPE Secretariat briefly explained what the GRPE top table has in mind for the workshop:
  An overview on FE harmonization worldwide: update since the last workshop in 2019-2020.
  Possible inclusion of other GRs (like GRBP with Tyre rolling resistance)
  Discussion of options to implement the proposals, i.e. 1958A / 1998A / Mutual Resolutions...
GRPE Chairmen confirmed the need to have a clear picture on what we stand since 2019-2020, and see what’s the goal after the workshop, e.g.:
  start with some harmonization process
  possible creation of an IWG
  define the first steps of measurement
  define the scope, activities, how to implement it (a Resolution? a UN GTR? UN regulation?
  to go step by step for harmonization.

## Slide 5: HD FE regulatory schedule in each area
Year | '13 | '14 | '15 | '16 | '17 | '18 | '19 | '20 | '21 | '22 | '23 | '24 | '25 | '26 | '27 | '28 | '29 | '30
JPN |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
US |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EU |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CHNA |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
India |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
GHG Phase I
2nd Stage of constant speed test
2015 HD FE standard
FE Phase I
Labeling of FE value
2025 HD FE standard
2025 target
1st stage
2nd stage
Phase 1 (EuroIV)
Phase 2 (BSIV)
3rd stage
Phase II
Phase1 (EuroVI)
Phase1 (BSVI)
4th stage
2030
Under consideration
Legislation
Possibility of Rule making

## Slide 6: Elements FE regulation including measurement method
Elements | Sub-Elements | Issues | Examples
FE Unit | - | Transport efficiency or Easily understand able unit | - km/L - ton.km/L
Others | Criteria | Limit of FE value or average value | - Averaged by number of sales (CAFE)
Vehicle classification | - | Simpler category is desired, but needs to reflect to real world complexity | - Vehicle type (Tractor, bus....etc) - GVW, type of cabin
Items of FE effect | - | Accuracy vs. cost of measurement Contribution for FE | - Engine, T/M - Aero dynamic and rolling resistance
Driving Mode | - | Vehicle speed base or road data base less complexity vs real world reflection | - Combination of two cycles - Unique mode for each vehicle type
Measurement Method | Chassis dynamometer | Chassis dynamometer measurement requires real vehicle | 
 | Simulation | Driver model is required for simulation | - Common calculation logic - Difference of steady and transient
 | Engine measurement | Number of measurement points Transient operation effect | - CO2 measurement by engine - Engine FE map and simulation
 | Aero dynamic measurement | Measurement methods Selection of vehicle type, rear body | - Coast down, steady speed drive - CFD - Wind tunnel
 | Tyre rolling resistance | Measurement method, labeling | - Common tyre measurement method - How to handle a number of axes
 | Others | Measurement method | - Driveline drag, Auxiliary drag, etc.

## Slide 7: FE Elements in each Area
Item |  | Sub-item | Status of each region |  |  | 
 |  |  | EU | US (PHASE II) | China | Japan (Next FES)
Categorize |  |  | Vehicle type, Axles, Configurations, Weight | Weight Cab type | Vehicle type Weight | Vehicle type Weight
FE Unit |  |  | CO2 g/ton-km g/passenger-km | gal/1000ton-mile CO2 g/ton-mile | L/100km | km/L
FE Criteria |  |  | Targets in force since 2019 (revised in 2024) for 2030, 2035, 2040 | Becomes strict every 3 years | Becoming strict in 2019 | FES value around 2025 is decided this year
Mode |  |  | 10type | ARB tangents 55,65 mph | C-WHVC | JE05, Inter city
Measurement method | Engine | Steady state Engine Map | 100 points | 70points for 55,65 mph | 81 points | 51 points
 |  | Transient Engine Map | NA | Cycle average map | NA (Include chassis dyno) | NA
 |  | Transient coefficient | WHTC correction factor tool | Include Cycle average map | NA (Include chassis dyno) | Table value 3%
 | Powertrain | FE map with powertrain | For Hybrid, AT, AMT by simulation | For Hybrid, AT, AMT by powertrain test | NA | For Hybrid and AMT by simulation
 | Gear | T/M efficiency | Table value or Measurement | Table value or Measurement | NA (Include chassis dyno) | Table value
 |  | AT parts efficiency | Table value or Measurement | Include powertrain test method | NA (Include chassis dyno) | Table value or Measurement
 |  | Axle efficiency | Table value or Measurement | Table value or Measurement | NA (Include chassis dyno) | Table value
 | Aero Drag | Aero Drag measurement | Constant speed Simulation | Coast down Wind tunnel CFD | Table value (Opt. Wind tunnel or coast down) | Coast down or Constant speed
 |  | Vehicle select method | Family Concept | ? | ? | Family Concept
 | Tire | Resistance measurement | (EC) 1222/2009 = ISO28580 | ISO 28580 | Table value | Ranking by ISO 28580
 |  | Resistance select Method | Direct input of tire RRC for each vehicle | Direct input of tire RRC for each vehicle | - | Averaging tire RRC to be used
 | auxiliary parts |  | Generic or OEM-specific | ? | NA | Only installed when measuring engine
Determine FE value | Simulation | Input data & Logic | Input data and driver model is different based on item above |  |  | 
 | Chassis dyno |  | NA | NA | Must family-representative vehicle | NA

## Slide 8: Summary
The elements that make up the fuel economy regulations of each country can be categorized into common items.
These elements can be divided mainly into those related to market and government policies and those related to technical approaches.
Due to the characteristics of heavy-duty vehicles, most regions have adopted a method of measuring devices that affect fuel efficiency and calculating fuel efficiency values by simulation or other means, rather than using the vehicle itself.
In many regions, engine fuel consumption maps, vehicle aerodynamic drag measurements, and tire rolling resistance measurements are used to measure devices that have a large impact on fuel efficiency.

## Slide 9
Thank You for the attention!