## Slide 1: Status of UN GTR No. 21 Determination of Electrified Vehicle Power (DEVP)
GRPE Power Determination Workshop
23 May 2024
Presented by Mike Safoutin – US EPA

## Slide 2: UN GTR No. 21 on Determination of Electrified Vehicle Power (DEVP)
Brief History
  Developed by IWG on on Electric Vehicles and the Environment (EVE IWG)
  Initial motivation: to support classification and downscaling under WLTP
    WLTP determines vehicle classification and cycle downscaling based on engine power rating
    However, it does not specify a method for determining an equivalent system power rating for electrified vehicles that have more than one source of propulsion, such as an internal combustion engine and one or more electric motors
  Under its mandate, in 2015 the EVE IWG formed a subgroup to investigate options for developing a test procedure for this purpose, applicable to UNECE class M1 and N1 light duty HEVs and pure electric vehicles (PEVs) with more than one propulsion motor
  EVE also considered other uses for a maximum power rating, such as consumer information
  ISO 20762 was under development at the time and provided an initial template
  Modifications were necessary to align with WLTP requirements and the needs of a regulatory application
  EVE members conducted a vehicle testing program to develop and validate the emerging GTR procedure

## Slide 3: UN GTR No. 21 on Determination of Electrified Vehicle Power (DEVP)
Phase 1 (original GTR)
  Proposal: ECE/TRANS/WP.29/2020/125
  Technical report: ECE/TRANS/WP.29/2020/126
  Approved by WP. 29 in the November 2020 session
  Established in the Global Registry as GTR No. 21 on January 18, 2021
After Phase 1, the EVE IWG continued work under its mandate to consider further development of the GTR (Phase 2)
A number of potential revisions were proposed by EVE IWG members during 2022 and 2023 and discussed at regular meetings of the EVE
The IWG reached consensus on a number of revisions to the GTR

## Slide 4: UN GTR No. 21 on Determination of Electrified Vehicle Power (DEVP)
Phase 2 topics included:
  Considered use of CAN signals in place of direct measurement
    Data analysis conducted
  Considered more appropriate accuracy requirements
    Reviewed technical necessity of requirements that posed a burden with little benefit
  Considered offering measurement alternatives for highly integrated systems
    Considered the use of vehicle CAN signals in lieu of instrumented values where power branches cannot be instrumented
  Considered need for a family concept to reduce testing burden
  Considered alternative for system bench testing in place of dynamometer testing
  Continued considering need for Candidate Method
  Continued considering need for power determination of heavy-duty and fuel-cell vehicles

## Slide 5: UN GTR No. 21 on Determination of Electrified Vehicle Power (DEVP)
Phase 2 revisions to GTR-21:
  Family concept added (Section 7)
  Additional TP1 method 6.1.3.1.2 (d) to accommodate highly integrated powertrain
    Uses a power distribution ratio between two powertrain branches based on CAN signal
  Use of a system bench is allowed in the case of vehicles that are too powerful to be tested on a chassis dynamometer (3.6 and 6.1)
  Revisions to accuracy requirements
    Soak area temperature revised to specify a tolerance around a set point and to accommodate Type 1 soak area target temperature (5.1.4)
    Engine speed, fuel flow rate, atmospheric pressure allowed from onboard signal (5.2.1/6.1.2)
    Accuracy of intake manifold pressure, dynamometer speed, time, accelerator pedal (5.2.1)
    TP1 calculation revised to 5% tolerance for fuel flow rate and manifold pressure to align with COP requirement (6.9.2.1)
Phase 2 revisions approved by GRPE in January 2024
June 2024: To be submitted as a working document for consideration by AC.3.

## Slide 6: EVE Terms of Reference – GTR No. 21
Topics of consideration for Phase 3
  Consider the scope and application of system bench testing.
  Consider the need for power determination of electrified heavy-duty vehicles.
  Consider measurement alternatives for highly integrated systems.
  Consider a candidate method.
  Consider fuel-cell electric vehicles.
  Future amendments as new data and continued research, analysis and testing lead to new developments
January 2026 (tentative): Submission of Phase 3 amendments as a working document for consideration by GRPE