## Slide 1: Status report to 80th GRBP (September 2024)
Task Force on Tyre Abrasion
On behalf of GRBP and GRPE
Transmitted by the co-chairs of TF for Tyre Abrasion
Informal document GRBP-80-22
(80th GRBP, September 17-20, 2024, agenda item 6 (e))

## Slide 2: Task Force on Tyre Abrasion
Targets | Develop a robust procedure for measuring the abrasion of tyres: Test conditions and methods; Define the acceptable uncertainty for the tyre abrasion test method(s) and assess the uncertainty of the tyre abrasion test method; Based on the abrasion test method, define a characterisation of relative mileage potential index; Evaluate the abrasion performance and tread depth reduction of a wide range of tyres available in the market; Define abrasion limits for tyres in order to limit the emission of microplastics to the environment; Develop a proposal of amendment to UN Regulation No 117 for the type approval of tyres in respect to their abrasion.
Roles | Co-chairs: United Kingdom (David.Miles@dft.gov.uk) and European Commission (Theodoros.GRIGORATOS@ec.europa.eu) Secretariat: ETRTO (European Tyre and Rim Technical Organisation)
Reporting | To both working parties: GRPE and GRBP Adoption: GRBP
Web page | Task Force on Tyre Abrasion (TF TA) - Transport - Vehicle Regulations - UNECE Wiki ToRs: TF TA Terms of Reference

## Slide 3: Task Force on Tyre Abrasion: facts and figures
  22nd online meeting: 12th March 2024 - https://wiki.unece.org/display/trans/TFTA+session+22
  23rd online meeting: 25th April 2024 - https://wiki.unece.org/display/trans/TF+TA+session+23
  24th online meeting: 29th May 2024 - https://wiki.unece.org/display/trans/TF+TA+session+24
  25th online meeting: 28th June 2024 - https://wiki.unece.org/display/trans/TF+TA+session+25
  26th online meeting: 6th September 2024 - https://wiki.unece.org/display/trans/TF+TA+session+26
  CPs: European Commission, France, China, Germany, India, Japan, Norway, Netherlands, South Korea, Spain, Switzerland, UK, USA, Canada
  NGOs: ADAC, AVL, ETRMA, ETRTO, HORIBA, IDIADA, ITMA, JAMA, JATMA, LINK, OICA, SMMT, TRAC, TÜV Nord, UniBW., USTMA, UTAC, VTI
Meetings
Attendees ~80

## Slide 4: Task Force on Tyre Abrasion: work progress
Work on the 2023 test campaign | Validation and correlation test campaign for C1 tyres: Tyres selections (candidate and “reference” tyres) for correlation: done  Tyres selections for alignment: done  Validation test campaign on 3 on-road test centres and 4 drum test centres: done  Alignment test campaign on 7 on-road test centres and 4 drum test centres: done  Post-processing: done  (for the correlation)
Working document | Test conditions and methods for C1 tyres: adopted  GRBP/2024/10 as amended by GRBP-79-12rev2 new supplement to UNR117.04  Adopted at WP.29 during its 193rd session in June 2024 ECE/TRANS/WP.29/2024/65 
Market assessment for 2024 | For C1: conduct an extensive market assessment test campaign to inform abrasion limit development – ongoing 

## Slide 5: Summary of the market assessment (indoor and on-road)
Tyres from across ETRTO, JATMA and ITMA members.
Tyre selection includes wide range of tyre sizes and wet grip and rolling resistance performances.
Market assessment testing to complete in December for on road method and March for drum method.
JRC carries out independent abrasion tests with few more tyres (6 3PMSF + 6 Normal).
 |  | On road | Drum
Number of tyre models | 3PMSF | 67 | 31
 | Normal | 110 | 69
 | Total | 177 | 100
Number tested so far | 3PMSF | 64 | 19
 | Normal | 32 | 27
 | Total | 96 | 46
Completion Rate | 3PMSF | 96% | 61%
 | Normal | 29% | 39%
 | Total | 54% | 46%
Measurement outputs include among others: i. Abrasion rate, ii. Abrasion index relative to SRTT, iii. Tread depth loss.

## Slide 6: Task Force on Tyre Abrasion: Important information
C1 tyres: ETRTO created a TF to work on evaluating the feasibility of characterizing tyres with respect to their “relative mileage potential calculated performance”. The first steps were presented to the TFTA (TA-23-2).
C1 tyres: The ETRTO tool to verify the suitability of a given circuit to perform tyre abrasion tests is available on ETRTO website.
The planned multi-circuit and multi-drum correlation exercise to verify the correlation between different circuits and drum facilities will be delayed - potential test centers are requested to express their interest to participate in the exercise.
C2 tyres: ETRTO completed full on-road tests with C2 tyres. More tests will follow in 2024 with the aim of finalizing the on-road testing method proposal (TA-26-8). JASIC announced that a preliminary verification of drum tests will be completed by March 2025 at least for C2 tyres with LI≤107 (TA-26-4).
C3 tyres: ETRTO introduced the C3 tyre abrasion rate index vehicle method preliminary concepts (TA-24-3). JASIC carried out an analysis of the Japanese C3 market (TA-26-4) and presented the main differences between European and Japanese HDV fleet (TA-23-5).

## Slide 7: Task Force on Tyre Abrasion: next
C1 tyres | Complete the market assessment campaign – ongoing  Develop proposal for C1 tyre abrasion limits – Working document at GRBP in Sept 2025  Assess the feasibility of rating and definition of the mileage of tyres -“relative mileage potential calculated performance”- ongoing - Feb 2025  Carry out a multi-circuit and multi-drum correlation exercise to verify the correlation between different circuits and drum facilities  Full updated timeline of C1 activities can be found here: TA-24-5
C2 tyres | Assessment of C1 method suitability for C2 tyres – ongoing  Propose abrasion method(s) – working document at GRBP in Feb 2026* Develop proposal for C2 tyre abrasion limits – working document at GRBP in Sept 2027*
C3 tyres | Propose abrasion method(s) – working document at GRBP in Feb 2027 Develop proposal for C3 tyre abrasion limits – working document at GRBP in Sept 2029
*Deadlines may be brought forward by one year should C1 methods be found to be suitable for C2

## Slide 8: Thank you