## Slide 1: Status report to the 80th session of GRBP (September 2024)
Task Force Vehicles’ Sound
(TF-VS)
NB: previous name of this TF was TF-SL for Sound Limits
Transmitted by the chair of the TF-SL (Sound Limits)/VS (Vehicles’ Sound)
Informal Document GRBP-80-27
80th GRBP, 17-20 September 2024
Agenda item 7

## Slide 2
“The experts from EC, ETRTO and OICA reported on their studies on sound level limits (GRBP-73-23, GRBP-73-11 and GRBP-73-25, respectively). To coordinate such initiatives, GRBP decided to establish a taskforce (TF) and sought a volunteer among the experts from Contracting Parties to take the leadership of TF, while OICA agreed to act as secretary. GRBP considered that TF should address the sound level limits of UN Regulation No. 51 and, at a later stage, No. 41. To kick-off the TF activities without delay, the Chair pointed out that he could take the lead of TF on a temporary basis, if needed.”
Reminder
Roles
Task Force on Sound Limits (TF SL) - Transport - Vehicle Regulations - UNECE Wiki
TF-VS homepage
Chair: France
Secretariat: OICA
TF Vehicles‘ Sound: Key Points

## Slide 3
15
~60-70
Number of Meetings
01st TF SL: March 24, 2021 (TFSL-01-07)
02nd TF SL: May 26, 2021 (TFSL-02-12)
03rd TF SL: July 12-13, 2021 (TFSL-03-08)
04th TF VS: September 13-14, 2021 (TFVS-04-16)
05th TF VS: October 26-27, 2021 (TFVS-05-07)
06th TF VS: December 17, 2021 (TFVS-06-04)
07th TF VS: February 07, 2022 (TFVS-07-15)
CPs: China, European Commission, France, Germany, India, Italy, Japan, Spain, Switzerland, The Netherlands, United Kingdom
NGO‘s: CLEPA, ETRTO, EUWA, IMMA, ISO, OICA
GUESTS: Aristotle University, ATEEL, BRUITPARIF, FEDRO, FEV, HS Data analysis & Consultancy, IDIADA, JARI, TNO, Brussels Env., …
Participants (Contracting Parties, NGOs, Guests)
Meetings were held in hybrid or virtual depending on the pandemic situation at that time
TF Sound Limits / Vehicles‘ Sound: Facts and Figures
08th TF VS: April 04, 2022 (TFVS-08-10)
09th TF VS: May 24, 2022 (TFVS-09-08)
10th TF VS: July 12, 2022 (TFVS-10-08 )
11th TF VS: September 09, 2022 (TFVS-11-09)
12th TF VS: July 10, 2023 (TFVS-12-08)
13th TF VS: August 29, 2023 (TFVS-13-05)
14th TF VS: November 10, 2023 (TFVS-14-06)
15th TF VS: June 03, 2024 (TFVS-15-09)

## Slide 4: TF VS – MAIN WORKS DONE & ONGOING (1/5)
Need to identify where the noise issues lie e.g. through a cross-matrix to get a reference scenario as close as possible of real life
Identified a subgroup within the TFVS to define a Cross-matrix.
Activities still on-going due to the complexity of the topic for example difficult to gather the required input data.
GUIDELINES OF THIS TASK FORCE:
During the 01st Session, a subgroup decided to draft a proposal that was approved at the 03rd Session and subsequently updated at the 04th session.
  Change of the name of this TF from TF-SL (Sound limit) to TF-VS (Vehicle Sound)
During the 13th session, it was pointed out the necessity to update the Guideline to take into account the future activities of the TFVS. It will be managed during next TFVS occurrences.
Impact of AVAS (UN-R138) on Noise Emissions (UN-R51) at low speeds
Thoughts from some Noise experts related to UN-R138 & UN-R51 matching
Actions to be defined through the documents related to the UN-R138
 To be followed with the new TF-QRTV (UN-R138-02)
Informal document
GRBP-74-03 Rev.1
GRBP-74-03 Rev 02 (Work in progress)
TFVS-02-07
TFVS-04-14
TFVS-05-06
TFVS-07-08
TFVS-04-12
TF-QRTV (UN-R138-02)
TFVS-06-03
TFVS-06-05
TFVS-07-05
TFVS-07-13
On going
On going with the UN TF-QRTV
TFVS-08-06
TFVS-09-06
TFVS-12-06
On going

## Slide 5: TF VS – MAIN WORKS DONE & ONGOING (2/5)
TOPICS DISCUSSED DURING TFVS-15 SESSION:
(OICA) “Regulation 51-03. Impact of Supplement 7 on the measurement uncertainties”
(OICA) “Proposal for a Document for Reference: measurement uncertainties when testing in UN Regulations under the purview of the Working Party on Noise and Tyres”
(ETRTO) "Measurement uncertainties reduction in rolling sound emission test method in R117 - ETRTO Status update"
(ENBF) “Low noise pavement – Life Cycle Assessment (LCA) and Life Cycle Costing (LCC)
(SINTEF) “Final results of the ELANORE project and proposals for improvement of the tyre labelling for noise”
(UK - DfT) “UK noise camera Research”
TFVS-15-09 (Status report)
Done

## Slide 6: TF VS – MAIN WORKS DONE & ONGOING (3/5)
MAIN OUTPUT OF TOPICS DISCUSSED DURING TFVS-15 SESSION:
(OICA) “Regulation 51-03. Impact of Supplement 7 on the measurement uncertainties”
  The correction method introduced in Supplement 7 has improved the accuracy of measurements in Annex 3 of the UN R51.03. Future studies should focus on the impact of the tyre torque effect.
(OICA) “Proposal for a Document for Reference: measurement uncertainties when testing in UN Regulations under the purview of the Working Party on Noise and Tyres”
  The aim is to enhance transparency on Measurement Uncertainties (MU) incorporated within measurement procedures during type approval, conformity of production, and other measurement-related activities.
(ETRTO) "Measurement uncertainties reduction in rolling sound emission test method in R117 - ETRTO Status update"
  An overview of the activity on measurement uncertainties reduction has been shared. The following next steps have been outlined: (1) to start a dedicated subgroup of the TF-VS to focus on noise test track correction; (2) to prepare a WD for next 2025 with focus on upgraded outdoor test method in R117 and its measurement uncertainty is expected
TFVS-15-09 (Status report)
Done

## Slide 7: TF VS – MAIN WORKS DONE & ONGOING (4/5)
MAIN OUTPUT OF TOPICS DISCUSSED DURING TFVS-15 SESSION:
4. (ENBF) “Low noise pavement – Life Cycle Assessment (LCA) and Life Cycle Costing (LCC)”
  This study presents the results of a Life Cycle Assessment (LCA) and Life Cycle Costing (LCC) analysis of Low Noise Asphalt. The research result indicates that the use of ad hoc pavement, although it might be more expensive, offers significant long-term economic benefits and mitigating noise-related impacts such as health problems.
5. (SINTEF) “Final results of the ELANORE project and proposals for improvement of the tyre labelling for noise”
  The purpose of this presentation is to share the primary conclusions and recommendations of the ELANORE Project (EU tyre LAbelling system for NOise and rolling REsistance) concerning noise labelling procedures. The report identified short and log terms recommendations. The detailed reports and findings are within the TFVS Report.
6. (UK - DfT) “UK noise camera Research”
  Noise camera technology has been assessed to determine its effectiveness in automatically detecting vehicles that are excessively noisy. Key aspects of the project include (1) defining Excessively Noisy Vehicles; (2) Identifying and testing suitable technology for noise detection; (3) Conducting real-world tests.
  The main output of the studies recommended a specific noise threshold (i.e. 95 dB LAFmax at 7.5 meters) for enforcement against excessively noisy cars and motorcycles.
TFVS-15-09 (Status report)
Done

## Slide 8: TF VS – MAIN WORKS DONE & ONGOING (5/5)
TOPICS STILL OPEN FOR THE NEXT SESSIONS:
Update of previous national presentations (EC, Japan, UK, China, Germany, Belgium …) and others (OICA, IMMA, ETRTO …)
Cross-matrix
(SINTEF) “Noise emission levels of electric and ICE vehicles on real roads in person” (TBC)
(ENBF) “Noise Radar Results – Genève” (TBC)
Next steps to be decided
…
To be continued
On going
The NEXT 16th Session is scheduled for October 28th, 2024
Hybrid – Barlin (TBC)
TBD

## Slide 9
Thank you!
Feel free for any comments / suggestions.
Feel free for contacting our subgroup to get any additional information and/or contribute to the work of our subgroup.

## Slide 10
Backup documents

## Slide 11: TF VS – MAIN WORKS DONE & ONGOING
A lot of studies about vehicles, tyres, roads, methods, enforcement … has been presented during the 12 sessions of the TF-VS (see UNECE TF-VS Website) with a potential to improve the noise in real life.
The TF agreed to the creation of a subgroup with the aim of preparing a Report in order to provide an overview and a common view of topic discussed from March 2021 to September 2022 and identify the potential for the future.
The full report has been completed, presented during the 12th session of the TF-VS and shared (see link on the right).
Volunteers: CPs with France, The Netherlands, Japan, and NGO with IMMA, OICA, ETRTO, ISO
EC study on sound level limits of M, N, L-cat. Veh.  Analysis & comparison between the different studies :
A lot of different points have been discussed and highlighted (for details see UNECE TF-VS Website)  work to be continued
EC Report for M/N
EC Report for L
ATEEL(OICA) Report (GRBP-75-16)
GRBP-76-14 ATEEL/OICA Comparison
TFVS-11-06 ETRTO comments
(OICA) Comparison of EMISIA and ATEEL study
TFVS-14-05 (Status Report TFVS-12th)
Full Report
Done
Done

## Slide 12: Work done by the sub-group Extract from the presentation done at the 12th session (TFVS-12-05)
REPORT OF THE 11 TF-VS SESSIONS

## Slide 13: TF Sound Limits / Vehicles‘ Sound: Facts and Figures
Volunteers
Other Meetings
SUBGROUP on
the report of the 11 sessions
01st Subgroup: October 21, 2022
02nd Subgroup: November 04, 2022
03rd Subgroup: November 29, 2022
04th Subgroup: December 14, 2022
05th Subgroup: January 16, 2023
06th Subgroup: January 26, 2023
07th Subgroup: February 15, 2023
08th Subgroup: March 02, 2023
09th Subgroup: March 10, 2023
10th Subgroup: March 29, 2023
CPs:
  France: Serge FICHEUX, Romain BARBEAU,
  Japan: Takehiro ITO, Yoshihiro SHIRAHASHI, Yoshihisa TSUBURAI,
  The Netherlands: Jan Sybren BOERSMA,
NGO‘s:
  ETRTO: Michael STEFFAN,
  IMMA: Edwin BASTIAENSEN, Alex DESPLENTER,
  OICA: Klaus NEUHAUS, Per-Uno STURK, Françoise SILVANI.
(Contracting Parties & NGOs)
11th Subgroup: April 11, 2023
12th Subgroup: April 26, 2023
13th Subgroup: May 16, 2023
14th Subgroup: May 30, 2023
15th Subgroup: June 20, 2023

## Slide 14: GENERAL GUIDELINES OF THE SUB-GROUP
Target: full report ready by June 2023 to be ready for next TF-VS Session
“Rules”:
  Need to remain factual, objective & neutral + take care for having the same ‘level’ of information in each document:
    cross-reading of the different documents between the members of our subgroup, and then
    getting feedback from the authors of the various TFVS presentations

## Slide 15: STRUCTURE OF THE REPORT & APPROACH
Grouping by subject/theme & distribution of the work between subgroup’s experts
54 Documents/presentations
25 subjects/themes  25 Individual sheets
Identification of the key points & Classification
PART 4.
31 Key points identified
Grouping by subject/theme & work split between the subgroup experts
5 main key domains identified & defined
PART 3.
Analysis distributed by pair between the subgroup experts
Identification of the general findings & open issues
DONE
PART 2.
PART 1.
Executive Summary
General introduction
General introduction
Executive summary
Analysis to identify the general findings/ statements for further consideration
Identification of the
  Main messages,
  Summary &
  Open issues
  of the 54 documents/ presentations
Feedback from the authors to be get
DONE
DONE
DONE
DONE
DONE
DONE

## Slide 16
During the 11 sessions of the TF-VS, there were 54 presentations on different topics such as:
  Road surfaces,
  Studies on noise emissions of M/N/L vehicles,
  Test methods,
  Noise mapping
  Noise camera/sonar experimentation,
  Test campaigns,
  General ideas, studies & considerations,
  Cross matrix to improve traffic noise scenario and test procedures.
From these 54 presentations, the subgroup decided to combine them as much as possible by subject/theme. This step led to 25 subjects/themes.
‘Individual sheets » x 25
PART 4.

## Slide 17
2. An ‘individual sheet’ (targeted in 2 pages) was built for each of these 25 subjects/ themes to:
  Identify the main messages shared during the different sessions of the TF-VS,
  Make a summary of the presentation(s),
  Add points discussed at the TF-VS,
  Identify the references related to the concerned subject/theme.
 The result is the Part 4. of this report.
Through this exercise, the subgroup identified several key points.
In the next step, these key points were combined and led to 5 key domains: vehicle, driver, enforcement, immission, tyres/roads.
‘Individual sheets » x 25
PART 4.

## Slide 18
For each of the 5 key domains fixed, the subgroup created a sheet to:
  Define/describe them
  Identify the general findings/ statements explained during the presentations/ reports to the TF-VS, and
  Identify the needs & questions for potential further considerations by the TF-VS.
 The result is the Part 3 of this report.
Identification & Definition of the main key-domains
  “DRIVER” means a person having the care and control of a motor vehicle on the road. He or she operates the vehicle's controls whether or not the motor vehicle is in motion. The driver is responsible for the safe, daily use of the vehicle including the after-market components in accordance with rules of the road.
  “ENFORCEMENT” (in the context of sound) means the activities to ensure vehicles are and remain compliant to the regulations.
  The applicable regulations are related to bringing-vehicles-into-the-market (type approval, market-surveillance) and to use of vehicles in the jurisdiction (roadworthiness, Periodic Technical Inspection, roadside inspection, sound radar, manipulation).
  “IMMISSION” means the sound recorded or predicted at receiver point, caused by the road vehicle fleet in continuous traffic flow or as single vehicle events, however potentially mitigated by abatement measures of various effect and efficiency (social impact and CBA).
  “TYRES_ROADS” have a recognized influence on vehicle sound emissions. Different aspects have to be considered as the road surface itself, the tyre rolling sound, the interaction between the tyre and the road, but also the different tools available to classify them (e.g., the tyre labelling) taking into account the performances and impacts of tyres/roads on health, safety and environment.
  “VEHICLE” (in the context of sound) means the sound produced by any means of transport resulting from its operation in traffic, including effects from alterations over its lifetime (NB: for tyre, see the other sheet related to tyre/road component).
PART 3.
NB: These 5 key-domains and their associated sheets have to be considered together, in parallel.

## Slide 19
 | Type approval | In use | 
Vehicle | R41, R51,R9, R63, R28,R138, R165 |  | 
Tire | R117 |  | 
Road surface | NA |  | 
Replacement parts
Driver
Driver behavior
Maintenance
Immission
Enforcement
Traffic flow,
road type etc.
Market surveillance
PTI, road side check, …
Five Key-domains
PART 3.
GRBP task
Maybe R.E.3

## Slide 20
Five Key-domains
PART 3.
GRBP task
Maybe R.E.3
Global regulation
Local rule
Need balance

## Slide 21
Noise issues in the (urban) environment have to be considered in a holistic way (combination of complementary measures necessary) and are mainly linked to:
  the manipulation of vehicles and components
  the maintenance of the vehicles
  the driver behaviour and awareness
  the single events
  the ‘organisation’ of the vehicle fleet (traffic flow, vehicles distribution, speed, bumps, …)
  the tyres contribution to the vehicle’s sound emissions and their interaction with
    the road surfaces which is becoming still more important with electrified vehicles
    the environmental & safety tyres performances and their inter-dependency
  the road surfaces including the road maintenance to maintain their performances regarding the noise
  the interaction between the environmental noise and the type-approval tests
  the sound assessment modelling tools to estimate sound from road traffic
  the various usages of the vehicles – private and commercial
General findings from the 5 Key-domains
PART 2.

## Slide 22
Education of the drivers to make them aware of the impact of their driving behaviour
  information’s display (roadside information, noise information inside the vehicle, …),
  prevention campaigns,
  roadside checks,
  sanction systems supported for instance by noise sonars/cameras including vehicle license plate detection, speed, acceleration, …
Development of solutions against manipulation of vehicles
  better control of aftersales component,
  periodical technical inspection,
  market surveillance,
  detection of illegally modified vehicles, for example by noise cameras
Needs & questions for further consideration
PART 2.

## Slide 23
Arrangement of traffic fleet to provide more ‘relaxed’ driving conditions and reduce noise by
  optimizing traffic flow,
  adding low speed areas,
  avoiding speed bumps,
  traffic flow distribution especially for the future with growing electrified vehicle part …
Improvement of the knowledge of vehicles impacts on noise including
  Future worldwide automotive electrification including AVAS and impact on environmental noise
  Data from real life for all categories of vehicles and not only for M1 & N1 categories of vehicles to be considered through test campaigns
Needs & questions for further consideration
PART 2.

## Slide 24
Definition of a cross-matrix between the traffic noise situations, contributing factors and major complaints
Update and improvement of the understanding of the environmental noise in real life concerning:
  CBA (Cost-Benefit-Analysis) to assess the potential health benefits of noise reduction to be improved
  Noise mapping tools including single events
  Traffic scenarios
Needs & questions for further consideration
PART 2.

## Slide 25
Further improve knowledge of tyres for:
  their performances and their inter-dependency regarding noise and other environmental aspects (as particles), and safety (as handling & braking of vehicles)
  their interaction with the road surfaces
  their test methods (indoor in addition to outdoor)
Further research on low-noise road surfaces with a focus on their acoustic behaviour, their maintenance with the associated costs, and their safety performances
Amend the UN Regulation no.51
  after assessment of previous steps and measures
  to expand the various potential uses of the vehicles (RD-ASEP and its assessment in real life in the future)
Needs & questions for further consideration
PART 2.

## Slide 26
Topics for potential future works of GRBP:
  Education of the drivers and their awareness
  Development of solutions against manipulation of vehicles
  Arrangement of traffic fleet
  Improvement of the knowledge of vehicles’ impacts on noise
  Cross-matrix
  Improvement & update of the understanding of the environmental noise in real life
  Improvement of the knowledge of tyres
  Further research on low-noise road surfaces and their maintenance
  Future for UN-R51-03.
Main messages
  Limited possibilities in further sound reduction on TA
  Improve relevance of TA test for in use (RD-ASEP) for both vehicles & tyres
  Tyre/road noise and technology challenge
  Other measures to reduce immission (speed reduction, road surface, …)
  Driver awareness
  Contribution of enforcement
SUMMARY of potential for the future

## Slide 27
Work on the cross matrix,
Follow-up of the different studies in progress everywhere
Potential actions/opportunities and prioritization:
  Experience (forum) to be continued to share various information linked to noise topics for as much as possible promote worldwide harmonization,
  Consider the needs and questions highlighted in the report for potential future work of the TF-VS.
Next steps for the TF-VS ?
Agreed for consideration? How to consider them?
Full report to be made as “GRBP Document for Ref.”?